MOTOROLA MC68020 INSTRUCTION SET
		      ================================


This file contains ALL of the extra instructions and addressing modes found
on the Motorola MC68020 processor, as found in Amiga 2000 machines with acc-
elerator cards fitted, and which can be executed (with very few exceptions)
on Amiga 3000 machines fitted with the Motorola MC68030 processor.


	The file shall be divided into several sections. First, I shall cover
the additional addressing modes available to MC68020 assembly language prog-
rammers, and the syntaxes used for those new modes. Then, I shall cover fully
the instruction extension words applicable to the MC68020, which follow the
main instruction opcodes and provide the MC68020 with the instruction infor-
mation available to access the new addressing modes. And finally, the comp-
lete set of MC68020 extra instructions PLUS OPCODES follow, documented accor-
ding to the standards laid down in the Official Motorola Documentation.


		       MC68020 - NEW ADDRESSING MODES
		       ==============================


The principal new modes available to the MC68020 fall into two classes:memory
indirect addressing, and bit field addressing. First, I shall outline some of
the conventions used throughout this file. They are:


		<EA>	: Effective Address. Stands for the
			  address of the operand under con-
			  sideration, whether computed at
			  assembly-time or runtime.

		{ }	: Curly braces are used to denote a
			  bit field. Bit fields are covered
			  below.

		off	: Offset for bit fields.

		wd	: Width for bit fields.

		[ ]	: Denotes "contents of".

		bd	: Stands for Base Displacement in
			  memory indirect addressing.

		od	: Stands for Outer Displacement in
			  memory indirect addressing.

		An	: One of the address registers A0-A7.

		Xn	: Any 680x0 data or address register
			  used in the context of an index
			  register.

		scale	: The multiplier applied to the value
			  of the index register in memory in-
			  direct addresing.

		size	: The size attribute applied to the
			  index register in memory indirect
			  addressing.


And now, for the various memory indirect addressing modes.


1) Memory Indirect Preindexed (using Address Register).

Generation	: <EA> = [bd + [An] + [Xn.s]*size] + od

Assembler	: ([bd,An,Xn.s*size],od)

Mode		: 110 in instruction address mode field

Description	: This addressing mode uses two constant displacements,
		  an address register, and an index register, PLUS a
		  scale factor (five components in all).

		  First, the contents of the specified Address Register
		  are added to the value of the Base Displacement. Then,
		  the contents of the specified Index Register are mul-
		  tiplied by the specified scale factor (1,2,4 or 8),
		  and this value is added to the whole.

		  This value is then used as a pointer into memory, and
		  a longword pointer extracted from memory. The value of
		  the Outer Displacement is then added to the value of
		  this longword pointer, and this value becomes the
		  effective address for the specified operand.

		  The legal ranges for the various components are:

		  An		: Any 680x0 address register, A0-A7.

		  bd		: Base displacement. Can be null, or
				  can be word or longword sized. Word
				  sized displacements are sign-extended
				  to longword values prior to addition.

		  Xn		: Index register. Can be either a
				  680x0 data register or an address
				  register.

		  s		: Either .W for word operands, or
				  .L for longword operands. NOTE:
				  word values are sign-extended to
				  longword values prior to addition
				  in common with all 680x0 address
				  arithmetic.

		  size		: The legal values for the scale
				  factor are 1,2,4 or 8.

		  od		: Outer displacement. Can be null,
				  or can be word or longword sized.
				  Again, word-sized displacements
				  are sign-extended to longword dis-
				  placements prior to addition.

Example		: Let bd = $40000, od = $8000, A0 contain the value
		  $20000, D2 contain the value $100, and the longword
		  value stored at location $60400 be $30000.

		  Then, the effective address of:

		  ([$40000,A0,D2.W*4],$8000.w)

		  is:

		  1) $40000 + $20000 + ($100 * 4)

		     = $60400

		  2) Contents of $60400 = $30000

		  3) $30000 + $8000.w = $0003000 + $FFFF8000

		     = $28000

		  Therefore the effective address is $28000.


2) Memory Indirect Postindexed (using Address Register).

Generation	: <EA> = [bd + [An]] + [Xn.s]*size + od

Assembler	: ([bd,An],Xn.s*size,od)

Mode		: 110 in instruction address mode field

Description	: This addressing mode uses the same five components as
		  Memory Indirect Preindexed, but in a different order.

		  First, the contents of the specified address register
		  are added to the value of the Base Displacement. This
		  value is used as a pointer into memory, from which a
		  longword value is extracted. This value has added to
		  it the value of the contents of the specified index
		  register (multiplied by the given scale factor) and
		  the value of the Outer Displacement, to create the
		  final effective address.

		  The range of legal values for the various components
		  id identical to that for Memory Indirect Preindexed.

Example		: Let bd = $1000, od = $20000, A2 contain the value
		  $10000, D7 contain the value $40000, and the long-
		  word value stored at $11000 be $58000.

		  Then, the effective address of:

		  ([$10000,A2],D7.L*1,$20000)

		  is:

		  1) $1000 + $10000 = $11000

		  2) Contents of $11000 = $58000

		  3) $58000 + $40000 + $20000 = $B8000

		  Therefore the effective address is $B8000.


3) Program Counter Memory Indirect With Preindex.

Generation	: <EA> = [bd + [PC] + [Xn.s]*size] + od

Assembler	: ([bd,PC,Xn.s*size],od)

Mode		: 111 in instruction address mode field

Description	: Add to the value of Base Displacement the value of the
		  Program Counter, and the value contained in the speci-
		  fied Index Register (multiplied by the specified scale
		  factor). Use this total value as a pointer into memory
		  and extract a longword value from this memory location.
		  Add to this longword value the value of the Outer Dis-
		  placement. This final result is the effective address
		  of the operand.

Example		: Let bd = $4000, PC = $2C00, D5 = $FFFF, and od = $1000.

		  Let location $6BFE contain the longword $5A800.

		  Then, the effective address of:

		  ([$4000,PC,D5.W*2],$1000)

		  is:

		  1) $4000 + $2C00 + ($FFFFFFFF * 2)

		     = $6BFE

		  2) Contents of $6BFE = $5A800.

		  3) $5A800 + $1000 = $5B800.

		  Therefore the effective address is $5B800.


4) Program Counter Memory Indirect With Postindex.

Generation	: <EA> = [bd + [PC]] + [Xn.s]*size + od

Assembler	: ([bd,PC],Xn.s*size,od)

Mode		: 111 in instruction address mode field

Description	: Add to the value of Base Displacement the value of the
		  Program Counter, and use this as a pointer into memory.
		  Extract the longword value stored at this address, and
		  add to this extracted value the value of the specified
		  Index Register (multiplied by the specified scale fac-
		  tor), and the value of the Outer Displacement. This fi-
		  nal value is the effective address of the operand.

Example		: Let bd = $6000, PC = $1A00, D1 = $0020, and od = $7000.

		  Let location $7A00 contain the longword $FC0000.

		  Then, the effective address of:

		  ([$6000,PC],D1.L*4,$7000)

		  is:

		  1) $6000 + $1A00 = $7A00

		  2) Contents of $7A00 = $FC0000.

		  3) $FC0000 + ($0020 * 4) + $7000 = $FC7080.

		  Therefore the effective address is $FC7080.


Note that with ANY of the memory indirect modes, the programmer can omit any
desired component for the desired effect. For example:

							        +
	68020 Instruction			68000 Equivalent

	MOVE.L	([Base]),D0			MOVE.L Base,A0
						MOVE.L (A0),D0

	MOVE.L	([Base,A0]),D0			MOVE.L	Base(A0),A0
						MOVE.L	(A0),D0

	JMP	([0,A0],D0.W*4)			ADD.W	D0,D0
						ADD.W	D0,D0
						MOVE.L	0(A0,D0.W),A0
						JMP	(A0)

	MOVE.W	([Base,A0],D2.L*8,Outer),D7	MOVE.L	Base(A0),A0
						ADD.L	D2,D2
						ADD.L	D2,D2
						ADD.L	D2,D2
						LEA	Outer(A0),A0
						MOVE.L	0(A0,D2.L),D7


Note that the 68020 forms can complete the given operation in one instruction
whereas the 68000 needs two or more instructions to perform the same task, &
requires extra register use. Hence the use of the '+' character to highlight
the fact that the equivalence is NOT complete - in general the 68020 does NOT
change the contents of the registers in the source operand UNLESS the destin-
ation happens to be one of those registers also. Note also how the 68020 can
access a jump table in one instruction - see the 68000 equivalent alongside!


	It can be seen from this that the 68020 addressing extensions are so
far ahead of the already powerful 68000 addressing modes (which still kick an
Intel chip into a cocked hat!) that Motorola didn't need to add any more to
the 68030 and 68040 (after all, many programmers still can't cope with single
instructions that are equivalent to half a C program...).


	It remains to cover bit fields. Bit fields are so radically different
from normal addressing modes that they do take a little getting used to. The
basic idea is that any collection of bits, of any size (within certain rest-
rictions), aligned anywhere in memory (not even on a byte boundary!) can be
accessed and manipulated.


	A bit field is denoted by the legend:


			{offset:width}


where either of the values 'offset' or 'width' can be specified within an in-
struction by a constant value or a data register reference. A comparison of
bit addressing (for instructions such as BCHG) and bit field addressing is:


			7 6 5 4 3 2 1 0
	 Byte N-1 |	Byte N		|   Byte N+1	| Byte N+2

			Bit Addressing


			7 6 5 4 3 2 1 0
	 Byte N-1 |	Byte N		|   Byte N+1	| Byte N+2
			      0 1 2 3 4   5 6 7 8 9 ...
			<---->
			offset
			      <------------------------>
					width

			Bit Field Addressing


In the above, a Bit Field is a consecutive string of 1 to 32 bits, specified
by a Base Address (the address of the byte containing Bit 0 of the Bit Field,
byte N in the example above), an Offset (the distance in bits from the most
significant bit of the Base Address) and the Width (number of bits that form
the Bit Field).


	If the Offset is specified using an immediate data value, then the
Offset ranges from 0 to 31. Simialrly, the Width ranges from 1 to 32, but in
this case the value is limited to the range 1-32 whether specified as an im-
mediate value or as a data register reference.


	When a data register is used, then the Offset specification can range
from:

			  31		 31
			-2	to	2  - 1


which means that the first bit of the Bit Field might reside in a byte which
is many bytes distant from the Base Address defined in any instruction Bit
Field reference! This facility allows scanning of Bit Field Arrays, an exam-
ple of which is:


	Byte:		N		N+1		N+2	  ...

	Bit : 7 6 5 4 3 2 1 0 | 7 6 5 4 3 2 1 0 | 7 6 5 4 3 2 1 0 ...

	BF  : 1 1 1 1 1 2 2 2   2 2 3 3 3 3 3 4   4 4 4 4 5 5 5 5 ...


Here, Bit Field 2 follows Bit Field 1 in the array immediately. If Byte N is
the Base Address for the entire Bit Field Array, then a data register can be
used to contain the Offset, and the next element in the array referenced by
adding the value of the Width (here, 5) to the value of the Offset contained
in the data register, and use one address to reference the entire array with-
out having to recompute the Base Address! In this case, our Bit Field Array,
containing Bit Field elements of 5 bits, can contain up to 4 BILLION elements
(assuming sufficient memory to store them all) all referenced via the same
Base Address!


	And by way of example, for the above Bit Field Array, if register A0
of the MC68020 points to Byte N above, then the various elements are referen-
ced as follows using immediate offset and width values:


		Element #1	: (A0){0:5}

		Element #2	: (A0){5:5}

		Element #3	: (A0){10:5}

			....

		Element #8	: 4(A0){3:5} (NOT (A0){35:5} !!!)

		Element #9	: 4(A0){8:5}


etc.


			   MC68020 EXTRA REGISTERS
			   =======================


The MC68020 possesses a number of extra registers, available to programs ex-
ecuting in supervisor mode. Also, the status register contains extra bits. A
summary of the registers is as follows (all registers are 32 bits wide unless
otherwise stated):


		D0 - D7 : Data Registers as per MC68000.

		A0 - A7	: Address Registers as per MC68000.

		SR	: Status Register (16 bits). See below.

		CCR	: Condition Code Register as per MC68000.

		A7'	: Also ISP : Interrupt Stack Pointer.

		A7''	: Also MSP : Master Stack Pointer.

		VBR	: Vector Base Register.

		CACR	: Cache Control Register (4 bits).

		CAAR	: Cache Address Register.

		SFC	: Source Function Code Register (3 bits).

		DFC	: Destination Function Code Register (3 bits).


The status register bits are allocated as follows:


		Bit	Meaning
		---	-------
		 0	Carry Flag (CCR).

		 1	Overflow Flag (CCR).

		 2	Zero Flag (CCR).

		 3	Negative Flag (CCR).

		 4	Extend Flag (CCR).

		 8	IPL0 Interrupt Bit.

		 9	IPL1 Interrupt Bit.

		10	IPL2 Interrupt Bit.

		12	Master Stack Bit.

		13	Supervisor Mode Bit.

		14	Trace On Change Of Program Flow.

		15	Trace (Single-Step Through Program).


The Vector Base Register allows different tasks to have different sets of ex-
ception vectors located in different areas of memory. The standard addresses
for the MC68000 exception vectors are now treated as offsets to be added to
the contents of the VBR, and when a MC68020 exception occurs, the exception
vector will be fetched from this new address. When the VBR contains zero, the
MC68020 operates in an identical fashion to the MC68000.


	The Supervisor Stack Pointer (SSP) is now divided into two different
entities. The Interrupt Stack Pointer (ISP) is accessed when the Master Stack
Bit of the Status Register is 0 (in which case, behaviour is identical to the
MC68000). When the M bit is 1, then the Master Stack Pointer is used instead
of the Interrupt Stack Pointer. The MC68020 can also access the User Stack
Pointer (USP) in supervisor mode via the appropriate instructions as per the
MC68000, but also has available several new instructions to access the USP.


	The Source Function Code (SFC) and Destination Function Code (DFC)
Registers allow MC68020-based systems equipped with a MC68851 Paged Memory
Management Unit (PMMU) to access areas of memory protected according to the
definitions of the 'address space' within the PMMU. The MOVEC instruction is
used to change the contents of these registers (in supervisor mode only!) to
allow a supervisor-mode program to read to or write from memory protected by
a PMMU. The values that these registers store are:


		000	Undefined, Reserved.
		001	User Data Space.
		010	User Program Space.
		011	Undefined, Reserved.
		100	Undefined, Reserved.
		101	Supervisor Data Space.
		110	Supervisor Program Space.
		111	CPU Space (see CALLM, BKPT).


	These registers are used in conjunction with the MOVES instruction in
supervisor mode to allow supervisor-mode programs to transfer data to either
user program/data space or supervisor program space without causing a PMMU
exception condition (memory access violation).


	The Cache Control Register (CACR) allows the on-chip cache memory to
be controlled. The bits of the CACR are:


		Bit	Meaning
		---	-------
		 0	E bit : 1 = enable cache

		 1	F bit : 1 = freeze cache (prevent
				    updating)

		 2	CE bit : 1 = invalidate single cache
				     entry (CPU clears valid
				     bit for entry)

		 3	C bit : 1 = invalidate all cache entries


The entries to be invalidated using the C/CE bits are controlled by the Cache
Address Register (CAAR). The address of the invalidated entry is written here
PRIOR to writing to the C/CE bits using MOVEC, and allows logical or virtual
addresses to be invalidated prior to task switching in a multiprogramming en-
vironment.


			MC68020 EXCEPTION VECTOR TABLE
			==============================


The MC68020 has an extended exception vector table. This vector table is de-
fined by the table below. In the table, SD refers to Supervisor Data Space,
and SP to Supervisor Program Space. FPCP refers to the Floating-Point Copro-
cessor, and PMMU to the Paged Memory Management Unit.


	Address	Vector	Assignment
	-------	------	----------
	$0000	0  SP	Reset:Initial ISP
	$0004	1  SP	Reset:Initial PC
	$0008	2  SD	Bus Error
	$000C	3  SD	Address Error
	$0010	4  SD	Illegal Instruction
	$0014	5  SD	Zero Divide
	$0018	6  SD	CHK/CHK2 Instruction
	$001C	7  SD	cpTRAPcc, TRAPcc, TRAPV Instructions
	$0020	8  SD	Privilege Violation
	$0024	9  SD	Trace Exception
	$0028	10 SD	Line-A Emulator (1010)
	$002C	11 SD	Line-F Emulator (1111) & Coprocessor Instructions
	$0030	12 SD	Unassigned, Reserved
	$0034	13 SD	Coprocessor Protocol Violation
	$0038	14 SD	Format Error
	$003C	15 SD	Uninitialised Interrupt

	$0040 to   SD	Unassigned, Reserved (16-23)
	$005C

	$0060	24 SD	Spurious Interrupt
	$0064	25 SD	Level 1 Interrupt Autovector (IPL1)
	$0068	26 SD	Level 2 Interrupt Autovector (IPL2)
	$006C	27 SD	Level 3 Interrupt Autovector (IPL3)
	$0070	28 SD	Level 4 Interrupt Autovector (IPL4)
	$0074	29 SD	Level 5 Interrupt Autovector (IPL5)
	$0078	30 SD	Level 6 Interrupt Autovector (IPL6)
	$007C	31 SD	Level 7 Interrupt Autovector (IPL7)

	$0080 to   SD	TRAP 0-15 Instruction Vectors (32-47)
	$00BC

	$00C0	48 SD	FPCP Branch Or Set on Unordered Condition
	$00C4	49 SD	FPCP Inexact Result
	$00C8	50 SD	FPCP Divide By Zero
	$00CC	51 SD	FPCP Underflow
	$00D0	52 SD	FPCP Operand Error
	$00D4	53 SD	FPCP Overflow
	$00D8	54 SD	FPCP Signalling NAN (Not-A-Number)
	$00DC	55 SD	Unassigned, Reserved
	$00E0	56 SD	PMMU Configuration Error
	$00E4	57 SD	PMMU Illegal Operation
	$00E8	58 SD	PMMU Access Level Violation

	$00EC to   SD	Unassigned, Reserved (59-63)
	$00FC

	$0100 to   SD	User Defined Vectors (64 to 255)
	$03FC


Special exception vectors new to the MC68020 include the cpTRAPcc and TRAPcc
instruction vector (shared with the MC68000 TRAPV vector) for handling those
instructions, and the range of coprocessor handling exceptions. These include
execptions for the MC68881/MC68882 mathematics coprocessor (FPCP), and the
MC68851 Paged Memory Management Unit (PMMU).


	The MC68020 now saves exception-generated data on the ISP or MSP in
the form of Stack Frames. These take a number of formats, and if the MC68020
encounters a Stack Frame that does not conform to these formats, then the CPU
takes the Format Error exception. This can be triggered by an illegal format
encountered during RTE, CALLM/RTM or cpRESTORE. This occurs if the Format
field (see below) does not conform to the expected specifications.


	The handling of the F-line exception changes in systems containing a
MC68020 plus one or more coprocessors. In such systems, the exception is ta-
ken only if the coprocessor(s) do not recognise an instruction passed to them
unless one of the coprocessor-specific exceptions occurs.


	Also changed is the Address Error handling-now, an address error only
occurs when an attempt is made to execute an instruction that is not word-al-
igned. The MC68020 can access word or longword data that is not aligned, but
with a degradation in performance as a result. The processor creates a Bus
Error stack frame.


	The Bus Error exception is now created by nonexistent memory, memory
errors reported to the CPU by external circuitry, or memory access errors of
certain types reported by a MC68851 PMMU. Some coprocessor errors can also be
the cause of a Bus Error-exercise CARE!


	Coprocessor exceptions include the Floating-Point Coprocessor (FPCP)
exceptions, which include floating-point underflow/overflow, inexact result,
operand error, and a condition called 'Signalling NAN'. This refers to the
use of certain special values (called NANs or 'Not-A-Number's) to signal to
the CPU certain special conditions not signalled via the normal routes. As
well as the FPCP exeptions, there are Paged Memory Management Unit (PMMU) ex-
ceptions, including illegal operation, access violation (caused by operations
such as an attempt by a user-mode program to write to a memory area designa-
ted as part of the supervisor data space by the PMMU, or an attempt to issue
a CALLM instruction without having been granted the correct access level), &
the Configuration Error exception which is caused by faults in the operating
system and its memory management (the only cure for which is to abort and re-
boot the operating system!).


	The final exception does not have a vector assigned to it-because it
is a complete catastrophe for the system. A double bus fault (Bus Error with-
in a Bus Error exception handler, for example) is considered to be so bad for
the system that the processor enters the Halted State. The ONLY way out is an
external RESET!


			MC68020 EXCEPTION STACK FRAMES
			==============================


The MC68020 stores exception-generated data onto the ISP or MSP in the form
of a Stack Frame. At least four words are stored on the stack, as follows:


		SP	Status Register

		SP+2	Program Counter High Word

		SP+4	Program Counter Low Word

		SP+6	Format Word


The Format Word is defined by:


		F F F F V V V V V V V V V V V V


where FFFF is the format type field, and VVVV... is the Vector Offset field,
identifying the exception number taken. Legal values for the FFFF field, and
the number of words saved on the stack, are:


		0000	Short Format (4 words)
		0001	Throwaway Format (4 words)
		0010	Instruction Exception (6 words)
		0011 to Unassigned, Reserved
		0111
		1000	MC68010 Bus Fault (29 words)
		1001	Coprocessor Mid-Instruction (10 words)
		1010	MC68020 Short Bus Fault (16 words)
		1011	MC68020 Long Bus Fault (46 words)
		1100 to Unassigned, Reserved
		1111

For example, the Format $02 Stack Frame is defined by:


		SP	Value of SR
		SP+2	Value of PC High Word
		SP+4	Value of PC Low Word
		SP+6	Format Word
		SP+8	Instruction Address High Word
		SP+10	Instruction Address Low Word


The next stack frames to be defined are the MC68020 Short Bus-Cycle Fault or
Format $0A Frame, and the Long-Frame Bus-Cycle Fault (or Format $0B) Frame.
First, the Format $0A Frame:


		SP	Value of SR
		SP+2	Program Counter (2 words)
		SP+6	Format Word $AXXX
		SP+8	Internal Register Value
		SP+10	Special Status Word
		SP+12	Instruction Pipe Stage C
		SP+14	Instruction Pipe Stage B
		SP+16	Data Cycle Fault Address (2 words)
		SP+20	Internal Register Value
		SP+22	Internal Register Value
		SP+24	Data Output Buffer (2 words)
		SP+28	Internal Register Value
		SP+30	Internal Register Value


and finally, the Format $0B Frame:


		SP	Value of SR
		SP+2	Program Counter (2 words)
		SP+6	Format Word $BXXX
		SP+8	Internal Register Value
		SP+10	Special Status Word
		SP+12	Instruction Pipe Stage C
		SP+14	Instruction Pipe Stage B
		SP+16	Data Cycle Fault Address (2 words)
		SP+20	Internal Registers (2 words)
		SP+24	Data Output Buffer (2 words)
		SP+28	Internal Registers (4 words)
		SP+36	Stage B Address (2 words)
		SP+40	Internal Registers (2 words)
		SP+44	Data Input Buffer (2 words)
		SP+48	Internal Registers (22 words!)


Information on the MC68010 Bus-Cycle Fault Format Stack Frame can be found in
the official Motorola MC68010 User's Manual, but is not of great use here.


		      MC68020 INSTRUCTION EXTENSION WORDS
		      ===================================


The MC68020 extends the range of MC68000 instructions by using a range of ex-
tension words to the basic instructions. The format of a typical MC68020 in-
struction is:


		Word 1 : x x x x x x x x x x M M M R R R

		Word 2 : Extension word

		Word 3 : Any extra required operand words

		 ...


where the extra operand words follow in the order:source operands first, des-
tination operands next.


	Here, the MMM and RRR fields determine the addressing mode of the in-
struction in accordance with the following table (applicable to ALL Motorola
MC680x0 processors unless otherwise stated):


	MMM	RRR	Mode
	---	---	----
	000	xxx	Data Register Direct : xxx = register number 0-7
			and operand is one of D0 - D7.

	001	xxx	Address Register Direct : xxx = register number 0-7
			and operand is one of A0 - A7.

	010	xxx	Address Register Indirect : xxx = 0 to 7,
			operand is one of (A0) to (A7).

	011	xxx	Postincrement:xxx = 0 to 7, operand is one
			of (A0)+ to (A7)+.

	100	xxx	Predecrement:xxx = 0 to 7, operand is on
			of -(A0) to -(A7).

	101	xxx	Address Register Indirect With Displacement:
			xxx = 0 to 7, operand is one of
			disp(A0) to disp(A7). The displacement word
			follows the instruction word.

	110	xxx	Address Register Indirect With Displacement
			And Index:xxx = 0 to 7, operand is one of
			disp(A0,Xn) to disp(A7,Xn). The index regis-
			ter Xn is specified in the extension word(s),
			and the displacement follows this extension
			word.

	111	000	Absolute short:address of operand follows
			instruction word as one word.

	111	001	Absolute long:address of operand follows
			instruction word as two words.

	111	010	Program Counter Indirect With Displacement.
			The displacement follows the instruction
			word as one word.

	111	011	Program Counter Indirect With Displacement
			And Index (all 680x0 series), and Memory Indirect
			(68020 onwards).

	111	100	Immediate Data. The immediate data follows the
			instruction word, using one or two words as is
			required.


The extension words fall into two types:the brief extension word (which is a
slight generalisation of the standard MC68000 extension word), and the full-
format extension word (which allows memory indirect addressing modes etc).


	First, the Brief Format extension word has the format defined by the
template below:


		D X X X W S S 0 d d d d d d d d


The various fields in this extension word are:


	D	: D/A Field. Specifies the index register type for
		  disp(An,Xn) and disp(PC,Xn).

		  0 = Data Register Dn

		  1 = Address Register An

	XXX	: Register number field. Specifies which register is
		  the specified index register, ranging from 0-7.

	W	: W/L field. Specifies whether the index register is
		  word sized or longword sized.

		  0 = word sized (value is sign-extended during
		      address computation)

		  1 = longword sized.

	SS	: Scale field. Determines the scale in memory indirect
		  and the extended form of the MC68000 disp(An,Xn)/
		  disp(PC,Xn) which on the MC68020 allows the use of a
		  scale multiplier. The values are:

		  00	: Multiplier = 1

		  01	: Multiplier = 2

		  10	: Multiplier = 4

		  11	: Multiplier = 8

		  The value SS=00 corresponds to the value used in the
		  original MC68000 extension word. The MC68020 allows
		  multipliers to be used as in:

			MOVE.W	0(A0,D2.W*2),D3

	ddd..	: Displacement field. Contains the byte value of the dis-
		  placement used in disp(An,Xn) and disp(PC,Xn) addressing
		  modes. This byte is sign-extended to a LONGWORD value
		  during computation of the effective address (so that a
		  value of $80 corresponds to -128).


The Full Format extension word is far more complex, since it must contain the
complete definition of any memory indirect addressing modes used. The Full
Format extension word is defined using:


		D X X X W S S 1 B I Z Z 0 J J J


where:


	D	: D/A field. Specifies whether index register is
		  a data register or an address register.

		  0 = Data Register Dn

		  1 = Address Register An

	XXX	: Index Register Number 0-7.

	W	: W/L Field. Specifies:

		  0 = Index register word-sized. Contents sign-
		      extended to longword prior to address com-
		      putation.

		  1 = Index register longword-sized.

	SS	: Scale Factor field. Values are:

		  00	: Multiplier = 1

		  01	: Multiplier = 2

		  10	: Multiplier = 4

		  11	: Multiplier = 8

	B	: Base Suppress (BS) field.

		  0 = Add contents of base address register to
		      base displacement.

		  1 = Suppress base address register-use base
		      displacement only.

	I	: Index Suppress (IS) field.

		  0 = Evaluate index operand and add to address

		  1 = Suppress index operand, do not use.

	ZZ	: Base Displacement Size (BD SIZE) field.

		  00 = Reserved.

		  01 = Null Displacement.

		  10 = Base Displacement Word Sized.

		  11 = Base Displacement Longword Sized.

	JJJ	: Index/Indirect Selection (I/IS) Field.

		  Used in conjunction with the IS bit according to
		  the table below. 'od' refers as always to the
		  Outer Displacement value.

		  IS	I/IS		Operation
		  --	----		---------
		  0	000		No Memory Indirection
		  0	001		Indirect Preindex, NULL od
		  0	010		Indirect Preindex, word od
		  0	011		Indirect Preindex, long od
		  0	100		Reserved
		  0	101		Indirect Postindex, NULL od
		  0	110		Indirect Postindex, word od
		  0	111		Indirect Postindex, long od

		  1	000		No Memory Indirection
		  1	001		Indirect, No index, NULL od
		  1	010		Indirect, No index, word od
		  1	011		Indirect, No index, long od

		  1	100-111		All Reserved


Once a Full Format extension word follows an instruction, then the Base Dis-
placement words follow that word, and the Outer Displacement words follow on
from those. Of course, if either the Base Displacement or the Outer Displace-
ment do not exist (are NULL) then those words are omitted.


	Note that for the MOVE instruction on the MC68020, it is possible to
select both source and destination Memory Indirect operands! In this case,
the order of the instruction words is as follows:


		Word 1		: MOVE instruction

		Word 2		: Source extension full format

		Words 3,4	: Base Displacement if non-NULL,
				  omitted otherwise

		Words 5,6	: Outer Displacement if non-NULL,
				  omitted otherwise

		Word 7		: Destination extension full format

		Words 8,9	: Base Displacement if non-NULL,
				  omitted otherwise

		Words 10,11	: Outer Displacement if non-NULL,
				  omitted otherwise


Thus a 68020 instruction can consist of as many as 11 words (!) provided that
all of the specified components exist. Needless to say, executing such a MOVE
takes rather longer than MOVE.W D0,D1, for example, but gives some indication
of the enhanced power of the new 32-bit members of the family.


		MC68020 EXTRA INSTRUCTIONS AND EXTENSIONS
		=========================================

			TO MC68000 INSTRUCTIONS
			=======================


Before covering specific instructions and extensions to the standard MC68000
instructions allowed by the MC68020, the following should be noted:


	1) Those instructions containing the MMM RRR fields to determine
	   the addressing mode of operands retain their original format,
	   extra values of those fields being used by the MC68020 to ac-
	   cess new addressing modes (e.g., memory indirect). The major
	   change is from the MC68000 instruction extension word for the
	   indexed operands to either the MC68020 Brief Format or MC68020
	   Full Format extension words (covered above);

	2) If there ARE changes to the instruction format, then these
	   changes will be covered below.


The full list of extended and new instructions now follows.


Bcc	: Branch Conditionally (Includes BRA) (MC68020)

	Operation : IF condition is TRUE
			THEN
			  PC + d -> PC
			ELSE
			continue normal sequential operation

	Assembler : Bcc <LABEL>

	Attributes: Size=Byte,Word,Long

	Description	: The conditional expression specified in the
			  instruction is evaluated and the result tested.
			  If the result is TRUE, then the displacement is
			  sign-extended to 32 bits and added on to the
			  current value of the program counter, at which
			  point program execution resumes. If the result
			  is FALSE, program execution continues sequen-
			  tially as normal.

	Condition Codes : NOT AFFECTED.

	Instruction Format :

		0 1 1 0 C C C C D D D D D D D D

	Instruction Fields :

		CCCC	: Condition code field. Specifies the condi-
			  tional expression to compute prior to the
			  branch decision. Values are given in the
			  conditional branch table in the companion
			  file typed_68000.doc. A field value of 0000
			  corresponds to a BRA instruction, and a
			  field value of 0001 corresponds to a BSR in-
			  struction (see below).

		DDDD..	: Displacement field. The 68020 accepts THREE
			  displacement sizes. For short branches, this
			  field contains the byte-sized displacement
			  which is sign-extended to 32 bits prior to
			  addition to the program counter.

			  If this field contains zero (00000000) then
			  the word following the instruction word con-
			  tains a word-sized displacement, which is
			  sign-extended to 32 bits prior to adding to
			  the program counter. This mode and the prev-
			  ious mode is available to ALL MC680x0 CPUs.

			  If this field contains $FF (11111111), then
			  the two words following the instruction word
			  contain a longword-sized displacement to be
			  added directly to the program counter. This
			  mode is available to the MC68020 onwards.


BFCHG	: Test Bit Field And Change

	Operation : dst{off:wd} -> CCR

		    NOT(dst{off:wd}) -> dst{off:wd}

	Assembler : BFCHG <ea>{off:wd}

	Attributes: Unsized.

	Description	: Test the state of the specified bit field and
			  alter the condition codes accordingly. Once
			  the condition codes have been duly altered,
			  invert all of the specified bits of the spec-
			  ified bit field.

	Condition Codes : X N Z V C
			  - * * 0 0

			  N : Set if the most significant bit of the
			      bit field is zero. Cleared otherwise.

			  Z : Set if all the bits of the bit field are
			      zero. Cleared otherwise.

			  V : Always Cleared.

			  C : Always Cleared.

			  X : Not Affected.

	Instruction Format :

		1 1 1 0 1 0 1 0 1 1 M M M R R R

		0 0 0 0 A O O O O O B W W W W W

	Instruction Fields :

		MMM, RRR: See MC68020 Instruction Extension
			  Words Above.

		A	: A = 0 if the offset is an immediate
			  value, A = 1 if the offset is con-
			  tained in a data register.

		OOO..	: Offset field. If the offset is an
			  immediate value, then the value 0-31
			  is stored here. If the offset is
			  contained in a data register, then
			  the register number D0-D7 is stored
			  here.

		B	: B = 0 if the width is an immediate
			  value. B = 1 if the width is contained
			  in a data register.

		WWW..	: Width Field. If the width is an immed-
			  iate value, then the values 0, 1-31 are
			  stored here, representing a width of
			  32, 1-31 respectively. If the width is
			  contained in a data register, then the
			  register number D0-D7 is stored here.

	Addressing Modes : All modes EXCEPT:

			   An
			   (An)+
			   -(An)
			   #<data>

			   and PC relative modes, are allowed for the
			   destination operand.


BFCLR	: Test Bit Field And Clear

	Operation : dst{off:wd} -> CCR

		    0 -> dst{off:wd}

	Assembler : BFCLR <ea>{off:wd}

	Attributes: Unsized.

	Description	: Test the state of the specified bit field and
			  alter the condition codes accordingly. Once
			  the condition codes have been duly altered,
			  clear all of the bits of the specified bit
			  field.

	Condition Codes : X N Z V C
			  - * * 0 0

			  N : Set if the most significant bit of the
			      bit field is zero. Cleared otherwise.

			  Z : Set if all the bits of the bit field are
			      zero. Cleared otherwise.

			  V : Always Cleared.

			  C : Always Cleared.

			  X : Not Affected.

	Instruction Format :

		1 1 1 0 1 1 0 0 1 1 M M M R R R

		0 0 0 0 A O O O O O B W W W W W

	Instruction Fields :

		MMM, RRR: See MC68020 Instruction Extension
			  Words Above.

		A	: A = 0 if the offset is an immediate
			  value, A = 1 if the offset is con-
			  tained in a data register.

		OOO..	: Offset field. If the offset is an
			  immediate value, then the value 0-31
			  is stored here. If the offset is
			  contained in a data register, then
			  the register number D0-D7 is stored
			  here.

		B	: B = 0 if the width is an immediate
			  value. B = 1 if the width is contained
			  in a data register.

		WWW..	: Width Field. If the width is an immed-
			  iate value, then the values 0, 1-31 are
			  stored here, representing a width of
			  32, 1-31 respectively. If the width is
			  contained in a data register, then the
			  register number D0-D7 is stored here.

	Addressing Modes : All modes EXCEPT:

			   An
			   (An)+
			   -(An)
			   #<data>

			   and PC relative modes, are allowed for the
			   destination operand.


BFEXTS	: Bit Field Extract Signed

	Operation : src{off:wd} -> Dn

	Assembler : BFEXTS <ea>{off:wd},Dn

	Attributes: Unsized

	Description	: Extract a bit field from the specified source
			  location, sign-extend to 32 bits, and store the
			  result in the specified data register.

	Condition Codes	: X N Z V C
			  - * * 0 0

			  N Set if the most significant bit of the bit
			    field is set. Cleared otherwise.

			  Z Set if the bit field contains all zeros.
			    Cleared otherwise.

			  V Always Cleared.

			  C Always Cleared.

			  X Not Affected.

	Instruction Format :

		1 1 1 0 1 0 1 1 1 1 M M M R R R

		0 D D D A O O O O O B W W W W W

	Instruction Fields :

		MMM, RRR: See MC68020 Instruction Extension Words
			  above.

		DDD	: Destination Data Register field. Specifies
			  the destination data register D0-D7.

		A	: A = 0 if the offset is an immediate
			  value, A = 1 if the offset is con-
			  tained in a data register.

		OOO..	: Offset field. If the offset is an
			  immediate value, then the value 0-31
			  is stored here. If the offset is
			  contained in a data register, then
			  the register number D0-D7 is stored
			  here.

		B	: B = 0 if the width is an immediate
			  value. B = 1 if the width is contained
			  in a data register.

		WWW..	: Width Field. If the width is an immed-
			  iate value, then the values 0, 1-31 are
			  stored here, representing a width of
			  32, 1-31 respectively. If the width is
			  contained in a data register, then the
			  register number D0-D7 is stored here.

	Addressing Modes : All modes EXCEPT:

			   An
			   (An)+
			   -(An)
			   #<data>

			   are allowed for the source operand.


BFEXTU	: Bit Field Extract Unsigned

	Operation : src{off:wd} -> Dn

	Assembler : BFEXTU <ea>{off:wd},Dn

	Attributes: Unsized

	Description	: Extract a bit field from the specified source
			  location, zero-extend to 32 bits, and store the
			  result in the specified data register.

	Condition Codes	: X N Z V C
			  - * * 0 0

			  N Set if the most significant bit of the bit
			    field is set. Cleared otherwise.

			  Z Set if the bit field contains all zeros.
			    Cleared otherwise.

			  V Always Cleared.

			  C Always Cleared.

			  X Not Affected.

	Instruction Format :

		1 1 1 0 1 0 0 1 1 1 M M M R R R

		0 D D D A O O O O O B W W W W W

	Instruction Fields :

		MMM, RRR: See MC68020 Instruction Extension Words
			  above.

		DDD	: Destination Data Register field. Specifies
			  the destination data register D0-D7.

		A	: A = 0 if the offset is an immediate
			  value, A = 1 if the offset is con-
			  tained in a data register.

		OOO..	: Offset field. If the offset is an
			  immediate value, then the value 0-31
			  is stored here. If the offset is
			  contained in a data register, then
			  the register number D0-D7 is stored
			  here.

		B	: B = 0 if the width is an immediate
			  value. B = 1 if the width is contained
			  in a data register.

		WWW..	: Width Field. If the width is an immed-
			  iate value, then the values 0, 1-31 are
			  stored here, representing a width of
			  32, 1-31 respectively. If the width is
			  contained in a data register, then the
			  register number D0-D7 is stored here.

	Addressing Modes : All modes EXCEPT:

			   An
			   (An)+
			   -(An)
			   #<data>

			   are allowed for the source operand.


BFFFO	: Bit Field Find First One

	Operation : src{off:wd} bit scan -> Dn

	Assembler : BFFFO <ea>{off:wd},Dn

	Attributes: Unsized

	Description	: Scan the specified bit field for the presence
			  of a '1' bit, starting at the most significant
			  bit of the bit field (the leftmost bit).

			  If a '1' bit is found, then the bit offset of
			  the first '1' bit located (which is the bit
			  offset of the source operand plus the relative
			  offset from the start of the bit field) is
			  stored in the specified data register.

			  If the bit field contains all zeros, then the
			  value stored in the specified data register is
			  the value of the source operand bit offset PLUS
			  the value of the source operand field width,
			  which is the offset to the next element of a
			  bit field array. The condition codes are set
			  according to the contents of the original bit
			  field.

	Condition Codes	: X N Z V C
			  - * * 0 0

			  N Set if the most significant bit of the bit
			    field is 1. Cleared otherwise.

			  Z Set if all bits of the bit field contain
			    zero. Cleared otherwise.

			  V Always Cleared.

			  C Always Cleared.

			  X Not Affected.

	Instruction Format :

		1 1 1 0 1 1 0 1 1 1 M M M R R R

		0 D D D A O O O O O B W W W W W

	Instruction Fields :

		MMM, RRR: See MC68020 Instruction Extension Words
			  above.

		DDD	: Destination Data Register field. Specifies
			  the destination data register D0-D7.

		A	: A = 0 if the offset is an immediate
			  value, A = 1 if the offset is con-
			  tained in a data register.

		OOO..	: Offset field. If the offset is an
			  immediate value, then the value 0-31
			  is stored here. If the offset is
			  contained in a data register, then
			  the register number D0-D7 is stored
			  here.

		B	: B = 0 if the width is an immediate
			  value. B = 1 if the width is contained
			  in a data register.

		WWW..	: Width Field. If the width is an immed-
			  iate value, then the values 0, 1-31 are
			  stored here, representing a width of
			  32, 1-31 respectively. If the width is
			  contained in a data register, then the
			  register number D0-D7 is stored here.

	Addressing Modes : All modes EXCEPT:

			   An
			   (An)+
			   -(An)
			   #<data>

			   are allowed for the source operand.


BFINS	: Bit Field Insert

	Operation : Dn -> dst{off:wd}

	Assembler : BFINS Dn,<ea>{off:wd}

	Attributes: Unsized

	Description	: Move a bit field from the low-order bits of the
			  specified data register and store the bits in
			  the bit field specified by the destination lo-
			  cation. The condition codes are set according to
			  the FINAL STATE of the bit field after insertion.

	Condition Codes	: X N Z V C
			  - * * 0 0

			  N Set if the most significant bit of the resul-
			    tant bit field is set. Cleared otherwise.

			  Z Set if the resultant bit field contains all
			    zeros. Cleared otherwise.

			  V Always Cleared.

			  C Always Cleared.

			  X Not Affected.

	Instruction Format :

		1 1 1 0 1 1 1 1 1 1 M M M R R R

		0 D D D A O O O O O B W W W W W

	Instruction Fields :

		MMM, RRR: See MC68020 Instruction Extension Words
			  above.

		DDD	: Destination Data Register field. Specifies
			  the destination data register D0-D7.

		A	: A = 0 if the offset is an immediate
			  value, A = 1 if the offset is con-
			  tained in a data register.

		OOO..	: Offset field. If the offset is an
			  immediate value, then the value 0-31
			  is stored here. If the offset is
			  contained in a data register, then
			  the register number D0-D7 is stored
			  here.

		B	: B = 0 if the width is an immediate
			  value. B = 1 if the width is contained
			  in a data register.

		WWW..	: Width Field. If the width is an immed-
			  iate value, then the values 0, 1-31 are
			  stored here, representing a width of
			  32, 1-31 respectively. If the width is
			  contained in a data register, then the
			  register number D0-D7 is stored here.

	Addressing Modes : All modes EXCEPT:

			   An
			   (An)+
			   -(An)
			   #<data>

			   and PC relative modes, are allowed for the
			   destination operand.


BFSET	: Test Bit Field And Set

	Operation : dst{off:wd} -> CCR

		    1 -> dst{off:wd}

	Assembler : BFSET <ea>{off:wd}

	Attributes: Unsized.

	Description	: Test the state of the specified bit field and
			  alter the condition codes accordingly. Once
			  the condition codes have been duly altered,
			  set all of the bits of the specified bit field
			  (to 1).

	Condition Codes : X N Z V C
			  - * * 0 0

			  N : Set if the most significant bit of the
			      bit field is zero. Cleared otherwise.

			  Z : Set if all the bits of the bit field are
			      zero. Cleared otherwise.

			  V : Always Cleared.

			  C : Always Cleared.

			  X : Not Affected.

	Instruction Format :

		1 1 1 0 1 1 1 0 1 1 M M M R R R

		0 0 0 0 A O O O O O B W W W W W

	Instruction Fields :

		MMM, RRR: See MC68020 Instruction Extension
			  Words Above.

		A	: A = 0 if the offset is an immediate
			  value, A = 1 if the offset is con-
			  tained in a data register.

		OOO..	: Offset field. If the offset is an
			  immediate value, then the value 0-31
			  is stored here. If the offset is
			  contained in a data register, then
			  the register number D0-D7 is stored
			  here.

		B	: B = 0 if the width is an immediate
			  value. B = 1 if the width is contained
			  in a data register.

		WWW..	: Width Field. If the width is an immed-
			  iate value, then the values 0, 1-31 are
			  stored here, representing a width of
			  32, 1-31 respectively. If the width is
			  contained in a data register, then the
			  register number D0-D7 is stored here.

	Addressing Modes : All modes EXCEPT:

			   An
			   (An)+
			   -(An)
			   #<data>

			   and PC relative modes, are allowed for the
			   destination operand.


BFTST	: Test Bit Field

	Operation : dst{off:wd} -> CCR

	Assembler : BFTST <ea>{off:wd}

	Attributes: Unsized.

	Description	: Test the state of the specified bit field and
			  alter the condition codes accordingly.

	Condition Codes : X N Z V C
			  - * * 0 0

			  N : Set if the most significant bit of the
			      bit field is zero. Cleared otherwise.

			  Z : Set if all the bits of the bit field are
			      zero. Cleared otherwise.

			  V : Always Cleared.

			  C : Always Cleared.

			  X : Not Affected.

	Instruction Format :

		1 1 1 0 1 0 0 0 1 1 M M M R R R

		0 0 0 0 A O O O O O B W W W W W

	Instruction Fields :

		MMM, RRR: See MC68020 Instruction Extension
			  Words Above.

		A	: A = 0 if the offset is an immediate
			  value, A = 1 if the offset is con-
			  tained in a data register.

		OOO..	: Offset field. If the offset is an
			  immediate value, then the value 0-31
			  is stored here. If the offset is
			  contained in a data register, then
			  the register number D0-D7 is stored
			  here.

		B	: B = 0 if the width is an immediate
			  value. B = 1 if the width is contained
			  in a data register.

		WWW..	: Width Field. If the width is an immed-
			  iate value, then the values 0, 1-31 are
			  stored here, representing a width of
			  32, 1-31 respectively. If the width is
			  contained in a data register, then the
			  register number D0-D7 is stored here.

	Addressing Modes : All modes EXCEPT:

			   An
			   (An)+
			   -(An)
			   #<data>

			   are allowed for the destination operand.


BKPT	: Breakpoint (MC68020)

	Operation : IF Breakpoint Vector Acknowledged
			THEN
			  execute returned operation word
			ELSE
			  trap via illegal instruction vector

	Assembler : BKPT #<data>

	Attributes: Unsized

	Description	: This instruction is used in conjunction
			  with external hardware support to provide
			  a breakpoint function for debuggers and
			  real-time emulators. As such, the opera-
			  tion will be implementation dependent.

			  Typically, this instruction will be sup-
			  ported by the MC68851 Paged Memory Manage-
			  Ment Unit, which contains the hardware re-
			  quired to replace the overwritten instruc-
			  tion word.

			  The MC68020 generates a Breakpoint Acknow-
			  edge bus cycle, with the immediate data on
			  address lines A2-A4, address lines A0 and A1
			  on the address bus being pulled low.

			  The normal response to a BKPT by supporting
			  hardware is to send an operation word (typi-
			  cally the original replaced instruction) on
			  the data lines with the DSACKx signal asser-
			  ted (this is an ACTIVE LOW signal). The op-
			  eration word is executed in place of the
			  breakpoint instruction.

			  For the exception response, a bus error sig-
			  nal will cause the MC68020 to take the ille-
			  gal instruction exception.

			  If external support for this instruction is
			  NOT provided in hardware, then the illegal
			  instruction exception is taken.

	Condition Codes : NOT AFFECTED.

	Instruction Format :

		0 1 0 0 1 0 0 0 0 1 0 0 1 V V V

	Instruction Fields :

		VVV	: Vector field. Specified the breakpoint for which
			  the processor is to request the corresponding
			  operation word. Eight breakpoints from BKPT #0
			  to BKPT #7 are supported by the MC68851, and
			  the MC68851 can save overwritten instructions
			  and replace them upon execution of the BKPT
			  instruction. Other hardware support possibil-
			  ities exist, but the MC68851 PMMU is THE support
			  system recommended by Motorola.


BSR	: Branch To Subroutine (MC68020 onwards)

	Operation : SP - 4 -> SP
		    PC -> (SP)
		    PC + d -> PC

	Assembler : BSR <label>

	Attributes: Size=Byte, Word, Long

	Description	: The long word address of the instruction
			  immediately following the BSR instruction
			  is pushed onto the stack. The value of the
			  displacement is then added to the value of
			  the program counter, and program execution
			  continues at this new location.

			  For the 68020, the BSR instruction is ex-
			  tended to allow longword displacements to
			  be specified, allowing relative subroutine
			  calls to be performed across the entire
			  address space of the machine.

	Condition Codes : NOT AFFECTED.

	Instruction Format :

		0 1 1 0 0 0 0 1 D D D D D D D D

	Instruction Fields :

		DDDD..	: Displacement field. The 68020 accepts THREE
			  displacement sizes. For short branches, this
			  field contains the byte-sized displacement
			  which is sign-extended to 32 bits prior to
			  addition to the program counter.

			  If this field contains zero (00000000) then
			  the word following the instruction word con-
			  tains a word-sized displacement, which is
			  sign-extended to 32 bits prior to adding to
			  the program counter. This and the previous
			  mode is available to all MC680x0 CPUs.

			  If this field contains $FF (11111111), then
			  the two words following the instruction word
			  contain a longword-sized displacement to be
			  added directly to the program counter. This
			  mode is available to the MC68020 onwards.


CALLM	: Call Module (MC68020 ONLY!)

	Operation : Save current module state on stack.
		    Load new module state from destination.

	Assembler : CALLM #<data>,<ea>

	Attributes: Unsized.

	Description	: The destination effective address is the
			  address of a module descriptor. A module
			  frame is created at the top of the stack,
			  and the current module state is saved in
			  the stack frame thus reserved.

			  A new module state is loaded from the de-
			  scriptor addressed by the destination op-
			  erand. Up to 255 bytes of arguments are
			  passed to the new module, the size of the
			  argument block being specified in the source
			  immediate operand. 

	Condition Codes : NOT AFFECTED.

	Instruction Format:

		0 0 0 0 0 1 1 0 1 1 M M M R R R

		0 0 0 0 0 0 0 0 A A A A A A A A

	Instruction Fields:

		MMM, RRR: See MC68020 Instruction Extension
			  Words Above.

		AAA...	: Argument Count field. Specifies the number
			  of bytes of arguments to be transferred to
			  the new module (as specified in the source
			  operand). Legal values are from 0 to 255
			  bytes. This same number of bytes is removed
			  from the stack by the RTM instruction (see
			  below).

	Addressing Modes : All modes EXCEPT:

			   An
			   (An)+
			   -(An)
			   #<data>

			   are allowed for the destination operand.


CAS	: Compare And Swap With Operand

	Operation : dst - Dc -> CCR

		    IF Z=1
			THEN
			  Du -> dst
			ELSE
			  dst -> Dc

	Assembler : CAS Dc,Du,<ea>

	Attributes: Size = Byte, Word, Long

	Description	: This instruction performs a Compare And Swap
			  operation. The destination operand is com-
			  pared with the contents of the data register
			  containing the comparison operand (here, Dc)
			  and the condition codes set accrordingly. If
			  the Zero flag is set (indicating that the two
			  operands have equal values), then the contents
			  of the data register containing the update op-
			  erand (here, Du) is moved to the destination
			  location. If the Zero flag is cleared, then
			  the destination operand is left unchanged, and
			  its value moved to the data register used to
			  store the comparison operand.

			  This operation is performed using an indivis-
			  ible read-modify-write cycle to allow synchron-
			  isation of several processors. See notes below.

	Condition Codes : X N Z V C

			  N : Set if the result is negative. Cleared
			      otherwise.

			  Z : Set if the result is zero. Cleared other-
			      wise.

			  V : Set if an overflow is generated. Cleared
			      otherwise.

			  C : Set if a carry is generated. Cleared
			      otherwise.

			  X : Not Affected.

	Instruction Format :

		0 0 0 0 1 Z Z 0 1 1 M M M R R R

		0 0 0 0 0 0 0 U U U 0 0 0 C C C

	Instruction Fields:

		MMM, RRR: See MC68020 Instruction Extension
			  Words Above.

		ZZ	: Size field. Specifies the size of the
			  operation:

			  01 = Byte operation.
			  10 = Word operation.
			  11 = Long operation.

		UUU	: Specifies the data register to be used to
			  contain the update operand to be moved to
			  the destination effective address if the
			  comparison is successful.

		CCC	: Specifies the data register to be used to
			  contain the comparison operand to compare
			  with the destination operand.

	Addressing Modes : All modes EXCEPT:

			   Dn
			   An
			   #<data>

			   and PC relative modes, are allowed for the
			   destination operand.

	Notes : This instruction may be used to manage a linked list
		safely in a multiprocessor environment, where the
		linked list is used to manage a resource shared be-
		tween several processors and their tasks.


CAS2	: Compare And Swap Two Operands Simultaneously

	Operation : dst1 - Dc1 -> CCR

		    IF Z=1
			THEN
			  dst2 - Dc2 -> CCR
			  IF Z=1
			      THEN
				Du1 -> dst1
				Du2 -> dst2
			      ELSE
				dst1 -> Dc1
				dst2 -> Dc2
			ELSE
			  dst1 -> Dc1
			  dst2 -> Dc2

	Assembler : CAS Dc1:Dc2,Du1:Du2,(Rn1):(Rn2)

	Attributes: Size = Word, Long

	Description	: This operation first compares the contents of
			  the first compare operand and the first dest-
			  ination operand, and sets the condition codes.

			  If the Zero flag is set after this first com-
			  parison, a second comparison is made, between
			  the second comparison operand and the second
			  destination operand, and the condition codes
			  set accordingly.

			  If the Zero flag is set after the second com-
			  parison, then the contents of the two update
			  operands are moved to the respective destin-
			  ation operands.

			  If either comparison fails, and the Zero flag
			  is cleared, then the destination operands are
			  left unmodified, and the values of the destin-
			  ation operands are copied to the respective
			  comparison operands.

			  NOTE : Due to the complexity of this instruction,
			  the programmer is free to specify data registers
			  in the destination operands, and use them as if
			  they were address registers. This is the ONLY
			  instruction where such freedom is allowed! For
			  example, it is legal to use:

				CAS2 D0:D1,D2:D3,(D4):(D5)

			  and use D4 and D5 as though they were address
			  registers using the (An) addressing mode.

			  This operation is performed using an indivis-
			  ible read-modify-write cycle to allow synchron-
			  isation of several processors. See notes below.
			  

	Condition Codes : X N Z V C

			  N : Set if the result is negative. Cleared
			      otherwise.

			  Z : Set if the result is zero. Cleared other-
			      wise.

			  V : Set if an overflow is generated. Cleared
			      otherwise.

			  C : Set if a carry is generated. Cleared
			      otherwise.

			  X : Not Affected.

	Instruction Format :

		0 0 0 0 1 Z Z 0 1 1 1 1 1 1 0 0

		A R R R 0 0 0 U U U 0 0 0 C C C

		B S S S 0 0 0 V V V 0 0 0 D D D

	Instruction Fields:

		MMM, RRR: See MC68020 Instruction Extension
			  Words Above.

		ZZ	: Size field. Specifies the size of the
			  operation:

			  01 = Byte operation.

			  10 = Word operation.

			  11 = Long operation.

		A	: D/A1 field. A = 0 if the RRR field specifies
			  a data register for the Rn1 operand, A = 1 if
			  the RRR field specifies an address register.

		RRR	: Register number for the Rn1 operand above.

		UUU	: Specifies which data register is to be used
			  for the first update operand (Du1 above).

		CCC	: Specifies which data register is to be used
			  for the first comparison operand (Dc1 above).

		B	: D/A2 field. B = 0 if the SSS field specifies
			  a data register for the Rn2 operand, B = 1 if
			  the SSS field specifies an address register.

		SSS	: Register number for the Rn2 operand above.

		VVV	: Specifies which data register is to be used
			  for the second update operand (Du2 above).

		DDD	: Specifies which data register is to be used
			  for the second comparison operand (Dc2 above).

	Addressing Modes : All modes EXCEPT:

			   Dn
			   An
			   (An)+
			   -(An)
			   #<data>

			   and PC relative modes, are allowed for the
			   destination operand.

	Notes : This instruction may be used to safely update a doubly-
		linked list in a multiprocessor environment where that
		list is used to manage a resource shared across several
		processors and their tasks.


CHK	: Check Register Against Bounds (MC68020)

	Operation : IF Dn < 0 OR Dn > <ea>
			THEN
			  TRAP (CHK exception vector)
			ELSE
			  continue normal execution

	Assembler : CHK <ea>,Dn

	Attributes: Size = Word, Long.

	Description	: The content of the data register is examined
			  and compared to the upper bound stored at the
			  source effective address. The upper bound is
			  a twos complement integer.

			  If the register value is less than zero, or
			  greater than the upper bound, then the pro-
			  cessor initiates exception processing via the
			  CHK exception vector.

			  The 68000 version of this instruction only
			  allows word-sized comparisons. The instruction
			  in this case is identical across both proces-
			  sors (see ZZZ field below).

	Condition Codes : X N Z V C
			  - * U U U

			  N : Set if Dn<0, cleared if Dn> <ea>.
			      Undefined otherwise.

			  Z : Undefined.

			  V : Undefined.

			  C : Undefined.

			  X : Not Affected.

	Instruction Format :

		0 1 0 0 D D D Z Z Z R R R M M M

	Instruction Fields :

		MMM, RRR: See MC68020 Instruction Extension
			  Words Above.

		ZZZ	: Size field. The two legal values
			  are:

			  110 : Word operation.

			  100 : Long operation.

		DDD	: Data Register field. Specifies the data
			  register to use for the destination op-
			  erand.


	Addressing Modes : All modes EXECPT An (address register
			   direct) are allowed.


CHK2	: Check Register Against Bounds Pair And TRAP

	Operation : IF Dn < <ea lower bound>
			OR
		       Dn > <ea upper bound>
			THEN
			  TRAP (CHK exception vector)
			ELSE
			  continue normal execution

	Assembler : CHK2 <ea>,Rn

	Attributes: Size = Byte, Word, Long.

	Description	: The contents of the specified register (here,
			  either data or address register) are compared
			  with the PAIR of bounds specifiers stored at
			  the source effective address in the order:

				<ea>	: Lower Bound
				<ea+N>	: Upper Bound

			  where N is the size of the operand.

			  If the value of the specified register is less
			  than the value of the lower bound, or greater
			  than the value of the upper bound, then an ex-
			  ception is taken via the CHK exception vector.
			  If the value lies within the specified bounds,
			  then execution continues as normal.

			  If the destination register is a data register,
			  then the comparison only affects that portion of
			  the data register whose size is specified.

			  If the destination register is an address regi-
			  ster, then the bounds values are sign-extended
			  to 32 bits before the comparison is performed. 

			  Note:either a signed or an unsigned comparison
			  can be performed. For signed comparisons, the
			  lower bound should be arithmetically smaller,
			  and for unsigned comparisons, the lower bound
			  should be logically smaller.

	Condition Codes : X N Z V C
			  - U * U *

			  N : Undefined.

			  Z : Set if Rn is equal to either bound. Cleared
			      otherwise.

			  V : Undefined.

			  C : Set if Rn is out of bounds. Cleared other-
			      wise.

			  X : Not Affected.

	Instruction Format :

		0 0 0 0 0 Z Z 0 1 1 M M M R R R

		A D D D 1 0 0 0 0 0 0 0 0 0 0 0

	Instruction Fields :

		MMM, RRR: See MC68020 Instruction Extension
			  Words Above.

		ZZ	: Size field. The two legal values
			  are:

			  01 : Byte operation.

			  10 : Word operation.

			  11 : Long operation.

		A	: D/A field. A = 0 if the register to be checked
			  is a data register, A = 1 if the register to be
			  checked is an address register.

		DDD	: Register field. Specifies the data or address
			  register to use for the destination operand.


	Addressing Modes : All modes EXECPT:

			   Dn
			   An
			   (An)+
			   -(An)
			   #<data>

			   are allowed for the source operand.


CMP2	: Check Register Against Bounds Pair

	Operation : Compare Rn against upper & lower bounds -> CCR

	Assembler : CHK2 <ea>,Rn

	Attributes: Size = Byte, Word, Long.

	Description	: The contents of the specified register (here,
			  either data or address register) are compared
			  with the PAIR of bounds specifiers stored at
			  the source effective address in the order:

				<ea>	: Lower Bound
				<ea+N>	: Upper Bound

			  where N is the size of the operand.

			  If the destination register is a data register,
			  then the comparison only affects that portion of
			  the data register whose size is specified.

			  If the destination register is an address regi-
			  ster, then the bounds values are sign-extended
			  to 32 bits before the comparison is performed. 

			  Note:either a signed or an unsigned comparison
			  can be performed. For signed comparisons, the
			  lower bound should be arithmetically smaller,
			  and for unsigned comparisons, the lower bound
			  should be logically smaller.

			  This instruction is analogous to CHK2, but is
			  provided to allow comparisons without the need
			  for exception processing.

	Condition Codes : X N Z V C
			  - U * U *

			  N : Undefined.

			  Z : Set if Rn is equal to either bound. Cleared
			      otherwise.

			  V : Undefined.

			  C : Set if Rn is out of bounds. Cleared other-
			      wise.

			  X : Not Affected.

	Instruction Format :

		0 0 0 0 0 Z Z 0 1 1 M M M R R R

		A D D D 0 0 0 0 0 0 0 0 0 0 0 0

	Instruction Fields :

		MMM, RRR: See MC68020 Instruction Extension
			  Words Above.

		ZZ	: Size field. The two legal values
			  are:

			  01 : Byte operation.

			  10 : Word operation.

			  11 : Long operation.

		A	: D/A field. A = 0 if the register to be checked
			  is a data register, A = 1 if the register to be
			  checked is an address register.

		DDD	: Register field. Specifies the data or address
			  register to use for the destination operand.


	Addressing Modes : All modes EXECPT:

			   Dn
			   An
			   (An)+
			   -(An)
			   #<data>

			   are allowed for the source operand.


cpBcc	: Branch On Coprocessor Condition

	Operation : If cpcc = TRUE
			THEN
			  PC + d -> PC
			ELSE
			  continue normal execution

	Assembler : cpBcc <label>

	Attributes: Size = Word, Long

	Description	: If the specified coprocessor condition is
			  true, then the value of the displacement
			  is added onto the value of the program
			  counter, and execution continues at this
			  new location. If the specified coprocessor
			  condition is false, then execution contin-
			  ues at the next instruction in sequence.

			  If the branch is a word branch, then the
			  displacement is sign-extended to 32 bits
			  before being added to the PC.

	Condition Codes : NOT AFFECTED.

	Instruction Format :

		1 1 1 1 I I I 0 1 W C C C C C C

		X X X X X X X X X X X X X X X X

	Instruction Fields :

		III	: Coprocessor ID field. Specifies the
			  coprocessor that is to perform this
			  operation.

			  Current values:

			  000 = MC68851 Paged Memory Management Unit

			  001 = MC6881/68882 Mathematics Coprocessor

		W	: W/L field. W = 0 specifies a word-length
			  branch, W = 1 specifies a longword-length
			  branch.

		CCC...	: Coprocessor condition field. Contains the
			  condition specification for the given co-
			  processor. This field is passed to the
			  coprocessor, which provides directives to
			  the CPU for processing this instruction.

		XXX...	: Optional Coprocessor Defined Extension Word(s)

		Following these words are either one word for a 16-bit
		branch displacement, or two words for a 32-bit displace-
		ment branch.


cpDBcc	: Test Coprocessor Condition, Decrement And Branch

	Operation : IF cpcc = FALSE
			THEN
			  Dn - 1 -> Dn
			  IF Dn <> -1
				THEN
				  PC + d -> PC
				ELSE
				  continue normal execution
			ELSE
			  continue normal execution

	Assembler : cpDBcc Dn,<label>

	Attributes: Size = Word.

	Description	: If the specified coprocessor condition is true,
			  then execution continues with the next instruc-
			  tion. If the specified coprocessor condition is
			  false, then the low order word of the specified
			  data register is decremented by 1. If the result
			  of this decrementation is equal to -1, execution
			  continues with the next instruction. Otherwise
			  the 16-bit displacement is sign-extended to 32
			  bits and added on to the program counter, and ex-
			  ecution continues at this new location.

	Condition Codes : NOT AFFECTED.

	Instruction Format :

		1 1 1 1 I I I 0 0 1 0 0 1 D D D

		0 0 0 0 0 0 0 0 0 0 C C C C C C

		X X X X X X X X X X X X X X X X

	Instruction Fields :

		III	: Coprocessor ID field. Specifies the coprocesor
			  that is to process this operation. See cpBcc
			  above for current coprocessor IDs.

		DDD	: Data Register field. Specifies the data regis-
			  ter to be used as the counter.

		CCC...	: Coprocessor condition field. Contains the
			  condition specification for the given co-
			  processor. This field is passed to the
			  coprocessor, which provides directives to
			  the CPU for processing this instruction.

		XXX...	: Optional Coprocessor Defined Extension Word(s).

		Following these words is a 16-bit word containing the
		displacement to be used.


cpGEN	: Coprocessor General Function.

	Operation : Pass Command Word To Coprocessor.

	Assembler : cpGEN <parameters>

		    <parameters> as defined by given coprocessor

	Attributes: Unsized.

	Description	: This instruction is used by coprocessors to
			  specify the general data movement and data
			  processing operations for the specified co-
			  processor. The coprocessor determines the
			  operation from the Coprocessor Command Word
			  immediately following the cpGEN command word.

			  Usually, a coprocessor defines specific ins-
			  tances of this instruction to provide its in-
			  struction set.

	Condition Codes : Determined By Coprocessor. Unchanged Otherwise.

	Instruction Format :

		1 1 1 1 I I I 0 0 0 M M M R R R

		C C C C C C C C C C C C C C C C

		X X X X X X X X X X X X X X X X

	Instruction Fields :

		III	: Coprocessor ID field. Specifies the coprocesor
			  that is to process this operation. See cpBcc
			  above for current coprocessor IDs.

		MMM, RRR: See MC68020 Instruction Extension Words Above.
			  Used to specify an operand in main memory for
			  the coprocessor operation if specified, or
			  the CPU registers.

		CCC...	: Coprocessor Command Field. Specifies the co-
			  processor instruction to be performed.

		XXX...	: Optional Coprocessor Defined Extension Word(s).


cpRESTORE	: Restore Coprocessor Machine State

		  (PRIVIEGED INSTRUCTION)

	Operation : IF supervisor state
			THEN
			  Restore Coprocessor Machine State
			ELSE
			  TRAP (Privilege Violation).

	Assembler : cpRESTORE <ea>

	Attributes: Unsized.

	Description	: If the CPU is in supervisor mode, then restore
			  the machine state of the coprocessor as saved
			  earlier by a cpSAVE instruction (see below).
			  If the CPU is in user mode, take the Privilege
			  Violation exception.

	Condition Codes : NOT AFFECTED.

	Instruction Format :

		1 1 1 1 I I I 1 0 1 M M M R R

	Instruction Fields :

		III	: Coprocessor ID field. Specifies the coprocesor
			  that is to process this operation. See cpBcc
			  above for current coprocessor IDs.

		MMM, RRR: See MC68020 Instruction Extension Words Above.
			  Used to specify the effective address of the
			  saved coprocessor state to restore.

	Addressing Modes : All EXECPT:

			   Dn
			   An
			   -(An)
			   #<data>

			   are allowed for the effective address operand.

	Notes : If the coprocessor passes a communication format word
		of the 'come again' form for continued processing,
		pending interrupts are not serviced. It is the PRO-
		GRAMMER'S responsibility to take account of this!


cpSAVE	: Save Coprocessor Machine State

	  (PRIVILEGED INSTRUCTION)

	Operation : IF supervisor state
			THEN
			  Save Coprocessor Machine State
			ELSE
			  TRAP (Privilege Violation).

	Assembler : cpSAVE <ea>

	Attributes: Unsized.

	Description	: If the CPU is in the supervisor mode, then
			  save the entire machine state of the speci-
			  fied coprocessor at the destination effec-
			  tive address. If the CPU is in user mode,
			  then take the Privilege Violation exception.

	Condition Codes : NOT AFFECTED.

	Instruction Format :

		1 1 1 1 I I I 1 0 0 M M M R R R

	Instruction Fields :

		III	: Coprocessor ID field. Specifies the coprocesor
			  that is to process this operation. See cpBcc
			  above for current coprocessor IDs.

		MMM, RRR: See MC68020 Instruction Extension Words Above.
			  Used to specify the effective address of the
			  saved coprocessor state to restore.

	Addressing Modes : All EXECPT:

			   Dn
			   An
			   (An)+
			   #<data>

			   are allowed for the effective address operand.


cpScc	: Set On Coprocessor Condition

	Operation : IF cpcc = TRUE
			THEN
			  1111...111 -> dst
			ELSE
			  0000...000 -> dst

	Assembler : cpScc <ea>

	Attributes: Size = Byte.

	Description	: Test the specified coprocessor condition. If
			  the condition is TRUE, set all bits of the
			  byte destination operand. If the condition
			  is FALSE, clear all bits of the byte desti-
			  nation operand.

	Condition Codes : NOT FFFECTED.

	Instruction Format :

		1 1 1 1 I I I 0 0 1 M M M R R R

		0 0 0 0 0 0 0 0 0 0 C C C C C C

		X X X X X X X X X X X X X X X X

	Instruction Fields :

		III	: Coprocessor ID field. Specifies the coprocesor
			  that is to process this operation. See cpBcc
			  above for current coprocessor IDs.

		MMM, RRR: See MC68020 Instruction Extension Words Above.
			  Used to specify an operand in main memory for
			  the coprocessor operation if specified, or
			  the CPU registers.

		CCC...	: Coprocessor Condition Field. Specifies the co-
			  processor condition to be tested.

		XXX...	: Optional Coprocessor Defined Extension Word(s).

	Addressing Modes : All EXECPT:

			   An
			   #<data>

			   are allowed for the effective address operand.


cpTRAPcc	: Trap On Coprocessor Condition.

	Operation : IF cpcc = TRUE
			THEN
			  TRAP (cpTRAP exception vector)
			ELSE
			  continue normal execution.

	Assembler : cpTRAPcc #<data>

	Attributes: Unsized or Size = Word.

	Description	: If the selected coprocessor condition is true,
			  then the CPU initiates exception processing.
			  The vector number is generated to reference the
			  TRAPV/TRAPcc exception vector, and the stacked
			  value of the program counter is the address of
			  the next instruction. If the selected condition
			  is false, then execution continues with the next
			  instruction. Following the condition word and
			  any coprocessor defined extension words is a
			  user-defined data operand specified as immediate
			  data, to be used by the trap handler.

	Condition Codes : NOT AFFECTED.

	Instuction Format :

		1 1 1 1 I I I 0 0 1 1 1 1 M M M

		0 0 0 0 0 0 0 0 0 0 C C C C C C

		X X X X X X X X X X X X X X X X

	Instruction Fields :

		III	: Coprocessor ID field. Specifies the coprocesor
			  that is to process this operation. See cpBcc
			  above for current coprocessor IDs.

		MMM	: Op-Mode field. Specifies the instruction form.

			  010 : Instruction is followed by one operand
				word.

			  011 : Instruction is followed by two operand
				words.

			  100 : Instruction has no operand words.

		CCC...	: Coprocessor Condition field. Specifies the co-
			  processor condition to be tested.

		XXX...	: Optional Coprocessor Defined Extension Word(s).

		If the Op-Mode field specifies one or two immediate data
		operand words, then the operand words follow the optional
		coprocessor defined extension words.


DIVSL	: Divide Signed Long.

	Operation : dst/src -> dst

	Assembler : DIVS.L <ea>,Dq	;32/32 -> 32r
		    DIVS.L <ea>,Dr:Dq	;64/32 -> 32r:32q
		    DIVSL.L <ea>,Dr:Dq	;32/32 -> 32r:32q

	Attributes: Size = Word, Long.

	Description	: Divide the destination operand by the source
			  operand, and store the result in the destina-
			  tion. The operation is performed using signed
			  arithmetic.

			  The first long form operates on a 32-bit divi-
			  dend (the destination) and a 32-bit divisor
			  (the source). The result is a 32-bit quotient
			  stored in the destination, and the remainder
			  is discarded.

			  The second long form operates on a 64-bit divi-
			  dend (the destination) and a 32-bit divisor (the
			  source). The result is a 32-bit quotient and a
			  32-bit remainder.

			  The third long form operates on a 32-bit divi-
			  dend (the destination) and a 32-bit divisor (the
			  source). The result is a 32-bit quotient and a
			  32-bit remainder.

			  Two special conditions may arise:

			  1) Division by zero : take the Zero Divide
			     exception.

			  2) Overflow detected & set before completion
			     of the instruction. If this occurs, then
			     the destination operand(s) are not affected.

	Condition Codes : X N Z V C
			  - * * * 0

			  N : Set if the quotient is negative. Undefined if
			      overflow or divide by zero.

			  Z : Set if the quotient is zero. Cleared otherwise.
			      Undefined if overflow or divide by zero.

			  V : Set if division overflow is detected. Cleared
			      otherwise.

			  C : Always Cleared.

			  X : Not Affected.

	Instruction Format :

		0 1 0 0 1 1 0 0 0 1 M M M R R R

		0 Q Q Q 1 Z 0 0 0 0 0 0 0 D D D

	Instruction Fields :

		MMM, RRR: See MC68020 Instruction Extension Words Above.

		QQQ	: Specifies the data register used to hold the
			  quotient.

		Z	: Size field. Selects a 32-bit or 64-bit dividend.

			  0 = 32-bit dividend in register Dq.

			  1 = 64-bit dividend in register Dr:Dq.

		DDD	: Specifies the data register used to hold the
			  remainder. If Dr = Dq, then only the quotient
			  is returned (1st long form). If the size
			  field is 1, this specifies the data register
			  containing the high 32 bits of the 64-bit divi-
			  dend.

	Addressing Modes : All EXCEPT An are allowed for the source
			   operand.


DIVUL	: Divide Unsigned Long.

	Operation : dst/src -> dst

	Assembler : DIVU.L <ea>,Dq	;32/32 -> 32r
		    DIVU.L <ea>,Dr:Dq	;64/32 -> 32r:32q
		    DIVUL.L <ea>,Dr:Dq	;32/32 -> 32r:32q

	Attributes: Size = Word, Long.

	Description	: Divide the destination operand by the source
			  operand, and store the result in the destina-
			  tion. The operation is performed using unsigned
			  arithmetic.

			  The first long form operates on a 32-bit divi-
			  dend (the destination) and a 32-bit divisor
			  (the source). The result is a 32-bit quotient
			  stored in the destination, and the remainder
			  is discarded.

			  The second long form operates on a 64-bit divi-
			  dend (the destination) and a 32-bit divisor (the
			  source). The result is a 32-bit quotient and a
			  32-bit remainder.

			  The third long form operates on a 32-bit divi-
			  dend (the destination) and a 32-bit divisor (the
			  source). The result is a 32-bit quotient and a
			  32-bit remainder.

			  Two special conditions may arise:

			  1) Division by zero : take the Zero Divide
			     exception.

			  2) Overflow detected & set before completion
			     of the instruction. If this occurs, then
			     the destination operand(s) are not affected.

	Condition Codes : X N Z V C
			  - * * * 0

			  N : Set if the quotient is negative. Undefined if
			      overflow or divide by zero.

			  Z : Set if the quotient is zero. Cleared otherwise.
			      Undefined if overflow or divide by zero.

			  V : Set if division overflow is detected. Cleared
			      otherwise.

			  C : Always Cleared.

			  X : Not Affected.

	Instruction Format :

		0 1 0 0 1 1 0 0 0 1 M M M R R R

		0 Q Q Q 0 Z 0 0 0 0 0 0 0 D D D

	Instruction Fields :

		MMM, RRR: See MC68020 Instruction Extension Words Above.

		QQQ	: Specifies the data register used to hold the
			  quotient.

		Z	: Size field. Selects a 32-bit or 64-bit dividend.

			  0 = 32-bit dividend in register Dq.

			  1 = 64-bit dividend in register Dr:Dq.

		DDD	: Specifies the data register used to hold the
			  remainder. If Dr = Dq, then only the quotient
			  is returned (1st long form). If the size
			  field is 1, this specifies the data register
			  containing the high 32 bits of the 64-bit divi-
			  dend.

	Addressing Modes : All EXCEPT An are allowed for the source
			   operand.


EXT	: Sign Extend (MC68020).

	Operation : dst (sign-extend) -> dst

	Assembler : EXT.W Dn	;extend byte to word
		    EXT.L Dn	;extend word to long
		    EXTB.L Dn	;extend byte to long

	Attributes: Size = Byte, Word, Long.

	Description	: Sign-extend the operand contained in the desti-
			  nation data register, according to the specified
			  size.

			  EXT.W copies bit 7 to bits [15:8] of the data
			  register. This instruction is available on all
			  MC680x0 CPUs.

			  EXT.L copies bit 15 to bits [31:16] of the data
			  register. This instruction is avaialble on all
			  MC680x0 CPUs.

			  EXTB.L copies bit 7 to bits [31:8] of the data
			  register. This instruction is avaialble on the
			  MC68020 onwards.

			  The instruction formats for EXT.W and EXT.L are
			  identical to the MC68000 EXT instruction. The
			  Op-Mode field provides for extensions to the
			  instruction set for higher processors such as
			  the MC68020.

	Condition Codes : X N Z V C
			  - * * 0 0

			  N : Set if the result is negative. Cleared
			      otherwise.

			  Z : Set if the result is zero. Cleared
			      otherwise.

			  V : Always Cleared.

			  C : Always Cleared.

			  X : Not Affected.

	Instruction Format :

		0 1 0 0 1 0 0 M M M 0 0 0 D D D

	Instruction Fields :

		MMM	: Op-Mode field. Specifies the size of the
			  sign-extension operation.

			  010 : sign-extend byte to word.

			  011 : sign-extend word to long.

			  111 : sign-extend byte to long.

		DDD	: Register field. Specifies which data register
			  to use.


MOVEC	: Move Control Register

	  (PRIVILEGED INSTRUCTION)

	Operation : IF supervisor state
			THEN
			  Rc -> Rn or Rn -> Rc
			ELSE
			  TRAP (Privilege Violation).

	Assembler : MOVEC Rc,Rn
		    MOVEC Rn,Rc

	Attributes: Size = Long.

	Description	: If the CPU is in supervisor mode, then copy the
			  contents of the specified control register to
			  the specified general register, or copy the con-
			  tents of the specified general register to the
			  specified control register. If the CPU is in
			  user mode, then take the Priivlege Violation ex-
			  ception.

			  The data transfer is ALWAYS a 32-bit transfer,
			  even though the register may be implemented with
			  fewer bits. Unimplemented bits are read as zeros
			  and ignored when written.

	Condition Codes : NOT AFFECTED.

	Instuction Format :

		0 1 0 0 1 1 1 0 0 1 1 1 1 0 1 D

		A R R R C C C C C C C C C C C C

	Instruction Fields :

		D	: Dr field. Specifies the direction of data
			  transfer.

			  0 = control register to general register.

			  1 = general register to control register.

		A	: A/D field. Specifies the type of general
			  register.

			  0 = Data Register.

			  1 = Address Register.

		RRR	: General Register field. Specifies which data
			  or address register is used.

		CCC...	: Control Register field. Specifies the control
			  register used. Values are:

			  $000	: Source Function Code (SFC) Register.
			  $001	: Destination Function Code (DFC)
				  Register.
			  $002	: Cache Control Register (CACR).
			  $800	: User Stack Pointer (USP).
			  $801	: Vector Base Register (VBR).
			  $802	: Cache Address Register (CAAR).
			  $803	: Master Stack Pointer (MSP).
			  $804	: Interrupt Stack Pointer (ISP).

			  All other codes cause an illegal instruction
			  exception.


MOVES	: Move Address Space

	  (PRIVILEGED INSTRUCTION)

	Operation : IF supervisor state
			THEN
			  Rn -> dst[DFC]
			  or
			  src[SFC] -> Rn
			ELSE
			  TRAP (Privilege Violation).

	Assembler : MOVES <ea>,Rn
		    MOVES Rn,<ea>

	Attributes: Size = Byte, Word, Long.

	Description	: Move the operand, using the specified size, from
			  the specified general register to a location wit-
			  hin the address space defined by the destination
			  function code (DFC) register. Or, move the oper-
			  and, using the specified size, from the location
			  within the address space defined by the source
			  function code (SFC) register to the specified
			  general register.

			  This transfer is ONLY performed if the CPU is in
			  supervisor mode. If the CPU is in user mode, then
			  the Privilege Violation exception is taken.

			  For suitable values of the SFC and DFC registers,
			  see MC68020 Extra Registers above.

	Condition Codes : NOT AFFECTED.

	Instruction Format :

		0 0 0 0 1 1 1 0 Z Z M M M R R R

		A D D D X 0 0 0 0 0 0 0 0 0 0 0

	Instruction Fields :

		ZZ	: Size field. Specifies the size of the operation.

			  00 = Byte Operation.
	
			  01 = Word Operation.

			  10 = Long Operation.

		MMM, RRR: See MC68020 Instruction Extension Words Above.

		A	: A/D field. Specifies whether the general register
			  is a data or address register. 0 = data register,
			  1 = address register.

		DDD	: Specifies which general register D0-D7 or A0-A7
			  is used.

		X	: Direction field. 0 = from <ea> to general regis-
			  ter, 1 = general register to <ea>.

	Addressing Modes : All EXCEPT Dn, An and #<data> are allowed for
			   the address operand in each case.

	Notes : MOVES.x An,(An)+ or MOVES.x An,-(An) where the same address
		register is used for both source and destination operands,
		is an undefined operation. The value stored in memory is
		undefined. On the MC68010 and MC68020 implementations, the
		value stored is the increment or decrement value of An. This
		implementation MAY NOT APPEAR on future devices.


MULS	: Multiply Signed (MC68020 Extended Version)

	Operation : dst * src -> dst

	Assembler : MULS.L <ea>,Dl	;32x32 -> 32
		    MULS.L <ea>,Dh:Dl	;32x32 -> 64

	Attributes: Size = Long.

	Description	: Multiply two operands using signed arithmetic,
			  and store the result in the specified destina-
			  tion.

			  In the first form, two 32-bit numbers are multi-
			  plied together, and a 32-bit result is stored in
			  the specified destination.

			  In the second form, two 32-bit numbers are multi-
			  plied together, these numbers being stored at the
			  source effective address and in the register des-
			  ignated Dl above. The result is stored as a 64-
			  bit value in Dh:Dl, Dh containing the high 32
			  bits, and Dl the low 32 bits of the result.

	Condition Codes : X N Z V C
			  - * * * 0

			  N : Set if the result is negative. Cleared
			      otherwise.

			  Z : Set if the result is zero. Cleared other-
			      wise.

			  V : Set if overflow detected. Cleared other-
			      wise.

			  C : Always Cleared.

			  X : Not Affected.

			  NOTE : Overflow (V=1) can ONLY occur with the
			  first form of the instruction. This occurs when
			  the high 32 bits of the result are NOT EQUAL to
			  the sign-extension of the low 32 bits.

	Instruction Format :

		0 1 0 0 1 1 0 0 0 0 M M M R R R

		0 L L L 1 Z 0 0 0 0 0 0 0 H H H


	Instruction Fields :

		MMM, RRR: See MC68020 Instruction Extension Words Above.
			  Define the addressing mode of the source oper-
			  and.

		LLL	: Register Dl field. Specifies which data register
			  is to be used as the Dl register in the above
			  specification.

		Z	: Size field. A 0 value indicates a 32-bit product,
			  a 1 value indicates a 64-bit product.

		HHH	: Register Dh field. Specifies which data register
			  is to be used as the Dh register in the above
			  specification. If Dh = Dl and Sz =1, then the
			  result of the operation are undefined. If Sz=0,
			  this field is unused (generally set to 0).


MULU: Multiply Unsigned (MC68020 Extended Version)

	Operation : dst * src -> dst

	Assembler : MULU.L <ea>,Dl	;32x32 -> 32
		    MULU.L <ea>,Dh:Dl	;32x32 -> 64

	Attributes: Size = Long.

	Description	: Multiply two operands using unsigned arithmetic,
			  and store the result in the specified destina-
			  tion.

			  In the first form, two 32-bit numbers are multi-
			  plied together, and a 32-bit result is stored in
			  the specified destination.

			  In the second form, two 32-bit numbers are multi-
			  plied together, these numbers being stored at the
			  source effective address and in the register des-
			  ignated Dl above. The result is stored as a 64-
			  bit value in Dh:Dl, Dh containing the high 32
			  bits, and Dl the low 32 bits of the result.

	Condition Codes : X N Z V C
			  - * * * 0

			  N : Set if the result is negative. Cleared
			      otherwise.

			  Z : Set if the result is zero. Cleared other-
			      wise.

			  V : Set if overflow detected. Cleared other-
			      wise.

			  C : Always Cleared.

			  X : Not Affected.

			  NOTE : Overflow (V=1) can ONLY occur with the
			  first form of the instruction. This occurs when
			  the high 32 bits of the result are NOT EQUAL to
			  the sign-extension of the low 32 bits.

	Instruction Format :

		0 1 0 0 1 1 0 0 0 0 M M M R R R

		0 L L L 0 Z 0 0 0 0 0 0 0 H H H


	Instruction Fields :

		MMM, RRR: See MC68020 Instruction Extension Words Above.
			  Define the addressing mode of the source oper-
			  and.

		LLL	: Register Dl field. Specifies which data register
			  is to be used as the Dl register in the above
			  specification.

		Z	: Size field. A 0 value indicates a 32-bit product,
			  a 1 value indicates a 64-bit product.

		HHH	: Register Dh field. Specifies which data register
			  is to be used as the Dh register in the above
			  specification. If Dh = Dl and Sz =1, then the
			  result of the operation are undefined. If Sz=0,
			  this field is unused (generally set to 0).


PACK	: Pack data into a single byte.

	Operation : src (unpacked BCD) + adjustment -> dst (packed BCD)

	Assembler : PACK -(Ax),-(Ay),#<adjustment>
		    PACK Dx,Dy,#<adjustment>

	Attributes: Unsized.

	Description	: The low four bits of two separate bytes are
			  adjusted and packed into a single byte.

			  When the source and destination operands are
			  data registers, the operation is performed as
			  follows:

			  src : xxxxabcdyyyyefgh +

			  adj : ....****....####

			  The highlighted bits (marked '*' and '#') are
			  then transferred to the destination as follows:

			  dst : ****####

			  When the source and destination operands are
			  predecrement operands, two bytes are fetched
			  from the source, concatenated to form a 16-
			  bit operand, and the adjustment added as above.
			  Then, the bits are transferred to the destina-
			  tion byte as above and the data pointers are
			  adjusted accordingly.

	Condition Codes : NOT AFFECTED.

	Instruction Format :

		1 0 0 0 Y Y Y 1 0 1 0 0 M X X X

		A A A A A A A A A A A A A A A A

	Instruction Fields :

		YYY	: Register Dy/Ay field:specifies the destina-
			  tion register used.

		XXX	: Register Dx/Ax field:specifies the source
			  register used.

		M	: Register/Memory Mode (R/M) field. Specifies
			  whether the addressing mode is data register
			  direct or predecrement.

			  0 : Instruction is PACK Dx,Dy

			  1 : Instruction is PACK -(Ax),-(Ay)

		AAA...	: Adjustment field. Contains the immediate data to
			  be added to the source operand. Appropriate con-
			  stants can be used to translate ASCII or EBCDIC
			  strings to packed BCD.

	Example : PACK D1,D0,#0

		  Before : D0 = $0000,

			   D1 = $3231 (= ASCII string "21").

			   Split word into bytes = $32, $31

			   Zero out upper nibbles = $02, $01

			   Concatenate these bytes to a word = $0201

			   Add adjustment : $0201 + $0000 = $0201

			   Now pack nibbles $2, $1 into a byte = $21

		  After  : D0 = $0021.


RTD	: Return And Deallocate Parameters

	Operation : (SP) -> PC
		    SP + d -> SP

	Assembler : RTD #<displacement>

	Attributes: Unsized.

	Description	: The program counter is pulled from the stack.
			  The previous value of the program counter is
			  lost. Then, the 16-bit displacement value is
			  sign-extended to 32 bits and added to the
			  stack pointer.

	Condition Codes : NOT AFFECTED.

	Instruction Format :

		0 1 0 0 1 1 1 0 0 1 1 1 0 1 0 0

		D D D D D D D D D D D D D D D D

	Instruction Fields :

		DDD...	: Displacement field. Specifies the 16-bit
			  displacement to sign-extend and add to the
			  stack pointer after pulling the program
			  counter from the stack.


RTE	: Return From Exception (MC68020)

	  (PRIVILEGED INSTRUCTION).

	Operation : IF supervisor state
			THEN
			  (SP) -> SR
			  SP + 2 -> SP
			  (SP) -> PC
			  SP + 4 -> SP
			  (SP) -> Internal Format Word register
			  Interpret format word and pull stack
			  frame off stack, restore state
			ELSE
			  TRAP (Privilege Violation)

	Assembler : RTE

	Attributes: Unsized.

	Description	: If the CPU is in the supervisor state, then
			  pull the status register from the stack,
			  followed by the program counter. Then pull
			  the stack frame format word from the stack,
			  and examine the format field to determine
			  if any extra words are to be pulled from
			  the stack, and how many. If extra words are
			  to be pulled from the stack, pull them and
			  restore to internal registers if needed.

			  If the CPU is in the user state, then the
			  CPU takes the Privilege Violation excep-
			  tion.

	Condition Codes : ALL AFFECTED ACCORDING TO THE WORD PULLED FROM
			  THE STACK.

	Instruction Format :

		0 1 0 0 1 1 1 0 0 1 1 1 0 0 1 1

	Stack Frame Format Word Format (pulled off the stack by the
	RTE instruction) :

		F F F F 0 0 V V V V V V V V V V

	Stack Frame Format Word Fields :
			  
		FFFF	: Format field. Specifies the format of the
			  stack frame to be pulled from the stack.
			  Values interpreted are:

			  0000	: Short Format. Only four words are
				  removed from the stack (SR, PC and
				  this format word).

			  0001	: Throwaway Format. Four words are
				  removed from the currently active
				  stack, and SR only is updated from
				  this stack frame. Then, the CPU
				  begins executing the RTE from the
				  top of the active stack AFTER pul-
				  ling SR. This format is used to
				  mark the bottom of the Interrupt
				  Stack, and when the CPU is using
				  the Master Stack for exception
				  processing.

			  0010	: Instruction Error format. Six words
				  are pulled from the top of the stack.
				  The first four words are as for the
				  short format:the remaining two words
				  are discarded.

			  1000	: MC68010 Long Format. The MC68020 takes
				  a Format Error exception.

			  1001	: Coprocessor Mid-Instruction Format. 10
				  words are removed from the stack. Re-
				  sumes coprocessor instruction execution.

			  1010	: MC68020 Short Format. 16 words are re-
				  moved from the stack. Resumes instruc-
				  tion execution.

			  1011	: MC68020 Long Format. 46 words are re-
				  moved from the stack. Resumes instruc-
				  tion execution.

			  Any other values:the CPU takes a Format Error
			  exception.

		VVV...	: Vector Offset field. This field contains the
			  exception number that was generated.


RTM	: Return From Module

	Operation : Reload saved module state from stack.

	Assembler : RTM Rn

	Attributes: Unsized.

	Description	: A previously saved module state (as saved by
			  the CALLM instruction) is reloaded from the
			  top of the stack. After the module state is
			  retrieved from the top of the stack, the
			  caller's stack pointer is incremented by the
			  argument count value in the module state.

			  Like CALLM above, this instruction requires
			  external hardware support, usually from the
			  MC68851 Paged Memory Management Unit (PMMU)
			  but also from other sources.

	Condition Codes : ALL AFFECTED ACCORDING TO THE CONTENT OF THE
			  WORD ON THE STACK.

	Instruction Format :

		0 0 0 0 0 1 1 0 1 1 0 0 A R R R

	Instruction Fields :

		A	: D/A field. Specifies whether the module data
			  pointer is a data or an address register.

			  0 = Data Register.

			  1 = Address Register.

		RRR	: Register Field. Specifies the register number
			  for the module data pointer which is to be
			  restored from the saved module state. If the
			  register specified is A7 (SP), the updated
			  value of the register reflects the stack poin-
			  ter operations, and the saved module data area
			  pointer is lost.


TRAP	: TRAP Instruction (MC68020)

	Operation : SSP - 2 -> SSP
		    Format/Offset -> (SSP)
		    SSP - 4 -> SSP
		    PC -> (SSP)
		    SSP - 2 -> SSP
		    SR -> (SSP)
		    TRAP Vector Address -> PC

	Assembler : TRAP #<vector>

	Attributes: Unsized.

	Description	: The processor initiates exception processing.
			  The vector number is generated to reference
			  the TRAP instruction vector specified by the
			  low order four bits of the instruction.

			  Sixteen TRAP instruction vectors (0-15) are
			  available.

	Condition Codes : NOT AFFECTED.

	Instruction Format :

		0 1 0 0 1 1 1 0 0 1 0 0 V V V V

	Instruction Fields :

		VVVV	: Vector Field. Specifies which TRAP vector
			  contains the new value of the program coun-
			  ter to be loaded.



TRAPcc	: Trap On Condition

	Operation : IF condition = TRUE
			THEN
			  TRAP (TRAPV/TRAPcc Vector)
			ELSE
			  continue normal execution

	Assembler : TRAPcc
		    TRAPcc.W #<data>
		    TRAPcc.L #<data)

	Attributes: Unsized or Size = Word, Long.

	Description	: If the condition specified in the instruction is
			  true, then the CPU initiates exception processing.
			  The vector number is generated to reference the
			  TRAPcc exception vector. The stacked program val-
			  ue points to the next instruction after the TRAPcc.
			  If the condition specified is false, then no oper-
			  ation occurs, and execution continues at the ins-
			  truction immediately following the TRAPcc.

			  If an immediate data operand is specified, then
			  the word (or words) containing that data follow
			  the TRAPcc instruction immedaitely, and this data
			  is available to the programmer as a user-definable
			  data field for use within the trap handler. For a
			  full list of CPU conditions see typed_68000.doc.

	Condition Codes : NOT AFFECTED.

	Instruction Format :

		0 1 0 1 C C C C 1 1 1 1 1 M M M

		W W W W W W W W W W W W W W W W

		L L L L L L L L L L L L L L L L

	Instruction Fields :

		CCCC	: Condition Code field. Selects one of the 16
			  possible conditions for the TRAPcc instruc-
			  tion. For a full list of conditions see the
			  companion file typed_68000.doc.

		MMM	: Op-Mode field. Selects the instruction form.

			  010 : Instruction is followed by one operand
				word.

			  011 : Instruction is followed by two operand
				words.

			  100 : Instruction has no following operand
				words.


UNPK	: Unpack BCD

	Operation : src (Packed BCD) + adjustment -> dst (Unpacked BCD)

	Assembler : UNPK -(Ax),-(Ay),#<adjustment>
		    UNPK Dx,Dy,#<adjustment>

	Attributes: Unsized.

	Description	: In the unpack operation, the byte operand is
			  split into its two component nibbles, and each
			  nibble is then zero-extended to a byte value.
			  These new byte values are concatenated into a
			  single 16-bit value. Then, the value of the ad-
			  justment is added to this 16-bit value, and the
			  two resulting bytes moved to the destination.

			  If the destination is a data register, then the
			  result is moved as a single 16-bit word to the
			  data register.

	Condition Codes : NOT AFFECTED.

	Instruction Format :

		1 0 0 0 Y Y Y 1 1 0 0 0 M X X X

		A A A A A A A A A A A A A A A A

	Instruction Fields :

		YYY	: Register Dy/Ay field:specifies the destina-
			  tion register used.

		XXX	: Register Dx/Ax field:specifies the source
			  register used.

		M	: Register/Memory Mode (R/M) field. Specifies
			  whether the addressing mode is data register
			  direct or predecrement.

			  0 : Instruction is UNPK Dx,Dy

			  1 : Instruction is UNPK -(Ax),-(Ay)

		AAA...	: Adjustment field. Contains the immediate data to
			  be added to the source operand. Appropriate con-
			  stants can be used to translate packed BCD to
			  ASCII or EBCDIC strings.

	Example : UNPK D1,D0,#$3030

		  Before : D1 = $0021 (BCD 21)

			   Unpack nibbles into bytes = $02, 01

			   Concatenate bytes to word = $0201

			   $0201 + $3030 = $3231

		  After  : D0 = $3132 (ASCII "21")