TABLE OF CONTENTS
                        --------------------------

            Specification for the ADVANCED AMIGA CHIP SET (AGA)

                 1.  Summary of New features for AGA
                 2.  Explanation of New Features
                 3.  List of Registers ordered by Address
                 4.  List of Registers ordered Alphabetically
                 5.  New List of Display Modes


-----------------------------------------------------------------------------



                    1. Summary of new features for AGA
                    ----------------------------------


o	32 bit wide data bus supports input of 32-bit wide bitplane data
	and allows doubling of memory bandwidth. Additional doubling of 
	bandwidth can be achieved by using FAST page mode Ram. The same 
	bandwidth enhancements are available for sprites. Also the maximum
	number of bitplanes useable in all modes was increased to eight (8).

o	The color Palette has been expanded to 256 colors deep and 25 bits
	wide (8 RED,8 GREEN,8 BLUE,1 GENLOCK). This permits display of 256
	simultaneouscolors in all resolutions. A palette of 16,777,216 
	colors are available in all resolutions.

o	28Mhz clock input allows for cleaner definition of HIRES and SHRES
	pixels ALICE`S clock genarator is synchronized by means of LISA`s
	14MHz and SCLK outputs, Genlock XCLK and XCLKEN pins have been
	eliminated (external MUX is now required).

o	A new register bit allows sprites to appear in the screen border
	regions (BRDRSPRT).

o	A bitplane mask field of 8 bits allows an address offset into the
	color palette. Two 4-bit mask fields do the same for odd and even
	sprites. In Dual Playfield modes,2 4-bitplane playfields are now
	possible in all resolutions.

o	Two Extra high-order playfield scrollbits allow seamless scrolling
	of up to 64 bit wide bitplanes in all resolutions. Resolution of
	bitplane scroll, display window,and horizontal sprite position has
	been improved to 35ns in all resolutions.

o	A new 8 bitplane HAM mode has been created, 6 for colors and 2 for
	control bits. All HAM modes are available in all resolutions (not
	just LORES as before).

o	A RST_input pin has been added, which resets all the bits contained
	in registers that were new for ECS or LISA: BPLCON3,BPLCON4,CLXCON2,
	DIWHIGH,FMODE.

o	Sprite resolution can be set to LORES,HIRES,SHRES,independant of
	bitplane resolution.

o	Attached Sprites are now available in all resolutions.

o	Hardware Scan Doubling support has been added for bitplanes and
	sprites. This is intended to allow 15KHz screens to be intelligentely
	displayed on a 31KHz monitor and share the display with 31KHz screens.








-----------------------------------------------------------------------------



                      2. Explanation of New Features
                      ------------------------------


                                Bitplanes:
                                ----------

There are now 8 bitplanes instead of 6. In single playfield modes they can
address 256 colors instead of 64. As long as the memory architecture can
support the bandwidth, all 8 bitplanes are available in all 3 resolutions
In the same vein, 4+4 bitplane dualplayfield is available in all 3
resolutions, unless bitplane scan-doubling is enabled, In which case both 
playfields share the same bitplane modulus register.

Bits 15 through 8 of BPLCON14 comprise an 8 bit mask for the 8 bitplane
address, XOR`ing the individual bits. This allows the copper to exchange
color maps with a single instruction. BPLCON1 now contains an 8 bit scroll
value for each of the playfields. Granularity of scroll now extends down to
35n Sec. (1 SHRES pixel), and scroll can delay playfield through 32 bus
cycles. Bits BPAGEM and BPL32 in new register FMODE control size of bitplane
data in BPL1DAT thru BPL8DAT.

The old 6 bitplane HAM mode, unlike before, works in HIRES and SHRES
resolutions.

       As before bitplanes 5 and 6 control it`s function as follows:

		+--------------------------------------------+
		|BP6|BP5|   RED  |  GREEN | BLUE             |
		|--------------------------------------------|
		| 0 | 0 | select new base register (1 of 16) |
		|--------------------------------------------|
		| 0 | 1 |  hold  |  hold  | modify           |
		|--------------------------------------------|
		| 1 | 0 | modify |  hold  |  hold            |
		|--------------------------------------------|
		| 1 | 1 |  hold  | modify |  hold            |
		+--------------------------------------------+

There is a new 8 bitplane HAM (Hold and Modify) mode. This mode is invoked
when BPU field in BPLCON0 is set to 8 , and HAMEN is set. Bitplanes 1 and 2
are used as control bits analagous to the function of bitplanes 5 and 6 in
6 bitplane HAM mode:

		+--------------------------------------------+
		|BP2|BP1|   RED  |  GREEN | BLUE             |
		|--------------------------------------------|
		| 0 | 1 | select new base register (1 of 64) |
		|--------------------------------------------|
		| 0 | 1 |  hold  |  hold  | modify           |
		|--------------------------------------------|
		| 1 | 0 | modify |  hold  |  hold            |
		|--------------------------------------------|
		| 1 | 1 |  hold  | modify |  hold            |
		+--------------------------------------------+

Since only 6 bitplanes are available for modify data, the data is placed in
6 MSB. The 2 LSB are left unmodified, which allows creation of all
16,777,216 colors simultaneously, assuming one had a large enough screen
and picked one`s base registers judiciously. This HAM mode also works in
HIRES and SHRES modes.

For compatibility reasons EHB mode remains intact. Its existence is rather
moot in that we have more than enough colors in the color table to replace
its functionality. As before, EHB is invoked whenever SHRES = HIRES =
HAMEN= DPF = 0 and BPU = 6. Please note that starting with ECS DENISE
there is a bit in BPLCON2 which disables this mode (KILLEHB).

Bits PF2OF2,1,0 in BPLCON3 determine second playfield`s offset into the
color table. This is now necessary since playfields in DPF mode can have up
to 4 bitplanes. Offset value are as defined in register map.

BSCAN2 bit in FMODE enables bitplane scan-doubling. When V0 bit of DIWSTRT
matches V0 of vertical beam counter, BPL1MOD contains the modulus for the
display line, else BPL2MODis used. When scan-doubled both odd and even 
bitplanes use the same modulus on a given line, whereas in normal mode odd
bitplanes used BPL1MOD and even bitplanes used BPL2MOD. As a result Dual
Playfields screens will probably not display correctly when scan-doubled.





                                 Sprites:
                                 --------


Bits SPAGEM and SPR32 in FMODE whether size of sprite load data in
SPR0DATA(B) thru SPR7DATA(B) is 16,32, or 64 bits, analagous to bitplanes.
BPLCON3 contains several bits relating to sprite behavior. SPRES1 and SPRES0
control sprite resolution, whether they conform to theECS standard or 
override tp LORES,HIRES,or SHRES. BRDRSPRT, when high,allows sprites to be
visible in border areas. ESPRM7 thru ESPRM4 allow relocation of the even
sprite color map. OSPRM7 thru OSPRN4 allow relocation of the odd sprite color
map. In the case of attached sprites OSPRM bits are used.

SSCAN2 bit in FMODE enables sprite scan-doubling. When enabled, individual
SH10 bits in SPRxPOS registers control whether or not a given sprite is to
be scan-doubled. When V0 bit of SPRxPOS register matches V0 bit of vertical
beam counter, the given sprite`s DMA is allowed to proceed as before. If
the don`t match, then sprite DMA is disabled and LISA reuses the sprite data
from the previous line. When sprites are scan-doubled, only the position and
control registers need be modified by the programmer; the data registers need
no modification.

NOTE: Sprite vertical start and stop positions must be of the same parity,
i.e. both odd or even.




                              Compatibility:
                              --------------


RST_pin resets all bits in all registers new to AA. These registers include:
BPLCON3,BPLCON4,CLXCON2,DIWHIGH,FMODE.

ECSENA bit (formerly ENBPLCN3) is used to disable those register bits in
BPLCON3 that are never accessed by old copper lists, and in addition are
required by old style copper lists to be in their default
settings.Specifically ECSENA forces the following bits to their default low
settings: BRDRBLNK,BRDNTRAN,ZDCLKEN,EXTBLKEN, and BRDRSPRT.

CLXCON2 is reset by a write to CLXCON, so that old game programs will be
able to correctly detect collisions.

DIWHIGH is reset by writes to DIWSTRT or DIWSTOP. This is interlock is
inhertied from ECS Denise.



                                 Genlock:
                                 --------

Lots of new genlock features were added to ECS DENISE and are carried over
to LISA. ZDBPEN in BPLCON2 allows any bitplane, selected by ZDBPSEL2,1,0,to
be used as a transparency mask (ZD pin mirrors contents of selected
bitplane). ZDCTEN disables the old COLOR00 is transparent mode, and allows
the bit31 position of each color in the color table to control
transparency. ZDCLKEN generates a 14MHz clock synchronized with the video
data that can be used by video post-processors. Finally, BRDNTRAN in
BPLCON3 generates an opaque border region which can be used to frame live
video.


                            Color Lookup Table:
                            -------------------

The color table has grown from 32 13-bit registers to 256 25-bit registers.
Several new register bits have been added to BPLCON3 to facilitate loading
the table with only 32 register addresses. LOCT, selects either the 16 MSB
or LSB for loading. Loading the MSB always loads the LSB as well for
compatibility, so when 24 bit colors are desired load LSB after MSB.
BANK2,1,0 of 8 32 address banks for loading as follows:

                BANK2 | BANK1 | BANK0 | COLOR ADDRESS RANGE
               --------------------------------------------
                 0   |   0   |   0   |  COLOR00 - COLOR1F 
                 0   |   0   |   1   |  COLOR20 - COLOR3F 
                 0   |   1   |   0   |  COLOR40 - COLOR5F 
                 0   |   1   |   1   |  COLOR60 - COLOR7F 
                 1   |   0   |   0   |  COLOR80 - COLOR9F 
                 1   |   0   |   1   |  COLORA0 - COLORBF 
                 1   |   1   |   0   |  COLORC0 - COLORDF 
                 1   |   1   |   1   |  COLORE0 - COLORFF 


RDRAM bit in BPLCON2 causes LISA to interpret all color table accesses as
reads.

Note: There is no longer any need to "scramble" SHRES color table entries. 
This artifice is no longer required and people who bypass ECS graphics
library calls to do their own 28MHz graphics are to be pointed at and
publicly humiliated.


                                 Collision:
                                 ----------

A new register CLXCON2 contains 4 new bits. ENBP7 and ENBP6 are the enable
bits for bitplanes 7 and 8, respectively. Similarly, MVBP7 and MPBP8 are
their match value bits. CLXDAT is unchanged.


                          Horizontal Comparators:
                          -----------------------

All programmable comparators with the exception of VHPOSW have 35nSec
resolution.: DIWHIGH,HBSTOP,SPRCTL,BPLCON1. BPLCON1 has additional
high-order bits as well. Note that horizontal bit position representing
140nSec resolution has been changed to 3rd least significant bit,where
before it used to be a field`s LSB, For example, bit 00 in BPLCON1 used to
be named PF1H0 and now it`s called PF1H2.


                        Coercion of 15KHz to 31KHz:
                        ---------------------------

We have added new hardware features to LISA to aid in properly displaying
15KHz and 31KHz viewports together on the same 31KHz display. LISA can
globally set sprite resolution to LORES,HIRES, or SHRES.
LISA will ignore SH10 compare bits in SPRxPOS when scan-doubling, thereby
allowing ALICE to use these bits individually set scan-doubling.





-----------------------------------------------------------------------------





                  3. List of Registers Ordered by Address
                  ---------------------------------------


                               Symbols Used:
			       -------------


&	 = Register used by DMA channel only.
%	 = Register used by DMA channel usually, processors sometimes.
+	 = Address register pair. Low word uses DB1-DB15, High word DB0-DB4.
~	 = Address not writable by the copper unless COPCON bit 1 is set true
h	 = New for HiRes chip set.
p	 = New for AGA chip set.
A	 = Agnus/Alice chip set.
D	 = Denise/Lisa chip set.
P	 = Paula chip.
W	 = Write.
R	 = Read.

ER	 = Early read. This is a DMA transfer to RAM, from either the disk or
	   from the blitter. Ram timing requires data to be on the bus earlier
	   than microprocessor read cycles. These transfers are therefore
           initiated by Agnus timing, rather than a read address on the register
	   address bus (RGA)

S	 = Strobe (Write address with no register bits).

PTL,PTH  = 20 bit pointer that addresses DMA data. Must be reloaded by a
	   processor before use (Vertical blank for bit plane and sprite
	   pointers and prior to starting the blitter for blitter pointers).
	   (Old chips - 18 bits).

LCL,LCH  = 20 bit location (starting address) of DMAdata. Used to
           automatically restart pointers. such as the Coprocessor program
	   counter (during vertical blank), and the audio sample counter
           (whenever the audio length count is finished),
	   (Old chips - 18 bits).

MOD	 = 15 bit Modulo. A number that is automatically added to the memory
	   address at the end of each line to generate the address for the
	   beginning of the next line. This allows the blitter (or the display
	   window) to operate on (or display) a window of data that is smaller
	   than the actual picture in memory. (memory map) Uses 15 bits, plus
    	   sign extended.




Name        Addr  R/W Chip(s) Function
---------------------------------------------------------------------------
BPTDDAT   & ~000  ER A  -  -  Blitter dest. early read (dummy address)
DMACONR   - ~002  R  A  -  P  DMA Control (and blitter status) read
VPOSR     - ~004  R  A  -  -  Read vert most sig. bits (and frame flop)
VHPOSR    - ~006  R  A  -  -  Read vert and horiz position of beam
DSKDATR   & ~008  ER -  -  P  Disk data early read (dummy address)
JOY0DAT   - ~00A  R  -  D  -  Joystick-mouse 0 data (vert,horiz)
JOT1DAT   - ~00C  R  -  D  -  Joystick-mouse 1 data (vert,horiz)
CLXDAT    - ~00E  R  -  D  -  Collision data reg. (read and clear)
ADKCONR   - ~010  R  -  -  P  Audio,disk control register read
POT0DAT   - ~012  R  -  -  P  Pot counter pair 0 data (vert,horiz)
POT1DAT   - ~014  R  -  -  P  Pot counter pair 1 data (vert,horiz)
POTINP    - ~016  R  -  -  P  Pot pin data read
SERDATR   - ~018  R  -  -  P  Serial port data and status read
DSKBYTR   - ~01A  R  -  -  P  Disk data byte and status read
INTENAR   - ~01C  R  -  -  P  Interrupt enable bits read
INTREQR   - ~01E  R  -  -  P  Interrupt request bits read
DSKPTH    + ~020  W  A  -  -  Disk pointer (high 5 bits)
DSKPTL    + ~022  W  A  -  -  Disk pointer (low 15 bits)
DSKLEN    - ~024  W  -  -  P  Disk length
DSKDAT    & ~026  W  -  -  P  Disk DMA data write
REFPTR    & ~028  W  A  -  -  Refresh pointer
VPOSW     - ~02A  W  A  -  -  Write vert most sig. bits(and frame flop)
VHPOSW    - ~02C  W  A  D  -  Write vert and horiz pos of beam
COPCON    - ~02E  W  A  -  -  Coprocessor control reg (CDANG)
SERDAT    - ~030  W  -  -  P  Serial port data and stop bits write
SERPER    - ~032  W  -  -  P  Serial port period and control
POTGO     - ~034  W  -  -  P  Pot count start,pot pin drive enable data
JOYTEST   - ~036  W  -  D  -  Write to all 4 joystick-mouse counters at once
STREQU    & ~038  S  -  D  -  Strobe for horiz sync with VB and EQU
STRVBL    & ~03A  S  -  D  -  Strobe for horiz sync with VB (vert blank)
STRHOR    & ~03C  S  -  D  P  Strobe for horiz sync
STRLONG   & ~03E  S  -  D  -  Strobe for identification of long horiz line
BPLCON0   - ~040  W  A  -  -  Blitter control reg 0
BPLCON1   - ~042  W  A  -  -  Blitter control reg 1
BLTAFWM   - ~044  W  A  -  -  Blitter first word mask for source A
BLTALWM   - ~046  W  A  -  -  Blitter last word mask for source A
BLTCPTH   + ~048  W  A  -  -  Blitter pointer to source C (high 5 bits)
BLTCPTL   + ~04A  W  A  -  -  Blitter pointer to source C (low 15 bits)
BLTBPTH   + ~04C  W  A  -  -  Blitter pointer to source B (high 5 bits)
BLTBPTL   + ~04E  W  A  -  -  Blitter pointer to source B (low 15 bits)
BLTAPTH   + ~050  W  A  -  -  Blitter pointer to source A (high 5 bits)
BLTAPTL   + ~052  W  A  -  -  Blitter pointer to source A (low 15 bits)
BPTDPTH   + ~054  W  A  -  -  Blitter pointer to destn  D (high 5 bits)
BLTDPTL   + ~056  W  A  -  -  Blitter pointer to destn  D (low 15 bits)
BLTSIZE   - ~058  W  A  -  -  Blitter start and size (win/width,height)
BPTCONOL  h ~05A  W  A  -  -  Blitter control 0 lower 8 bits (minterms)
BLTSIZV   h ~05C  W  A  -  -  Blitter V size (for 15 bit vert size)
BLTSIZH   h ~05E  W  A  -  -  Blitter H size & start (for 11 bit H size)
BLTCMOD   - ~060  W  A  -  -  Blitter modulo for source C
BLTBMOD   - ~062  W  A  -  -  Blitter modulo for source B
BLTAMOD   - ~064  W  A  -  -  Blitter modulo for source A
BLTDMOD   - ~066  W  A  -  -  Blitter modulo for destn  D
RESERVED  - ~068  -  -	-  -  Reserved for future
RESERVED  - ~06A  -  -  -  -  Reserved for future
RESERVED  - ~06C  -  -	-  -  Reserved for future
RESERVED  - ~06E  -  -	-  -  Reserved for future
BLTCDAT   & ~070  W  A  -  -  Blitter source C data reg
BLTBDAT   & ~072  W  A  -  -  Blitter source B data reg
BLTADAT   & ~074  W  A  -  -  Blitter source A data reg
RESERVED  - ~076  -  -  -  -  Reserved for future
SPRHDAT   &h 078  W  A  -  -  Ext logic UHRES sprite ptr & data identifier
BPLHDAT   - ~07A  ?  ?  -  -  Function Undefined
LISAID    h ~07C  R  -  D  -  Chip revision level for Denise/Lisa
DSKSYNC   - ~07E  W  -  -  P  Disk sync pattern reg for disk read
COP1LCH   +  080  W  A  -  -  Coprocessor first location reg (high 5 bits)
COP1LCL   +  082  W  A  -  -  Coprocessor first location reg (low 15 bits)
COP2LCH   +  084  W  A  -  -  Coprocessor second reg (high 5 bits)
COP2LCL   +  086  W  A  -  -  Coprocessor second reg (low 15 bits)
COPJMP1   -  088  S  A  -  -  Coprocessor restart at first location
COPJMP2   -  08A  S  A  -  -  Coprocessor restart at second location
COPINS    -  08C  W  A  -  -  Coprocessor inst fetch identify
DIWSTRT   -  08E  W  A  D  -  Display wins tart  (upper left vert-hor pos)
DIWSTOP   -  090  W  A  D  -  Display win stop (lower right vert-hor pos)
DDFSTRT   -  092  W  A  -  -  Display bit plane data fetch start.hor pos
DDFSTOP   -  094  W  A  -  -  Display bit plane data fetch stop.hor pos
DMACON    -  096  W  A  -  P  DMA control write (clear or set)
CLXCON    -  098  W  -  D  -  Collision control
INTENA    -  09A  W  -  -  P  Interrupt enable bits (clear or set bits)
INTREQ    -  09C  W  -  -  P  Interrupt request bits (clear or set bits)
ADKCON    -  09E  W  -  -  P  Audio,disk,UART,control
AUD0LCH   +  0A0  W  A  -  -  Audio channel 0 location (high 5 bits)
AUD0LCL   +  0A2  W  A  -  -  Audio channel 0 location (low 15 bits)
AUD0LEN   -  0A4  W  -  -  P  Audio channel 0 length
AUD0PER   -  0A6  W  -  -  P  Audio channel 0 period
AUD0VOL   -  0A8  W  -  -  P  Audio channel 0 volume
AUD0DAT   &  0AA  W  -  -  P  Audio channel 0 data
RESERVED  -  0AC  -  -  -  -  Reserved for future
RESERVED  -  0AE  -  -  -  -  Reserved for future
AUD1LCH   +  0B0  W  A  -  -  Audio channel 1 location (high 5 bits)
AUD1LCL   +  0B2  W  A  -  -  Audio channel 1 location (low 15 bits)
AUD1LEN   -  0B4  W  -  -  P  Audio channel 1 length
AUD1PER   -  0B6  W  -  -  P  Audio channel 1 period
AUD1VOL   -  0B8  W  -  -  P  Audio channel 1 volume
AUD1DAT   &  0BA  W  -  -  P  Audio channel 1 data
RESERVED  -  0BC  -  -  -  -  Reserved for future
RESERVED  -  0BE  -  -  -  -  Reserved for future
AUD2LCH   +  0C0  W  A  -  -  Audio channel 2 location (high 5 bits)
AUD2LCL   +  0C2  W  A  -  -  Audio channel 2 location (low 15 bits)
AUD2LEN   -  0C4  W  -  -  P  Audio channel 2 length
AUD2PER   -  0C6  W  -  -  P  Audio channel 2 period
AUD2VOL   -  0C8  W  -  -  P  Audio channel 2 volume
AUD2DAT   &  0CA  W  -  -  P  Audio channel 2 data
RESERVED  -  0CC  -  -  -  -  Reserved for future
RESERVED  -  0CE  -  -	-  -  Reserved for future
AUD3LCH   +  0D0  W  A  -  -  Audio channel 3 location (high 5 bits)
AUD3LCL   +  0D2  W  A  -  -  Audio channel 3 location (low 15 bits)
AUD3LEN   -  0D4  W  -  -  P  Audio channel 3 length
AUD3PER   -  0D6  W  -  -  P  Audio channel 3 period
AUD3VOL   -  0D8  W  -  -  P  Audio channel 3 volume
AUD3DAT   &  0DA  W  -  -  P  Audio channel 3 data
RESERVED  -  0DC  -  -	-  -  Reserved for future
RESERVED  -  0DE  -  -	-  -  Reserved for future
BPL1PTH   +  0E0  W  A  -  -  Bit plane pointer 1 (high 5 bits)
BPL1PTL   +  0E2  W  A  -  -  Bit plane pointer 1 (low 15 bits)
BPL2PTH   +  0E4  W  A  -  -  Bit plane pointer 2 (high 5 bits)
BPL2PTL   +  0E6  W  A  -  -  Bit plane pointer 2 (low 15 bits)
BPL3PTH   +  0E8  W  A  -  -  Bit plane pointer 3 (high 5 bits)
BPL3PTL   +  0EA  W  A  -  -  Bit plane pointer 3 (low 15 bits)
BPL4PTH   +  0EC  W  A  -  -  Bit plane pointer 4 (high 5 bits)
BPL4PTL   +  0EE  W  A  -  -  Bit plane pointer 4 (low 15 bits)
BPL5PTH   +  0F0  W  A  -  -  Bit plane pointer 5 (high 5 bits)
BPL5PTL   +  0F2  W  A  -  -  Bit plane pointer 5 (low 15 bits)
BPL6PTH   +  0F4  W  A  -  -  Bit plane pointer 6 (high 5 bits)
BPL6PTL   +  0F6  W  A  -  -  Bit plane pointer 6 (low 15 bits)
BPL7PTH   +  0F8  W  A  -  -  Bit plane pointer 7 (high 5 bits)
BPL7PTL   +  0FA  W  A  -  -  Bit plane pointer 7 (low 15 bits)
BPL8PTH   +  0FC  W  A  -  -  Bit plane pointer 8 (high 5 bits)
BPL8PTL   +  0FE  W  A  -  -  Bit plane pointer 8 (low 15 bits)
BPLCON0   -  100  W  A  D  -  Bit plane control reg (misc control bits)
BPLCON1   -  102  W  -  D  -  Bit plane control reg (scroll val PF1,PF2)
BPLCON2   -  104  W  -  D  -  Bit plane control reg (priority control)
BPLCON3   -  106  W  -  D  -  Bit plane control reg (enhanced features)
BPL1MOD   -  108  W  A  -  -  Bit plane modulo (odd planes,or active fetch lines if bitplane scan-doubling is enabled)
BPL2MOD   -  10A  W  A  -  -  Bit plane modulo (even planes or inactive fetch lines if bitplane scan-doubling is enabled)
BPLCON4   p  10C  W  -  D  -  Bit plane control reg (bitplane and sprite masks)
CLXCON2   p  10E  W  -  D  -  Extended collision control reg
BPL1DAT   &  110  W  -  D  -  Bit plane 1 data (parallel to serial convert)
BPL2DAT   &  112  W  -  D  -  Bit plane 2 data (parallel to serial convert)
BPL3DAT   &  114  W  -  D  -  Bit plane 3 data (parallel to serial convert)
BPL4DAT   &  116  W  -  D  -  Bit plane 4 data (parallel to serial convert)
BPL5DAT   &  118  W  -  D  -  Bit plane 5 data (parallel to serial convert)
BPL6DAT   &  11A  W  -  D  -  Bit plane 6 data (parallel to serial convert)
BPL7DAT   &p 11C  W  -  D  -  Bit plane 7 data (parallel to serial convert)
BPL8DAT   &p 11E  W  -  D  -  Bit plane 8 data (parallel to serial convert)
SPR0PTH   +  120  W  A  -  -  Sprite 0 pointer (high 5 bits)
SPR0PTL   +  122  W  A  -  -  Sprite 0 pointer (low 15 bits)
SPR1PTH   +  124  W  A  -  -  Sprite 1 pointer (high 5 bits)
SPR1PTL   +  126  W  A  -  -  Sprite 1 pointer (low 15 bits)
SPR2PTH   +  128  W  A  -  -  Sprite 2 pointer (high 5 bits)
SPR2PTL   +  12A  W  A  -  -  Sprite 2 pointer (low 15 bits)
SPR3PTH   +  12C  W  A  -  -  Sprite 3 pointer (high 5 bits)
SPR3PTL   +  12E  W  A  -  -  Sprite 3 pointer (low 15 bits)
SPR4PTH   +  130  W  A  -  -  Sprite 4 pointer (high 5 bits)
SPR4PTL   +  132  W  A  -  -  Sprite 4 pointer (low 15 bits)
SPR5PTH   +  134  W  A  -  -  Sprite 5 pointer (high 5 bits)
SPR5PTL   +  136  W  A  -  -  Sprite 5 pointer (low 15 bits)
SPR6PTH   +  138  W  A  -  -  Sprite 6 pointer (high 5 bits)
SPR6PTL   +  13A  W  A  -  -  Sprite 6 pointer (low 15 bits)
SPR7PTH   +  13C  W  A  -  -  Sprite 7 pointer (high 5 bits)
SPR7PTL   +  13E  W  A  -  -  Sprite 7 pointer (low 15 bits)
SPR0POS   %  140  W  A  D  -  Sprite 0 vert-horiz start pos data
SPR0CTL   %  142  W  A  D  -  Sprite 0 position and control data
SPR0DATA  %  144  W  -  D  -  Sprite 0 image data register A
SPR0DATB  %  146  W  -  D  -  Sprite 0 image data register B
SPR1POS   %  148  W  A  D  -  Sprite 1 vert-horiz start pos data
SPR1CTL   %  14A  W  A  D  -  Sprite 1 position and control data
SPR1DATA  %  14C  W  -  D  -  Sprite 1 image data register A
SPR1DATB  %  14E  W  -  D  -  Sprite 1 image data register B
SPR2POS   %  150  W  A  D  -  Sprite 2 vert-horiz start pos data
SPR2CTL   %  152  W  A  D  -  Sprite 2 position and control data
SPR2DATA  %  154  W  -  D  -  Sprite 2 image data register A
SPR2DATB  %  156  W  -  D  -  Sprite 2 image data register B
SPR3POS   %  158  W  A  D  -  Sprite 3 vert-horiz start pos data
SPR3CTL   %  15A  W  A  D  -  Sprite 3 position and control data
SPR3DATA  %  15C  W  -  D  -  Sprite 3 image data register A
SPR3DATB  %  15E  W  -  D  -  Sprite 3 image data register B
SPR4POS   %  160  W  A  D  -  Sprite 4 vert-horiz start pos data
SPR4CTL   %  162  W  A  D  -  Sprite 4 position and control data
SPR4DATA  %  164  W  -  D  -  Sprite 4 image data register A
SPR4DATB  %  166  W  -  D  -  Sprite 4 image data register B
SPR5POS   %  168  W  A  D  -  Sprite 5 vert-horiz start pos data
SPR5CTL   %  16A  W  A  D  -  Sprite 5 position and control data
SPR5DATA  %  16C  W  -  D  -  Sprite 5 image data register A
SPR5DATB  %  16E  W  -  D  -  Sprite 5 image data register B
SPR6POS   %  170  W  A  D  -  Sprite 6 vert-horiz start pos data
SPR6CTL   %  172  W  A  D  -  Sprite 6 position and control data
SPR6DATA  %  174  W  -  D  -  Sprite 6 image data register A
SPR6DATB  %  176  W  -  D  -  Sprite 6 image data register B
SPR7POS   %  178  W  A  D  -  Sprite 7 vert-horiz start pos data
SPR7CTL   %  17A  W  A  D  -  Sprite 7 position and control data
SPR7DATA  %  17C  W  -  D  -  Sprite 7 image data register A
SPR7DATB  %  17E  W  -  D  -  Sprite 7 image data register B
COLOR00   -  180  W  -  D  -  Color table 00
COLOR01   -  182  W  -  D  -  Color table 01
COLOR02   -  184  W  -  D  -  Color table 02
COLOR03   -  186  W  -  D  -  Color table 03
COLOR04   -  188  W  -  D  -  Color table 04
COLOR05   -  18A  W  -  D  -  Color table 05
COLOR06   -  18C  W  -  D  -  Color table 06
COLOR07   -  18E  W  -  D  -  Color table 07
COLOR08   -  190  W  -  D  -  Color table 08
COLOR09   -  192  W  -  D  -  Color table 09
COLOR10   -  194  W  -  D  -  Color table 10
COLOR11   -  196  W  -  D  -  Color table 11
COLOR12   -  198  W  -  D  -  Color table 12
COLOR13   -  19A  W  -  D  -  Color table 13
COLOR14   -  19C  W  -  D  -  Color table 14
COLOR15   -  19E  W  -  D  -  Color table 15
COLOR16   -  1A0  W  -  D  -  Color table 16
COLOR17   -  1A2  W  -  D  -  Color table 17
COLOR18   -  1A4  W  -  D  -  Color table 18
COLOR19   -  1A6  W  -  D  -  Color table 19
COLOR20   -  1A8  W  -  D  -  Color table 20
COLOR21   -  1AA  W  -  D  -  Color table 21
COLOR22   -  1AC  W  -  D  -  Color table 22
COLOR23   -  1AE  W  -  D  -  Color table 23
COLOR24   -  1B0  W  -  D  -  Color table 24
COLOR25   -  1B2  W  -  D  -  Color table 25
COLOR26   -  1B4  W  -  D  -  Color table 26
COLOR27   -  1B6  W  -  D  -  Color table 27
COLOR28   -  1B8  W  -  D  -  Color table 28
COLOR29   -  1BA  W  -  D  -  Color table 29
COLOR30   -  1BC  W  -  D  -  Color table 30
COLOR31   -  1BE  W  -  D  -  Color table 31
HTOTAL    h  1C0  W  A  -  -  Highest number count in horiz line (VARBEAMEN = 1)
HSSTOP    h  1C2  W  A  -  -  Horiz line pos for HSYNC stop
HBSTRT    h  1C4  W  A  D  -  Horiz line pos for HBLANK start
HBSTOP    h  1C6  W  A  D  -  Horiz line pos for HBLANK stop
VTOTAL    h  1C8  W  A  -  -  Highest numbered vertical line (VARBEAMEN = 1)
VSSTOP    h  1CA  W  A  -  -  Vert line for VBLANK start
VBSTRT    h  1CC  W  A  -  -  Vert line for VBLANK start
VBSTOP    h  1CE  W  A  -  -  Vert line for VBLANK stop
SPRHSTRT  h  1D0  W  A  -  -  UHRES sprite vertical start
SPRHSTOP  h  1D2  W  A  -  -  UHRES sprite vertical stop
BPLHSTRT  h  1D4  W  A  -  -  UHRES bit plane vertical stop
BPLHSTOP  h  1D6  W  A  -  -  UHRES bit plane vertical stop
HHPOSW    h  1D8  W  A  -  -  DUAL mode hires H beam counter write
HHPOSR    h  1DA  R  A  -  -  DUAL mode hires H beam counter read
BEAMCON0  h  1DC  W  A  -  -  Beam counter control register (SHRES,UHRES,PAL)
HSSTRT    h  1DE  W  A  -  -  Horizontal sync start (VARHSY)
VSSTRT    h  1E0  W  A  -  -  Vertical sync start (VARVSY)
HCENTER   h  1E2  W  A  -  -  Horizontal pos for vsync on interlace
DIWHIGH   h  1E4  W  A  D  -  Display window upper bits for start/stop
BPLHMOD   h  1E6  W  A  -  -  UHRES bit plane modulo
SPRHPTH   +h 1E8  W  A  -  -  UHRES sprite pointer (high 5 bits)
SPRHPTL   +h 1EA  W  A  -  -  UHRES sprite pointer (low 15 bits)
BPLHPTH   +h 1EC  W  A  -  -  VRam (UHRES) bitplane pointer (hi 5 bits)
BPLHPTL   +h 1EE  W  A  -  -  VRam (UHRES) bitplane pointer (lo 15 bits)
RESERVED  -  1F0  -  -	-  -  Reserved for future
RESERVED  -  1F2  -  -	-  -  Reserved for future
RESERVED  -  1F4  -  -	-  -  Reserved for future
RESERVED  -  1F6  -  -	-  -  Reserved for future
RESERVED  -  1F8  -  -	-  -  Reserved for future
RESERVED  -  1FA  -  -	-  -  Reserved for future
FMODE     p  1FC  W  A  D  -  Fetch mode register
NO-OP     -  1FE  -  -  -  -  Can also indicate last 2 or 3 refresh cycles or the restart of the COPPER after lockup.





-----------------------------------------------------------------------------





                4. LIST OF REGISTERS ORDERED ALPHABETICALLY
                -------------------------------------------

P  =  New register in Pandora chip set
p  =  Added or changed in hires chips
H  =  New register in hires chips
h  =  Added or changed in hires chips

A  =  Agnus/Alice chip
D  =  Denise/Lisa chip
P  =  Paula chip

W  =  Write
R  =  Read

ER =  Early read. This is a DMA data transfer to RAM, from either the disk
      or from the blitter, Ram timing requires data to be on the bus
      earlier than microprocessor read cycles. These transfers are
      therefore initiated by Agnus timing, rather than a read address on
      the register address bus (RGA).



NAME   rev ADDR type chip Description
---------------------------------------------------------------------------
ADKCON     09E   W   P    Audio,Disk,Uart,Control write

ADKCONR    010   R   P    Audio,Disk,Uart,Control read

                 BITS  USE
                 ----  ----------------------------------------------------
                 15    SET/CLEAR  Set/clear control bit.determines if bits
                                  written with a 1 get set or cleared.bits
                                  written with a zero are always unchanged.

                 14-13 PRECOMP 1-0   CODE   PRECOMP VALUE
                                     ----   -------------
                                      00    none
                                      01    140 ns
                                      10    280 ns
                                      11    560 ns

                 12    MFMPREC    (1 = MFM precomp / 0 = GCR precomp)
                 11    UARTBRK    Forces a UART break (clears TXD) if true

                 10    WORDSYNC   Enables disk read synchronizing on a word
                                  equal to DISK SYNC CODE, Located in
                                  address DSKSYNC (7E).

                 09    MSBSYNC    Enables disk read synchrinizing on the                                   MSB (most signif bit) appl type GCR

                 08    FAST       Disk data clock rate control 1=fast(2us)
                                  0=slow(4us)
                                  (Fast for MFM or 2us,slow for 4us GCR)

                 07    USE3PN     Use audio channel 3 to modulate nothing
                 06    USE2P3     Use audio channel 2 to modulate period
                                  of channel 3
                 05    USE1P2     Use audio channel 1 to modulate period
                                  of channel 2
                 04    USE0P1     Use audio channel 0 to modulate period
                                  of channel 1
                 03    USE3VN     Use audio channel 3 to modulate nothing                  02    USE2V3     Use audio channel 2 to modulate volume
                                  of channel 3
                 01    USE1V2     Use audio channel 1 to modulate volume
                                  of channel 2
                 00    USE0V1     Use audio channel 0 to modulate volume
                                  of channel 1

                 NOTE: If both period and volume aremodulated on the same
                       channel,the period and volume will be alternated.
                       first AUDxDAT word is used for V6-V0 of UDxVOL.
                       second AUDxDAT word is used for P15-P0 of AUDxPER.
                       This alternating sequence is repeated.


AUDxLCH h 0A0    W   A Audio channel x location (high 5 bits)
                       (old-3 bits)

AUDxLCL   0A2    W   A Audio channel x location (low 15 bits)
                       This pair of registers contains the 20 bit starting
                       address(location) of audio channel x (x=0,1,2,3)DMA
                       data. This is not a pointer reg and therfore only
                       needs to be reloaded if a diffrent memory location
                       is to be outputted.

AUDxLEN   0A4    W   P Audio channel x length
                       This reg contains the length (number of words) of
                       audio channel x DMA data.

AUDxPER h 0A6    W   P Audio channel x period
                       This reg contains the period (rate) of audio channel
                       x DMA data transfer.
                       The minimum period is 124 clocks. This means that
                       the smallest number that should be placed in this
                       reg is 124.

AUDxVOL   0A8    W   P Audio channel x volume
                       This reg contains the volume setting for audio
                       channel x. Bits 6,5,4,3,2,1,0 specify 65 linear
                       volume levels as shown below.

                 BITS    USE
                 ----    --------------------------------------------------
                 15-07   Not used
                 06      Forces volume to max (64 ones,no zeros)
                 05-00   Sets one of the 64 levels (000000 = no output
                         (111111 = 63 ones, one zero)

AUDxDAT   0AA    W   P   Audio channel x data
                         This reg is the audio channel x (x=0,1,2,3) DMA
                         data buffer. It contains 2 bytes of data (each
                         byte is a twos complement signed integer) that
                         are outputed sequentially (with digital to analog
                         conversion)to the audio output pins. With maximum
                         volume, each byte can drive the audio outputs
                         with 0.8 volts(peak to peak,typ). The audio DMA
                         channel controller automatically transfers data
                         to this reg from RAM. The processor can also
                         write directly to this reg. When the DMA data is
                         finished (words outputted=length)and the data in
                         this reg has been used, an audio channel interrupt
                         request is set.

BEAMCON0 h 1DC  W    A   Beam counter control bits

                 BIT     FUNCTION
                 ---     --------------------------------------------------
                 15      (unused)
                 14      HARDDIS
                 13      LPENDIS
                 12      VARVBEN
                 11      LOLDIS
                 10      CSCBEN
                  9      VARVSYEN
                  8      VARHSYEN
                  7      VARBEAMEN
                  6      DUAL
                  5      PAL
                  4      VARCSYEN
                  3      (unused, formerly BLANKEN)
                  2      CSYTRUE
                  1      VSYTRUE
                  0      HSYTRUE

HARDDIS = This bit is used to disable the hardwire vertical horizontal
          window limits. It is cleared upon reset.

LPENDIS = When this bit is a low and LPE (BPLCON0,BIT 3) is enabled, the
          light-pen latched value(beam hit position) will be read by
          VHPOSR,VPOSR and HHPOSR. When the bit is a high the light-pen
          latched value is ignored and the actual beam counter position is           read by  VHPOSR,VPOSR, and HHPOSR.

VARVBEN = Use the comparator generated vertical blank (from VBSTRT,VBSTOP)           to run the internal chip stuff-sending RGA signals to Denise,           starting sprites,resetting light pen. It also disables the hard
          stop on the vertical display window.

LOLDIS  = Disable long line/short toggle. This is useful for DUAL mode
          where even multiples are wanted, or in any single display
          where this toggling is not desired.

CSCBEN  = The variable composite sync comes out on the HSY pin, and the
          variable conosite blank comes out on the VSY pin. The idea is
          to allow all the information to come out of the chip for a
          DUAL mode display. The normal monitor uses the normal composite
          sync, and the variable composite sync &blank come out the HSY &
          VSY pins. The bits VARVSTEN & VARHSYEN (below) have priority over
          this control bit.

VARVSYEN= Comparator VSY -> VSY pin. The variable VSY is set vertically on
          VSSTRT, reset vertically on VSSTOP, with the horizontal position
          for set set & reset HSSTRT on short fields (all fields are short
          if LACE = 0) and HCENTER on long fields (every other field if
          LACE = 1).

VARHSYEN= Comparator HSY -> HSY pin. Set on HSSTRT value, reset on HSSTOP
          value.

VARBEAMEN=Enables the variable beam counter comparators to operate 
          (allowing diffrent beam counter total values) on the main horiz 
          counter. It also disables hard display stops on both horizontal
          and vertical.

DUAL    = Run the horizontal comparators with the alternate horizontal beam
          counter, and starts the UHRES pointer chain with the reset of
          this counter rather than the normal one. This allows the UHRES 
          pointers to come out more than once in a horizontal line,
          assuming there is some memory bandwidth left (it doesn`t work in
          640*400*4 interlace mode) also, to keep the two displays synced,
          the horizontal line lengths should be multiples of each other.
          If you are amazingly clever, you might not need to do this.

PAL     = Set appropriate decodes (in normal mode) for PAL. In variable
          beam counter mode this bit disables the long line/short line
          toggle- ends up short line.

VARCSYEN= Enables CSY from the variable decoders to come out the CSY
          (VARCSY is set on HSSTRT match always, and also on HCENTER
          match when in vertical sync. It is reset on HSSTOP match when VSY
          and on both HBSTRT &HBSTOP matches during VSY. A reasonable
          composite can be generated by setting HCENTER half a horiz line
          from HSSTRT, and HBSTOP at (HSSTOP-HSSTRT) before HCENTER, with
          HBSTRT at (HSSTOP-HSSTRT) before .... see below 

---------------------------------------------------------------------------

                      PAGE 19 MISSING (SORRY!)

---------------------------------------------------------------------------

BLTCON0    040  W   A    Blitter control register 0
BLTCON0L H 05A  W   A    Blitter control register 0 (lower 8 bits)
                         This is to speed up software - the upper bits are
                         often the same.

BLTCON1  h 042  W   A    Blitter control register 1
                         These two control registers are used together to
                         control blitter operations. There are 2 basic
                         modes, area and line, which are selected by bit 0
                         of BLTCON1, as shown below.

                         AREA MODE ("normal")     LINE MODE (line draw)
                         --------------------------------------------------
                         BIT#  BLTCON0  BLTCON1    BIT#  BLTCON0  BLTCON1
                         --------------------------------------------------
                         15    ASH3     BSH3       15    ASH3     BSH3
                         14    ASH2     BSH2       14    ASH2     BSH2
                         13    ASH1     BSH1       13    ASH1     BSH1
                         12    ASA0     BSH0       12    ASH0     BSH0
                         11    USEA      0         11     1         0
                         10    USEB      0         10     0         0
                         09    USEC      0         09     1         0
                         08    USED      0         08     1         0
                         07    LF7      DOFF       07    LF7       DPFF
                         06    LF6       0         06    LF6       SIGN
                         05    LF5       0         05    LF5       OVF
                         04    LF4      EFE        04    LF4       SUD
                         03    LF3      IFE        03    LF3       SUL
                         02    LF2      FCI        02    LF2       AUL
                         01    LF1      DESC       01    LF1       SING
                         00    LF0      LINE(=0)   00    LF0       LINE(=1)

                         ASH3-0    Shift value of A source
                         BSH3-0    Shift value of B source and line texture
                         USEA      Mode control bit to use source A
                         USEB      Mode control bit to use source B
                         USEC      Mode control bit to use source C
                         USED      Mode control bit to use destination D
                         LF7-0     Logic function minterm select lines
                         EFE       Exclusive fill enable
                         IFE       Inclusive fill enable
                         FCI       Fill carry input
                         DESC      Descending (dec address)control bit
                         LINE      Line mode control bit
                         SIGN      Line draw sign flag
                         OVF       Line/draw r/l word overflow flag
                         SUD       Line draw, Sometimes up or down (=AUD)
                         SUL       Line draw, Sometimes up or left
                         AUL       Line draw, Always up or left
                         SING      line draw, Single bit per horiz line
                         DOFF      Disables the D output- for external ALUs
                                   The cycle occurs normally, but the data
                                   bus is tristate (hires chips only)
                         
BLTSIZH  h 05E  W   A           Blitter H size & start (11 bit width)

                    BIT# 15 14 13 12 11 10  09 08 07 06 05 04 03 02 01 00
                          x  x  x  x  x w10 w9 w8 w7 w6 w5 w4 w3 w2 w1 w0

BLTSIZV  h 05C  W   A           Blitter V size (15 bit height)
                     
                    BIT# 15 14  13  12  11  10  09 08 07 06 05 04 03 02 01 00
                          x h14 h13 h12 h11 h10 h9 h8 h7 h6 h5 h4 h3 h2 h1 h0
                         
                         These are the blitter size regs for blits larger than 
                         the earlier chips could accept. The original commands
                         are retained for compatibility. BLTSIZV should be 
                         written first, followed by BLTSIZH, which starts the
                         blitter. BLTSIZV need not be rewritten for subsequent
                         bits if the vertical size is the same.
                         Max size of blit 32k pixels * 32k lines, x s should be 
                         written to 0 for upward compatibility.
                         
BPLHDAT  h 07A  W               Ext logic UHRES bit plane identifier
BPLHMOD  h 1E6  W   A           Uhres bit plane modulo

                      This is the number (sign extended) that is added to the
                      UHRES bit plane pointer (BPLHPTL,H) every line, and
                      then another 2 is added, just like the other modulos.

BPLHPTH  h 1EC  W   A           UHRES (VRAM) bit plane pntr (high 5 bits)
BPLHPTL  h 1EE  W   A           UHRES (VRAM) bit plane pntr (low 15 bits)

                      When UHRES is enabled, this pointer comes out on the
                      2nd 'free' cycle after the start of each horizontal
                      line. It`s modulo is added every time it comes out.
                      'free' means priority above the copper and below the
                      fixed stuff (audio,sprites....).
                      BPLHDAT comes out as an identifier on the RGA lines when
                      the pointer address is valid so that external detectors
                      can use this to do the special cycle for the VRAMs, The
                      SHRHDAT gets the first and third free cycles.
                         
BPLHSTOP p 1D6  W   A           UHRES bit plane vertical stop

                         BIT#   name
                         ----   ----
                         15     BPLHWRM 
                         14-11  Unused
                         10-0   V10-V0
                         
                      BPLHWRM = Swaps the polarity of ARW* when the BPLHDAT
                      comes out so that external devices can detect the RGA
                      and put things into memory (ECS and later versions).
                         
BPLHSTRT h 1D4  W   A           UHRES bit plane vertical stop

                      This controls the line when the data fetch starts for
                      the BPLHPTH,L pointers. V10-V0 on DB10-0.
                         
BPLxPTH   0E0   W   A           Bit plane x pointer (high 5 bits)

          0E8            x=1,2,3,4,5,6,7,8
          0EC
          0F0
          0F4
        p 0F8
        p 0FC
       
BPLxPTL   0E2  W    A           Bit plane pointer (low 15 bits)

          0EA          Address of bit plane x  (x=1,2,3,4,5,6,7,8) DMA data.
          0EE          This pointer must be reinitialized by the processor or
          0F2          coprocessor to point to the beginning of bit plane data
          0F6          every vertical blank time.
        p 0FA
        p 0FE        
                                                                        
BPLxDAT   110  W    A           Bit plane x data (parallel to serial convert)

          112          These regs recieve the DMA data fetched from RAM by the
          114          bit plane address pointers described above.
          116          They may also be rewritten by either micro.
          118          they act as a 8 word parallel to serial buffer for up 
          11A          to 8 memory 'bit planes'. x=1-8 the parallel to serial
        p 11C          conversion id triggered whenever bit plane #1 is
        p 11E          written, indicing the completion of all bit planes for
                       that word (16/32/64 pixels). The MSB is output first,
                       and is therefore always on the left.
                         
BPL1MOD   108  W    A           Bit plane modulo (odd planes)
BPL2MOD   10A  W    A           BIt plane modulo (even planes)
 
                       These registers contain the modulos for the odd and
                       even bit planes. A modulo is a number that is automa-
                       itcally added to the address at the end of each line,
                       in order that the address then points to the start of
                       the next line. Since they have seperate modulos, the
                       odd and even bit planes may have sizes that are
                       different from each other, as well as different from
                       the display window size.
                       If scan-doubling is enabled, BPL1MOD serves as the
                       primary bitplane modulos and BPL2MOD serves as the
                       alternate. Lines whose LSBs of beam counter and DIWSTRT
                       match are designated primary, whereas lines whose LSBs
                       don`t match are designated alternate.
                         
BPLCON0 p 100  W    A  D        Bit plane control reg. (misc, control bits)
BPLCON1 p 102  W       D        Bit plane control reg. (horiz, scroll counter)
BPLCON2 p 104  W       D        Bit plane control reg. (new control bits)
BPLCON3 p 106  W       D        Bit plane control reg. (enhanced features)
BPLCON4 p 10c  W       D        Bit plane control reg. (display masks)
                          
                      These regs control the operation of the bit planes and
                      various aspects of the display.
                         
                      BIT#   BPLCON0   BPLCON1   BPLCON2   BPLCON3    BPLCON4
                      ----   -------   -------   -------   -------    -------
                      15     HIRES     PF2H7=0   X         BANK2=0    BPLAM7=0 
                      14     BPU2      PF2H6=0   ZDBPSEL2  BANK1=0    BPLAM6=0
                      13     BPU1      PF2H1=0   ZDBPSEL1  BANK0=0    BPLAM5=0
                      12     BPU0      PF2H0=0   ZDBPSEL0  PF2OF2=0   BPLAM4=0
                      11     HAM       PF1H7=0   ZDBPEN    PF2OF1=1   BPLAM3=0
                      10     DPF       PF1H6=0   ZDCTEN    PF2OF0=1   BPLAM2=0
                      09     COLOR     PF1H1=0   KILLEHB   LOCT=0     BPLAM1=0
                      08     GAUD      PF1H0=0   RDRAM=0   X          BPLAM0=0
                      07     UHRES     PF2H5     SOGEN=0   SPRES1=0   ESPRM7=0
                      06     SHRES     PF2H4     PF2PRI    SPRES0=0   ESPRM6=0
                      05     BYPASS=0  PF2H3     PF2P2     BRDRBLNK=0 ESPRM5=0
                      04     BPU3=0    PF2H2     PF2P1     BRDNTRAN=0 ESPRM4=1
                      03     LPEN      PF1H5     PF2P0     X          OSPRM7=0
                      02     LACE      PF1H4     PF1P2     ZDCLKEN=0  OSPRM6=0
                      01     ERSY      PF1H3     PF1P1     BRDSPRT=0  OSPRM5=0
                      00     ECSENA=0  PF1H2     PF1P0     EXTBLKEN=0 OSPRM4=1
                                     
          x = don`t care; but drive to 0 for upward compatibility!
                           
          HIRES = High resoloution (640*200/640*400 interlace) mode
          
          BPUx  = Bit plane use code 0000-10000 (NONE thru 8 inclusive)
          
          HAM   = Hold and modify mode, now using either 6 or 8 bit planes.
          
          New HAM mode is invoked when this bit is set and BPU = 1000.
          
          DPF   = Double playfield (PFI=odd FP2= even bit planes)
          now available in all resoloutions.
          (If BPU=6 and HAM=0 and DPF=0 a special mode is defined that allows
          bitplane 6 to cause an intensity reduction of the other 5 bitplanes
          The color register output selected by 5 bitplanes is shifted to half
          intensity  by the 6th bit plane. This is called EXTRA-HALFBRITE
          Mode.
          
          COLOR = Enables color burst output signal
          
          GAUD  = Genlock audio enable. This level appears on the ZD pin
          on denise during all blanking periods, unless ZDCLK bit is set
          
          UHRES = Ultrahi res enables the UHRES pointers (for 1k*1k) (also
          needs bits in DMACON (hires chips only).
          Disables hard stops for vert, horiz display windows
          
          SHRES = Super hi-res mode (35ns pixel width)
          
          BYPASS = Bitplanes are scrolled and prioritized normally, but
          bypass color table and 8 bit wide data appear on R(7:0).
          
          LPEN = Light pen enable (reset on power up)
          
          LACE = Interlace enable (reset om power up)
          
          ERSY = External resync (HSYNC, VSYNC pads become inputs)
          (reset on power up)
          
          ECSENA = When low (default), the following bits in BPLCON3 are
          disabled: BRDRBLNK,BRDNTRAN,ZDCLKEN,BRDSPRT, and EXTBLKEN.
          These 5 bits can always be set by writing to BPLCON3, however
          there effects are inhibited until ECSENA goes high. This allows
          rapid context switching between pre-ECS viewports and new ones.
          
          PF2Hx = Playfield 2 horizontal scroll code, x=0-7
          
          PF1Hx = Playfield 1 horizontal scroll code, x=0-7 
          where PFyH0=LSB=35ns SHRES pixel (bits have been renamed, old
          PFyH0 now PFyH2, ect). Now that the scroll range has been 
          quadrupled to allow for wider (32 or 64 bits) bitplanes.
          
          ZDBPSELx =3 bit field which selects which bitplane is to be used
          for ZD when ZDBBPEN is set;000 selects BB1 and 111 selects BP8.
                   
          ZDBPEN = Causes ZD pin to mirror bitplane selected by ZDBPSELx
          bits. This does not disable the ZD mode defined by ZDCTEN, but
          rather is "ored" with it.
          
          ZDCTEN = Causes ZD pin to mirror bit #15 of the active entry in
          high color table. When ZDCTEN is reset ZD reverts to mirroring
          color (0).
          
          KILLEHB = Disables extra half brite mode.
          
          RDRAM = Causes color table address to read the color table instead
          of writing to it.
          
          SOGEN = When set causes SOG output pin to go high
          
          PF2PRI = Gives playfield 2 priority over playfield 1.
          
          PF2Px = Playfield 2 priority code (with resp. to sprites).
          
          PF1Px = Playfield 1 priority code (with resp. to sprites). 
          
          BANKx = Selects one of eight color banks, x=0-2.
          
          PF20Fx = Determine bit plane color table offset whe playfield 2
          has priority in dual playfield mode:
          
          PF20F || AFFECTED BITPLANE ||OFFSET
          -------------------------------------------------------
          | 2 | 1 | 0 || 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 ||(decimal
          -------------------------------------------------------
          | 0 | 0 | 0 || - | - | - | - | - | - | - | - || none 
          | 0 | 0 | 1 || - | - | - | - | - | - | 1 | - || 2
          | 0 | 1 | 0 || - | - | - | - | - | 1 | - | - || 4 
          | 0 | 1 | 1 || - | - | - | - | - | 1 | - | - || 8 (default)    
          | 1 | 0 | 0 || - | - | - | 1 | - | - | - | - || 16   
          | 1 | 0 | 1 || - | - | 1 | - | - | - | - | - || 32 
          | 1 | 1 | 0 || - | 1 | - | - | - | - | - | - || 64  
          | 1 | 1 | 1 || 1 | - | - | - | - | - | - | - || 128
          
          LOCT = Dictates that subsequent color palette values will be
          written to a second 12- bit color palette, constituting the
          RGB low minus order bits. Writes to the normal hi monus order
          color palette automattically copied to the low order for back-
          wards compatibility.
          
          SPRESx = Determine resolution of all 8 sprites (x=0,1);

          -------------------------------------------------------------
          SPRES1 | SPRES0 | SPRITE RESOLUTION
          -------------------------------------------------------------
          0      | 0      | ECS defaults (LORES,HIRES=140ns,SHRES=70ns)
          0      | 1      | LORES (140ns)
          1      | 0      | HIRES (70ns)
          1      | 1      | SHRES (35ns)
          
          BRDRBLNK = "Border area" is blanked instead of color (0).
          Disabled when ECSENA low.
          
          BRDNTRAN = "Border area" is non minus transparant (ZD pin is low
          when border is displayed).
          Disabled when ECSENA low.
          
          ZDCLKEN = ZD pin outputs a 14MHz clock whose falling edge coincides
          with hires (7MHz) video data. this bit when set disables all other
          ZD functions.
          Disabled when ESCENA low.
           
          BRDRSPRT = enables sprites outside the display window.
          disabled when ESCENA low.
          
          EXTBLKEN = causes BLANK output to be programmable instead of
          reflecting internal fixed decodes.
          disabled when ESCENA low.
          
          BPLAMx = This 8 bit field is XOR`ed with the 8 bit plane color
          address, thereby altering the color address sent to the color
          table (x=1-8)
          
          ESPRMx = 4 Bit field provides the 4 high order color table address
          bits for even sprites: SPR0,SPR2,SPR4,SPR6. Default value is 0001
          binary. (x=7-4)
          
          OSPRMx = 4 Bit field provides the 4 high order color table address
          bits for odd sprites: SPR1,SPR3,SPR5,SPR7. Default value is 0001
          binary. (x=7-4)
         
CLXCON    098  W   A            Collision control

                      This register controls which bitplanes are included 
                      (enabled) in collision detection, and their required
                      state if included. It also controls the individual
                      inclusion of odd numbered sprites in the collision
                      detection, by logically OR`ing them with their
                      corresponding even numbered sprite. Writing to this
                      register resets the bits in CLXCON2.
                         
                BIT# FUNCTION DESCRIPTION
                ---- -------- -----------
                15   ENSP7    Enable Sprite 7 (ORed with Sprite 6)
                14   ENSP5    Enable Sprite 5 (ORed with Sprite 4)
                13   ENSP3    Enable Sprite 3 (ORed with Sprite2)
                12   ENSP1    Enable Sprite 1 (ORed with Sprite 0)
                11   ENSP6    Enable bit plane 6 (match reqd. for collision
                10   ENSP5    Enable bit plane 5 (match reqd. for collision                    09   ENSP4    Enable bit plane 4 (match reqd. for collision
                08   ENSP3    Enable bit plane 3 (match reqd. for collision
                07   ENSP2    Enable bit plane 2 (match reqd. for collision
                06   ENSP1    Enable bit plane 1 (match reqd. for collision
                05   ENSP6    Match value for bit plane 6 collision
                04   ENSP5    Match value for bit plane 5 collision
                03   ENSP4    Match value for bit plane 4 collision
                02   ENSP3    Match value for bit plane 3 collision
                01   ENSP2    Match value for bit plane 2 collision
                00   ENSP1    Match value for bit plane 1 collision
                       
CLXCON2 P  10C  W    D          Extended collision control

                       This reg controls when bit planes 7 and 8 are included
                       in collision detection, and there required state if 
                       included. Contents of this register are reset by a
                       write to CLXCON.
                       BITS INITIALIZED BY RESET
                         
                         BIT#  FUNCTION DESCRIPTION
                         ----  -------- -----------
                         15-08          unused
                         07    ENBP8    Enable bit plane 8 (match reqd. for
                                        collision)
                         06    ENBP7    Enable bit plane 7 (match reqd. for 
                                        collision)
                         05-02          unused
                         01    MVBP8    Match value for bit plane 8 collision
                         00    MVBP7    Match value for bit plane 7 collision
                         
                         note: Disable bit planes cannot prevent collisions.
                         Therefore if all bitplanes are disabled, collision
                         will be continuous, regardless of the match values.
                         
CLXDAT   00E  R     D           Collision data reg. (read and clear)

                         This address reads (and clears) the collision
                         detection reg. the bit assignments are below
                  NOTE: Playfield 1 is all odd numbered enabled bit planes.
                        Playfield 2 is all even numbred enabled bit planes.
                          
                         BIT#   COLLISIONS REGISTERED
                         ----   --------------------- 
                         15     not used
                         14     Sprite 4 (or 5) to Sprite 6 (or 7)
                         13     Sprite 2 (or 3) to Sprite 6 (or 7)
                         12     Sprite 2 (or 3) to Sprite 4 (or 5)
                         11     Sprite 0 (or 1) to Sprite 6 (or 7)
                         10     Sprite 0 (or 1) to Sprite 4 (or 5)
                         09     Sprite 0 (or 1) to Sprite 2 (or 3)
                         08     Playfield 2 to Sprite 6 (or 7)
                         07     Playfield 2 to Sprite 4 (or 5)
                         06     Playfield 2 to Sprite 2 (or 3)
                         05     Playfield 2 to Sprite 0 (or 1)
                         04     Playfield 1 to Sprite 6 (or 7)
                         03     Playfield 1 to Sprite 4 (or 5)
                         02     Playfield 1 to Sprite 2 (or 3)
                         01     Playfield 1 to Sprite 0 (or 1)
                         00     Playfield 2 to Playfield 2
                         
COLORxx  180-1BE  W             COLOR table xx

                       There 32 of these registers (xx=00-31) and together
                       with the banking bits they address the 256 locations in
                       the color palette.
                       There are actually two sets of color regs, selection of
                       which is controlled by the LOCT reg bit. When LOCT = 0
                       the 4 MSB of red, green and blue video data are
                       selected along with the T bit for genlocks the low
                       order set of registers is also selected as well, so
                       that the 4 bi valuesare automatically extended to 8
                       bits.This provides compatibility with old software. If
                       the full range of palette values are desired, then LOCT
                       can be set high and independant values for the 4 LSB of
                       red, green  and blue can be written. The low order
                       color registers do not contain a transparency (T) bit.
                       The table below shows the color register bit usage.
                         
      BIT#    15,14,13,12    11,10,09,08    07,06,05,04    03,02,01,00
      ----    -----------    -----------    -----------    -----------
      LOCT=0  T  X  X  X     R7 R6 R5 R4    G7 G6 G5 G4    B7 B6 B5 B4
      LOCT=1  X  X  X  X     R3 R2 R1 R0    G3 G2 G1 G0    B3 B2 B1 B0 
      
      T = TRANSPARENCY      R = RED    G = GREEN    B = BLUE    X = UNUSED
      
                       T bit of COLOR00 thru COLOR31 sets ZD_pin HI, When that
                       color is selected in all video modes.
                         
COPCON h  02E  W     A          Coproccessor control register

                       This is a-1 bit register that when set true, allows
                       the coprocessor to access the blitter hardware this bit
                       is cleared power on reset, so that the coprocessor
                       cannot access the blitter hardware.
                         
                         BIT# NAME   FUNCTION
                         ---- ----   --------
                       01   CDANG  Coprocessor danger mode. Allows coprocessor 
                       access to all RGA registers if true.
                       (if 0, access to RGA>7E)
                       (On old chips access to only RGA>3E if CDANG=1)
                       (see VPOSR)
                         
COPJMP1   088  S    A           Coprocessor restart at first location
COPJMP2   08A  S    A           Coprocessor restart at second location

                       These address are strobe address, that when written to
                       cause the coprocessor to jump indirect useing the add-
                       ress contained in the first or second location regs
                       described below. The coprocessor itself can write to
                       these address, causeing it`s own jump indirect.
                         
COP1LCH h 080  W    A         A Coprocessor first location reg
                                (high 5 bits) (old-3 bits)   
COP1LCL   082  W    A         A Coprocessor first location reg
                                (low 15 bits)
COP2LCH h 084  W    A         A Coprocessor second location reg
                                (high 5 bits) (old-3 bits)
COP2LCL   086  W    A         A Coprocessor second location reg
                                (low 15 bits)
                                
                       These regs contain the jump addresses described below
                                                                                                                    
COPINS    08C  W   A            Coprocessor inst. fetch identify

                       This is a dummy address that is generated by the co-
                       processor whenever it is loading instructions into its
                       own instruction register.
                       This actually occurs every coprocessor cycle except
                       for the second (IR2) cycle of the MOVE instruction. The
                       three types of instructions are shown below.
                         
                       MOVE Move immediate to dest
                         
                       WAIT Wait until beam counter is equal to, or greater
                       than. (Keeps coprocessor off of bus until beam position
                       has been reached)
                         
                       SKIP Skip if beam counter is equal to, or greater than. 
                       (skips following MOVE inst. unless beam position has
                       been reached)
                         
          MOVE             WAIT UNTIL               SKIP IF
          ------------------------------------------------------
          BIT#     IR1     IR2       IR1     IR2     IR1     IR2
          ----     ---     ---       ---     ---     ---     ---
          15        x      RD15      VP7     BFD     VP7     BFD
          14        x      RD14      VP6     VE6     VP6     VE6
          13        x      RD13      VP5     VE5     VP5     VE5
 	  12	    x	   RD12      VP4     VE4     VP4     VE4
	  11	    x	   RD11	     VP3     VE3     VP3     VE3
	  10	    x	   RD10	     VP2     VE2     VP2     VE2
	  09	    x	   RD09	     VP1     VE1     VP1     VE1
	  08       DA8	   RD08	     VP0     VE0     VP0     VE0
	  07       DA7	   RD07      HP8     HE8     HP8     HE8
	  06       DA6	   RD06	     HP7     HE7     HP7     HE7
	  05       DA5	   RD05	     HP6     HE6     HP6     HE6
	  04       DA4	   RD04      HP5     HE5     HP5     HE5
	  03       DA3	   RD03	     HP4     HE4     HP4     HE4
	  02       DA2     RD02	     HP3     HE3     HP3     HE3
	  01       DA1	   RD01	     HP2     HE2     HP2     HE2
	  00        0	   RD00	      1	      0       1       1
				
	IR1=First instruction register
	
	IR2=Second insturction register
	
	DA =Destination address for MOVE instruction.Fetched during 
	    IR1 time,used during IR2 time on RGA bus.
	
	RD =RAM Data moved by MOVE instruction at IR2 time
	    directly from RAM to the address given by the DA field.
        
	VP =Vertical beam position comparison bit.
	
	HP =Horizontal beam position comparison bit.
	       
 	VE =Enable comparison (mask bit)

	HE -Enable comparison (mask bit)

	* NOTE BFD=Blitter finished disable. When this bit is true,
		   the blitter finished flag will have no 
		   effect on the coprocessor. When this bit is zero
		   the blitter finished flag must be true
                   (in addition to the rest of the bit comparisons)
	           before the coprocessor can exit from it`s wait 
	           state, or skip over an instruction. Note  that the 
		   V7 comparison cannot be masked.

	The coprocessor is basically a 2 cycle machine that requests 
 	the bus only during odd memory cycles. (4 memory cycles per in)
        			
	It has priority over the blitter and micro.
	
	There are only three types of instructions, MOVE immediate,
	WAIT until ,and SKIP if. All instructions require 2 bus cycles
	(and two instruction words).Since only the odd bus cycles are
	requested, 4 memory cycle times are required per instruction.
	(memory cycles are 280 ns)

	There are two indirect jump registers COP1LC and COP2LC.
	These are 20 bit pointer registers whose contents are
	used to modify program counter for initalization or jumps.
	
	They are transfered to the program counter whenever strobe
	address COPJMP1 or COPJMP2 are written.In addition  COP1LC 
	is automatically used at the beginning of each vertical
	blank time.

	It is important that one of the jump registers be initalized 
	and it`s jump strobe address hit, after power up but before 
	coprocessor DMAis initalized.T his insures a determined
	startup address, and state.

DDFSTRT  092  W  A  Display data fetch start(horiz. position)
DDFSTOP  094  W  A  Display data fetch stop (horiz. position)
	These registers control the horizontal timing of the beginning
	and end of the bit plane DMA timing display data fetch.
	The vertical bit plane DMA timing is identical to the display 
	windows described above.
	The bit plane Modulos are dependent on the bit plane 
	horizontal size, and on this data fetch window size.

	Register bit assignment 
	-----------------------

	BIT# 15  14  13  12  11  10  09  08  07  06  05  04  03  02  01  00
	USE  XX   X   X   X   X   X   X  H8  H7  H6  H5  H4  H3  H2   X 
	  (X bits should always be driven with 0 to maintain upward 
	   compatability)

	The tables below show the start and stop timing for 
	different register contents
	DDFSTRT (Left edge of display data fetch)
	------------------------------------------
	   PURPOSE 	   H8  H7  H6  H5  H4		
	------------------------------------------
	Extra wide (max)    0   0   1   0   1

	      wide	    0   0   1   1   0

	    normal	    0   0   1   1   1

	    narrow	    0   1   0   0   0

	DDFSTOP (Right edge of display data fetch)
	------------------------------------------
	------------------------------------------
	   PURPOSE 	   H8  H7  H6  H5  H4		
	------------------------------------------
	    narrow	    1   1   0   0   1

	    normal	    1   1   0   1   0

        wide (max)	    1   1   0   1   1

	Note that these numbers will vary with variable beam counter
	mode set: (The maxes and mins, that is)

DIWSTRT 08E  W  A D   Display window start (upper left vert-hor pos)
DIWSTOP 090  W  A D   Display window stop (lower right vert-hor pos)
	These registers control the display window size and position,
	by locating the upper left and lower right corners.
	
	BIT# 15  14  13  12  11  10  09  08  07  06  05  04  03  02  01  00
	USE  V7  V6  V5  V4  V3  V2  V1  V0  H9  H8  H7  H6  H5  H4  H3  H2

	DIWSTRT is vertically restricted to the upper 2/3 
	of the display (v8=0),and horizontally restricted to the 
	left 3/4 of the display (H8=0).*
	* Poof.. (see DIWHIGH for exceptions) don`t ask me i didn`t write it?

DIWHIGH  p 1E4  W  A D Display window upper bits for start, stop 
	this is an added register for Hires chips, and allows 
	larger start & stop ranges. If it is not written, the above 
	(DIWSTRT,STOP) description holds. If this register is written,
	direct start & stop positions anywhere on the screen.
	It doesn`t affect the UHRES pointers.
 
	BIT# 15  14  13  12  11  10  09  08  07  06  05  04  03  02  01  00
	      X   X  H10 H1  H0  V10 V9  V8   X   X  H10 H1  H0  V10 V9  V8
                      (stop)                 |         (start)
					       
	Take care (X) bits should always be written to 0 to 
	maintain upwards compatibility. H1 and H0 values define 
	70ns amd 35ns increments respectively, and new LISA bits.

   NOTE: In all 3 display window registers, horizontal bit
	positions have been renamed to reflect HIRES pixel 
	increments, e.g. what used to be called H0 is now referred to as H2.

DMACON  096  W  A D P DMA control write (clear or set)
DMACONR 002  R  A   P DMA control (and blitter status) read

	This register controls all of the DMA channels, and contains 
	blitter DMA status bits.
	
	BIT#    FUNCTION       DESCRIPTION
	----    --------   ------------------------------------------------
	 15     SET/CLR	   Set/Clear control bit. Determines if bits 
			   written wit a 1 get set or cleared.
		             Bits written witn a zero are unchanged.
	 14     BBUSY	   Blitter busy status bit (read only)
	 13     BZERO          Blitter logic zero status bit. (read only)
	 12     X
	 11     X
	 10     BLTPRI	   Blitter DMA prioiry (over CPU micro)
			   (also called "blitter nasty")
			   (disables /BLS pin, preventing micro 
			   from stealing any bus cycles while 
			   blitter DMA is running)
	 09     DMAEN	   Enable all DMA below (also UHRES DMA)
	 08     BPLEN          Bit plane DMA enable 
	 07     COPEN	   Coprocessor DMA enable
	 06     BLTEN	   Blitter DMA enable
	 05     SPREN	   Sprite DMA enable
	 04     DSKEN	   Disk DMA enable
	 03     AUD3EN         Audio chanel 3 DMA enable	
	 02     AUD2EN         Audio chanel 2 DMA enable				 		 		      
	 01     AUD1EN         Audio chanel 1 DMA enable	
 	 00     AUD0EN         Audio chanel 0 DMA enable	

DSKPTH h 020 W  A	Disk pointer (high 5 bits) (old-3 bits)
DSKPTL   022 W  A	Disk pointer (low 15 bits)
		This pair of registers contains the 20 bit address 
		of disk DMA data. These address registers must be
		initalized by the processor or coprocessor 
		before disk DMA is enabled.

DSKLEN	024 W		P    Disk length
	This register contains the length (number of words) of 
	disk DMA data. It also contains 2 control bits. These
	are a DMA enable bit, and a DMA direction (read/write) bit.


	BIT#    FUNCTION   DESCRIPTION
	----    --------   ------------------------------------------------
	 15	DMAEN	   Disk DMA enable
	 14	WRITE      Disk write (RAM or disk) if 1
	 13-0   LENGTH     LENGTH (# of words) of DMA data.
	 

DSKDAT	026 W  P  Disk DMA data write
DSKDATR 008 ER   P  Disk DMA  data read (early read dummy address)

	This register is the disk-DMA data buffer.It contains 2 
	bytes of data that are either sent to (write) or received 
	from (read) the disk. The DMA controller automatically 
	transfers data to or from this register and RAM, and when
	the DMA data is finished (length=0) it causes a disk 
	block interrupt. See interrupts below.

DSKBYTR 01A  R  p Disk data byte and status read

	This register is the Disk-Microrocessor data buffer.
	Data from the disk (in read mode) is leaded into this
	register one byte at a time, and bit 15 (DSKBYT) is set true.
		
	BIT#    FUNCTION   DESCRIPTION
	----    --------   ------------------------------------------------
	 15     DSKBYT     Disk byte ready (reset on read)
	 14     DMAON      DMAEN (DSKLEN) & DMAEN (DMACON) & DSKEN (DMACON)	
	 13     DISKWRITE  Mirror of bit 14 (WRITE) in DSKLEN 
	 12     WORDEQUAL  This bit true only while DSKSYNC register 
		         equals the data from disk 
	 11-08  0	         Not used
	 07-00  DATA       Disk byte data 

DSKSYNC  07E W  	P Disk sync register,the match code for disk
		  read synchronization. See ADKCON bit 10

FMODE P  1FC W 		  Memory Fetch Mode
		This register controls the fetch mechanism for different
		types of Chip RAM accesses: 
	
	BIT#    FUNCTION   DESCRIPTION
	----    --------   -------------------------------------------
 	 15     SSCAN2     Global enable for sprite scan-doubling.
	 14     BSCAN2	   Enables the use of 2nd P/F modulus on an
			   alternate line basis to support bitplane 
			   scan-doubling.
	 13-04  Unused
	 03     SPAGEM     Sprite page mode (double CAS)
	 02     SPR32      Sprite 32 bit wide mode 
	 01     BPAGEM     Bitplane Page Mode (double CAS)
	 00     BLP32	   Bitplane 32 bit wide mode

	BPAGEM BPL32 Bitplane Fetch Increment Memory Cycle Bus Width 	  
  	------------------------------------------------------------
	  0	0    By 2 bytes    (as before) normal CAS     16
	  0	1    By 4 bytes 	       normal CAS     32		
	  1	0    By 4 bytes 	       double CAS     16
	  1 	1    By 8 bytes      	       double CAS     32

	SPAGEM SPR32 Sprite Fetch Increment  Memory Cycle  Bus Width
	------------------------------------------------------------
	  0     0    By 2 bytes    (as before) normal CAS     16
	  0     1    By 4 bytes                normal CAS     32
	  1     0    By 4 bytes                double CAS     16
	  1     1    By 8 bytes                double CAS     32

HBSTOP 1C6 W  D    Horizontal STOP position 
HBSTRT 1C4 W  D    Horizontal START position
		
		Bits 7-0 contain the stop and start positions,
		respectively, for programed horizontal blanking in 
		280nS increments.Bits 10-8 provide a fine position
		control in 35nS increments.

	
	BIT#    FUNCTION   DESCRIPTION
	----    --------   ------------------------------------------------	
	 15-11  x          (unused)
	 10     H1         140nS
	 09     H1         70nS
	 08     H0         35nS  
	 07     H10        35840nS
	 06     H9         17920nS
	 05     H8         8960nS
	 04     H7         4480nS
	 03     H6         2240nS
	 02     H5         1120nS
	 01     H4         560nS 
	 00     H3         280nS


HCENTER H 1E2  W  A  Horizontal position (CCKs) of VSYNC on long field

	 this is necessary for interlace mode with variable beam
	 counters. See BEAMCON0 for when it affects chip outputs.
	 See HTOTAL for bits.

HHPOSR  H 1DA  R  A  DUAL mode hires Hbeam counter read
HHPOSW  H 1D8  W  A  DUAL mode hires Hbeam counter write

	This the secondary beam counter for 
	the faster mode, triggering the UHRES pointers & doing the 
	comparisons for HBSTRT,STOP,HTOTAL,HSSRT,HSSTOP
	(See HTOTAL for bits)

HHSTOP H  1C2  W  A   Horiz line position for SYNC stop
		Sets # of colour clocks for sync stop (HTOTAL for bits)

HHSTRT H  1DE  W  A  Horiz line position for HSYNC stop
		Sets # of colour clocks for sync start (HTOTAL for bits)
		See BEAMCON0 for details of when these 2 are active.

HTOTAL H  1C0  W  A    Highest colour clock count in horiz line


	BIT#  15  14  13  12  11  10  09  08  07  06  05  04  03  02  01  00
	       x   x   x   x   x   x   x   x  h8  h7  h6  h5  h4  h3  h2  h1

	(x`s should be driven to 0 for upward compatibility)    
	Horiz line has theis many + 1 280nS increments. If the 
	pal bit & LOLDIS are not high, long line/skort line toggle
	will occur, and there will be this many +2 every other line.
	Active if VARBEAMEN=1 or DUAL+1.

INTREQ   09C  W         P Interrupt request bits (clear or set)
INTREQR  01E  R         P Interrupt request bits (read)

	This register contains interrupt request bits (or flags).
	These bits may be polled by the processor, and if enabled
	by the bits listed in the next register, they may cause 
	processor interrupts. Both a set and clear operation 
	are required to load arbitary data into this register.
	The bit assignments are identical to the enable register 
	below.   

INTENA   09A  W 	   P Interrupt enable bits (clear or set bits)
INTENAR  01C  R        P Interrupt enable bits (read)

	This register contains interrupt enable bits. The bit 
	assignment for both the request, and enable registers
	is given below.


	BIT#    FUNCTION  LEVEL DESCRIPTION
	----    --------  ----- ----------------------------------------
	 15     SET/CLR         Set/clear control bit. Determines if bits 
			    written with a 1 get set or cleared. Bits
 			    written with a zero are always unchanged.
	 14     INTEN	    Master interrupt (enable only, no request)
	 13     EXTER      6    External interrupt
	 12     DSKSYN     5    Disk sync register (DSKSYNC) matches disk
	 11     RBF        5    Serial port receive buffer full
	 10     AUD3       4    Audio channel 3 block finished 
 	 09     AUD2       4    Audio channel 2 block finished 
 	 08     AUD1       4    Audio channel 1 block finished 
 	 07     AUD0       4    Audio channel 0 block finished 
	 06     BLIT       3    Blitter has finished 
	 05     VERTB      3    Start of vertical blank
	 04     COPER      3    Coprocessor
	 03     PORTS      2    I/O Ports and timers 
	 02     SOFT       1    Reserved for software initated interrupt.
	 01     DSKBLK     1    Disk block finished
	 00     TBE        1    Serial port transmit buffer empty
	
JOY0DAT  00A R     D   Joystick-mouse 0 data (left vert, horiz)
JOY1DAT  00C R     D   Joystick-mouse 1 data (right vert,horiz)

	These addresses each read a 16 bit register. These in turn
	are loaded from the MDAT serial stream and are clocked in on 
	the rising edge of SCLK. MLD output is used to parallel load
	the external parallel-to-serial converter.This in turn is
	loaded with the 4 quadrature inputs from each of two game 
	controller ports (8 total) plus 8 miscellaneous control bits 
	which are new for LISA and can be read in upper 8 bits of 
	LISAID.
	Register bits are as follows:
	Mouse counter usage (pins  1,3 =Yclock, pins 2,4 =Xclock)

    BIT#  15  14  13  12  11  10  09  08     07  06  05  04  03  02  01  00	
JOY0DAT   Y7  Y6  Y5  Y4  Y3  Y2  Y1  Y0     X7  X6  X5  X4  X3  X2  X1  X0
JOY1DAT   Y7  Y6  Y5  Y4  Y3  Y2  Y1  Y0     X7  X6  X5  X4  X3  X2  X1  X0


	0=LEFT CONTROLLER PAIR, 1=RIGHT CONTROLLER PAIR.
	(4 counters total).The bit usage for both left and right
	addresses is shown below. Each 6 bit counter (Y7-Y2,X7-X2) is
	clocked by 2 of the signals input from the mouse serial
	stream. Starting with first bit recived:   	

       Serial Bit Name	Description
	--------------------------------------------------------------------
	    0    | M0H  | JOY0DAT Horizontal Clock
	    1    | M0HQ | JOY0DAT Horizontal Clock (quadrature)
	    2    | M0V  | JOY0DAT Vertical Clock  
	    3    | M0VQ | JOY0DAT Vertical Clock  (quadrature)
	    4    | M1V  | JOY1DAT Horizontall Clock  	
	    5    | M1VQ | JOY1DAT Horizontall Clock (quadrature)
	    6    | M1V  | JOY1DAT Vertical Clock	
	    7    | M1VQ | JOY1DAT Vertical Clock (quadrature)
	 	
	Bits 1 and 0 of each counter (Y1-Y0,X1-X0) may be 
	read to determine the state of the related input signal pair.
	This allows these pins to double as joystick switch inputs.
	Joystick switch closures can be deciphered as follows:

		  Directions     Pin#     Counter bits
		  ----------     ----	  --------------------
		  Forward          1      Y1 xor Y0 (BIT#09 xor BIT#08)
		  Left             3      Y1 
		  Back             2      X1 xor X0 (BIT#01 xor BIT#00)
		  Right            4      X1

JOYTEST  036 W   D     Write to all 4  joystick-mouse counters at once.
		  Mouse counter write test data:
     BIT#  15  14  13  12  11  10  09  08     07  06  05  04  03  02  01  00	
  JOY0DAT  Y7  Y6  Y5  Y4  Y3  Y2  xx  xx     X7  X6  X5  X4  X3  X2  xx  xx  
  JOY1DAT  Y7  Y6  Y5  Y4  Y3  Y2  xx  xx     X7  X6  X5  X4  X3  X2  xx  xx


LISAID  H  07C  R   D    Denise/Lisa (video out chip) revision level

	The original Denise (8362) does not have this register, so
	whatever value is left over on the bus from the last cycle
	will be there. ECS Denise (8373) returns hex (fc) in the lower
	8 bits.Lisa returns hex (f8). The upper 8 bits of this 
	Register are loaded from the serial mouse bus, and are 
	reserved for future hardware implentation.

	The 8 low-order bits are encoded as follows:

	BIT#  Description
	----  --------------------------------------------------
	 7-4  Lisa/Denise/ECS Denise Revision level(decrement to
	      bump revision level, hex F represents 0th rev. level).
	   3  Maintain as a 1 for future generation
	   2  When low indicates AA feature set (LISA) 
	   1  When low indicates ECS feature set (LISA or ECS DENISE)
	   0  Maintain as a 1 for future generation

POT0DAT h  012  R       P  Pot counter data left pair (vert, horiz)
POT1DAT h  014  R       P  Pot counter data right pair (vert,horiz)

	These addresses each read a pair of 8 bit pot counters.
	(4 counters total). The bit assignment for both 
	addresses is shown below. The counters are stopped by signals
	from 2 controller connectors (left-right) with 2 pins each.
   		 
  BIT#  15  14  13  12  11  10  09  08     07  06  05  04  03  02  01  00	 	 
 RIGHT  Y7  Y6  Y5  Y4  Y3  Y2  Y1  Y0     X7  X6  X5  X4  X3  X2  X1  X0
  LEFT  Y7  Y6  Y5  Y4  Y3  Y2  Y1  Y0     X7  X6  X5  X4  X3  X2  X1  X0 
   
		CONNECTORS 
		-------------------------PAULA
                  
		Loc.    dir.  sym   pin   pin
                -----   ----- ----- ----- ----- 
		RIGHT   Y     RX     9    33
               	RIGHT   X     RX     5    32
		 LEFT   Y     LY     9    36
		 LEFT   X     LX     5    35

	With normal (NTSC or PAL) horiz. line rate, the pots will
	give a full scale (FF) reading with about 500kohms in one
	frame time. With proportionally faster horiz line times,
	the counters will count proportionally faster.
	This should be noted when doing variable beam displays.

POTGO  034 W      P   Pot port (4 bit) bi-direction and data,

	and pot counter start.

POTINP 016 R      P Pot pin data read

	This register controls a 4 bit bi-direction I/O port
	that shares the same 4 pins as the 4 pot counters above.

	BIT#    FUNCTION   DESCRIPTION
	----    --------   ----------------------------------------
         15     OUTRY      Output enable for Paula pin 33	
	 14     DATRY      I/O data Paula pin 33
	 13     OUTRX      Output enable for Paula pin 32
	 12     DATRX      I/O data Paula pin 32 
	 11     OUTLY      Out put enable for Paula pin 36
	 10     DATLY      I/O data Paula pin 36
	 09     OUTLX      Output enable for Paula pin 35
         08     DATLX      I/O data  Paula pin 35
	 07-01    X        Not used
	 00     START      Start pots (dump capacitors,start counters)

REFPTR   028  W   A     Refresh pointer 

	This register is used as a dynamic RAM refresh address
	generator. It is writeable for test purposes only,and
	should never be written by the microprocesor.

 
SERDAT  030  W      P   Serial port data and stop bits write.

	This address writes data to a transmit data buffer.
	Data from this buffer is moved into a serial shift register
	for output transmission whenever it is empty.This sets the 
	interrupt request TBE  (transmit buffer empty). A stop bit
	must be provided as part of the data word. The length
	of the data word is set by the position of the stop bit.

 
  BIT#  15  14  13  12  11  10  09  08     07  06  05  04  03  02  01  00
  USE    0   0   0   0   0   0   S  D8     D7  D6  D5  D4  D3  D2  D1  D0

	Note :  S= Stop bit =1, D= data bits

SERDATR  018  R      P  Serial port data and status read.

	This address reads data from a recive data buffer.
	Data in this buffer is loaded from a receiving shift
	register whenever it is full. Several interrupt request 
	bits are also read at this address, along with the data as
	shown below.
  

	BIT#    FUNCTION   DESCRIPTION
	----    --------   ----------------------------------------
	 15     OVRUN      Serial port receiver overun
	 14     RBF        Serial port receive buffer full (mirror)
	 13     TBE        Serial port transmit buffer empty (mirror)
	 12     TSRE       Serial port transmit shift reg. empty
	 11     RXD        RXD pin receives UART serial data for 
			   direct bit test by the micro.
	 10     X          Not used.
	 09     STP        Stop bit
	 08   STP-DB8      Stop bit if LONG, data bit if not.
	 07     DB7        Data bit.
	 06     DB6        Data bit.
	 05     DB5        Data bit.
	 04     DB4        Data bit.
	 03     DB3        Data bit.
	 02     DB2        Data bit.
	 01     DB1        Data bit.
	 00     DB0        Data bit.

SERPER  032  W        P    Serial port period and control.
		This register contains the control bit LONG reffered to 
		above, and a 15 bit number defining the serial port
		Baud rate.If this number is N,then the baud rate is
		1 bit every (N+1)*.2794 microseconds.

	BIT#    FUNCTION   DESCRIPTION
	----    --------   ----------------------------------------
	 15     LONG       Defines serial receive as 9 bit word.
	 14-00  RATE       Defines baud rate=1/((N+1)*.2794 microseconds)

SPRHDAT  H 078   W  exe logic UHRES sprite identifier and data

	This identifies the cycle when this pointer address is on 
	the bus accessing the memory.

SPRHPTH  H  1E8  W   A    UHRES sprite pointer (high 5 bits)
SPRHPTL  H  1EA  W   A    UHRES sprite pointer (low 15 bits)

	This pointer is activated in the 1st and 3rd `free` cycles
	(see BPLHPTH,L) after horiz line start.It increments 
	for the next line.

SPRHSTOP H 1D2  W    A    UHRES sprite vertical display stop
  	
    BIT#  15  14  13  12  11  10  09  08     07  06  05  04  03  02  01  00
SPRHWRM   x   x   x   x   x  v10  v9  v8     v7  v6  v5  v4  v3  v2  v1  v0 

	SPRHWRM = Swaps the polarity of ARW* when the SPRHDAT comes
	out so that external devices can detect the RGA and put 
	things into memory.(ECS and later chips only)



SPRHSTRT H 1D0  W   A     UHRES sprite vertical display start

 BIT#  15  14  13  12  11  10  09  08     07  06  05  04  03  02  01  00
        x   x   x   x   x  v10 v9  v8     v7  v6  v5  v4  v3  v2  v1  v0
  
SPRxPTH    120  W    A      Sprite x pointer (High 5 bits)
SPRxPTL    122  W    A      Sprite x pointer (low 15 bits)

	This pair of registers contains the 20 bit address
	of sprite x (x=0,1,2,3,4,5,6,7) DMA data.These address
	registers must be initalized by the processor or coprocessor
	every vertical blank time.

SPRxPOS   140   W    A  D   Sprite x vert-horiz start position data.

	BIT#	SYM		FUNCTION
        ----    ----    	-----------------------------------------
	15-08  SV7-SV0  	Start vertical value.High bit (SV8) is 
				in SPRxCTL register below.
	07-00  SH10-SH3 	Sprite horizontal start value. Low order
			        3 bits are in SPRxCTL register below. If 
				SSCAN2 bit in FMODE is set, then disable
				SH10 horizontal coincidence detect.This bit
				is then free to be used by ALICE as an 
				individual scan double enable.


SPRxCTL p 142 W     A  D   Sprite position and control data

	  BIT#	SYM		FUNCTION
          ----   ----    	----------------------------------------
 	 15-08  EV7-EV0         End (stop) vert. value. Low 8 bits 
	  07    ATT	        Sprite attach control bit (odd sprites only)
	  06    SV9	        Start vert value 10th bit.
	  05    EV9             End (stop) vert. value 10th bit
	  04   SH1=0            Start horiz. value, 70nS increment
	  03   SH0=0            Start horiz. value 35nS increment
	  02    SV8             Start vert. value 9th bit
	  01    EV8             End (stop) vert. value 9th bit
	  00    SH2             Start horiz.value,140nS increment

	These 2 registers work together as position, size and 
	feature sprite control registers.They are usually loaded
	by the sprite DMA channel, during horizontal blank,
	however they may be loaded by either processor any time.
	Writing to SPRxCTL disables the corresponding sprite.

SPRxDATA  144  W      D    Sprite x image data register A
SPRxDATB  146  W      D    Sprite x image data register B

	These registers buffer the sprite image data.They are 
	usually loaded by the sprite DMA channel but may be 
	loaded by either processor at any time. When a horizontal
	coincidence occurs the buffers are dumped into shift
	registers and serially outputed to the display, MSB first
	on the left.
	NOTE: Writing to the A buffer enables (arms) the sprite.
	Writing to the SPRxCTL registers disables the sprite.
	If enabled, data in the A and B buffers will be output
	whenever the beam counter equals the sprite horizontal 
	position value in the SPRxPOS register. In lowres mode,
	1 sprite pixel is 1 bitplane pixel wide.In HRES and 
	SHRES mode, 1 sprite pixel is 2 bitplane pixels.
	The DATB bits are the 2SBs (worth 2) for the color registers,
	and MSB for SHRES. DATA bits are LSBs of the pixels.
   

STREQU    038   S    D    Strobe for horiz sync with VB (vert blank) and EQU
STRVBL    038   S    D    Strobe for horiz sync with VB
STRHOR    03C   S    D P  Strobe for horiz sync
STRLONG h 03E   S    D    Strobe for identification of long horiz line (228CC)
	  		  
			  One of the first 3 strobe addresses above, it is
			  placed on the RGA bus during the first refresh time
			  slot of every other line, to identify lines with 
			  long counts (228- NTSC, HTOTAL+2- VARBEAMEN=1
			  hires chips only).There are 4 refresh time slots
			  and any not used for strobes will leave a null 
			  (1FE) address on the RGA bus.
		 
					    		 	
VBSTOP H 1CE   W    A    Vertical line for VBLANK stop
VBSRTR H 1CC   W    A    Vertical line for VBLANK start
			 (V10-0 <- D10-0) Affects CSY pin if BLAKEN=1 and VSY pin
			 if CSCBEN=1 (see BEAMCON0)

VPOSR  p 004   R    A   Read vert most sig. bits (and frame flop)
VPOSW    02A   W    A   Write most sig. bits (and frame flop)

  	 		 	 	     		
 BIT#  15  14  13  12  11  10  09  08     07  06  05  04  03  02  01  00
 USE LOF   I6  I5  I4  I3  I2  I1  I0 LOL --  --  --  --  --  V10 V9  V8
		
		LOF=Long frame(auto toggle control bit in BPLCON0)
		I0-I6 Chip identitication:
		8361 (Regular) or 8370 (Fat) (Agnus-ntsc)=10
		8367 (Pal) or 8371 (Fat-Pal) (Agnus-pal)=00
		8372 (Fat-hr) (agnushr),thru rev4 = 20 Pal,30 NTSC
		8372 (Fat-hr) (agnushr),rev 5 = 22 Pal, 31 NTSC 
		8374 (Alice) thru rev 2 = 22 Pal, 32 NTSC
		8374 (Alice) rev 3 thru rev 4 = 23 Pal, 33 NTSC
		LOL = Long line bit. When low, it indicates short raster 
		line.
		v9,10 -- hires chips only (20,30 identifiers)

VHPOSR     006  R   A    Read vert and horiz position of beam, or lightpen 
VHPOSW     02C  W   A    Write vert horiz position of beam, or lightpen
 BIT#  15  14  13  12  11  10  09  08     07  06  05  04  03  02  01  00
 USE   V7  V6  V5  V4  V3  V2  V1  V0     H8  H7  H6  H5  H4  H3  H2  H1

		RESOLUTION = 1/160 of SCREEN WITH ( 280 nS)

VSSTOP H   1CA W   A   Vert position for VSYNC start
VTOTAL H   1C8 W   A   Highest numbered vertival line (VARBEAMEN = 1)

	It`s the line number to reset the counter,
	so there`s this many + 1 in a field. The exception is 
	if the LACE bit is set (BPLCON0), in which case every 
	other field is this many + 2 and the short field is this
	many + 1.









----------------------------------------------------------------------------


                     5.	NEW LISA DISPLAY MODES  
                     -------------------------

                  Now there is a palette of 2~24 colours.


	LORES  (320x200)
	----------------

	6 Bitplane (non HAM, non EHB) 64 colours                !
	7 Bitplane 		128 colours			!
	8 Bitplane		256 colours			!
	8 Bitplane HAM  	Any 2~24 colours                !

	Dual playfield, Max 4 bitplane per playfield            !
	16 colours per playfield.The bank of 16 colours
	in the 256 colour palette is selectabel per playfield


	HIRES  (640x200)
	----------------

	5 Bitplanes		32 colours			@
	6 Bitplanes		64 colours			@
	7 Bitplanes		128 colours			@
	8 Bitplanes		256 colours			@
	6 Bitplanes EHB  	32 * 2 colours			@
	6 Bitplanes HAM		4096 colours			@
	8 Bitplanes HAM		any of 2~256 colours		@

	Dual playfield, max 4 bitplane per playfield	        ! or @
	16 colours per playfield. The bank of 16 colours 
	in the 256 colour palette is selectable per playfield.


	SUPERHIRES (1280X200)
	---------------------

	1 or 2 bitplanes, as ECS, but no colour fudging		!
	3 Bitplanes		8 colours			@
	4 Bitplanes		16 colours			@	
	5 Bitplanes		32 colours			$
	6 Bitplanes		64 colours			$
	7 Bitplanes		128 colours			$
	8 Bitplanes		256 colours			$
	6 Bitplanes EHB         32 * 2 colours			$
	6 Bitplanes HAM		4O96 colours			$
	8 Bitplanes HAM         any of 2~24 colours		$

	Dual Playfield, max 4 bitplanes per playfield   	@ or $
	16 colours per playfield. The bank of 16 of colours
	in the 256 colours palette is selectable per playfield.


	VGA  (640X480 non-interlaced)
	-----------------------------
	
	1 or 2 bitplanes, as ECS, but no colour fudging		!
	3 Bitplanes		8 colours			@
	4 Bitplanes		16 colours			@	
	5 Bitplanes		32 colours			$
	6 Bitplanes		64 colours			$
	7 Bitplanes		128 colours			$
	8 Bitplanes		256 colours			$
	6 Bitplanes EHB         32 * 2 colours			$
	6 Bitplanes HAM		4O96 colours			$
	8 Bitplanes HAM         any of 2~24 colours		$

	Dual playfield,Max 4 bitplanes per playfield	        @ or $
	16 colours per playfield . The bank of 16 colours 
	in the 256 colour palette is selectable per playfield	


	Super 72 (848x614 interlaced, 70 Hz frame rate)
	-----------------------------------------------

	1 or 2 bitplanes, as ECS, but no colour fudging		1X
	3 Bitplanes		8 colours			2X
	4 Bitplanes		16 colours			2X
	5 Bitplanes		32 colours			4X
	6 Bitplanes		64 colours			4X
	7 Bitplanes		128 colours			4X
	8 Bitplanes		256 colours			4X
	6 Bitplanes EHB         32 * 2 colours			4X
	6 Bitplanes HAM		4O96 colours			4X
	8 Bitplanes HAM         any of 2~24 colours		4X

	Dual playfield,Max 4 bitplanes per playfield	        2X or 4X
	16 colours per playfield . The bank of 16 colours 
	in the 256 colour palette is selectable per playfield	


	All playfield scrolling is now in 35ns increments.
	Pre AGA scrolling was in 140ns increments.

		SCROLL RANGE AS PROGRAMMED IN BPLCON1




end.