MOTOROLA 68000 INSTRUCTION SET
			==============================


This file is Public Domain. It contains the Motorola 68000 instruction set,
fully documented, in a manner conforming to the standards laid down in the
official Motorola documentation. The information contained here should be
sufficient not only to allow newcomers to 680x0 assembly language to famil-
iarise themselves with the instruction set, but for more experienced 68000
programmers to devise the basis of their own assembler, containing as it
does the actual machine words corresponding to each instruction in binary
format.

	The file includes extra information:


	1) Extra instructions found upon the 68010 processor, and
	   where possible, some extra instructions found upon the
	   68020 processor.

	2) Extra addressing modes found upon the 68020 processor.


There are several conventions used here. The following convention is used to
illustrate condition code status:


			X N Z V C
			- 0 1 * U

		-	Flag unchanged by operation

		0	Flag set to 0 by operation

		1	Flag set to 1 by operation

		*	Flag changed functionally according
			to operation

		U	Flag undefined after operation


Where instruction words are given, they are given in binary, with various bit
fields picked out using various letter combinations. These bit fields in turn
have their own explicit documentation within each instruction. The characters
X, N, Z, V and C refer to those condition code bits throughout except where a
different convention from below specifies otherwise.

	The following abbreviations are used in the documentation of the var-
ious 68000 instructions:


		src	Source Operand

		dst	Destination Operand

		Dn	Any Data Register

		An	Any Address Register

		Rn	Any 680x0 Register, be it
			Data or Address Register

		Xn	Any 680x0 Register, be it
			Data or Address Register,
			in the context of an index
			register

		CCR	Condition Code Register

		SR	Status Register

		PC	Program Counter

		<ea>	Any Effective Address using a legal
			680x0 addressing mode.

		#nnn	Any Immediate Operand

		(10)	Specifies BCD Operand

		op{N}	Specifies bit N of Operand for
			68000/68010.


	The main documentation will consist of two parts. The first part is
the individual instructions and their descriptions, the second is a full list
of possible addressing modes and condition code computations.

	Furthermore, some instructions are PRIVILEGED. This means that they
can ONLY be executed when the 68000 is operating in SUPERVISOR mode (i.e.,
bit 13 of the status register is set). Attempting to execute these instruc-
tions with the 68000 in USER mode will cause the 68000 to enter exception
processing, and trap via the Privilege Violation exception vector.

	NOTES : Some warnings for programmers inclined to use various tricks:

	1) All arithmetic performed upon address registers uses the ENTIRE
	   32 bits of the address register! WORD size operands are SIGN
	   EXTENDED to 32 bits within the 68000 prior to the operation.
	   Source operands are NOT affected, however.

	2) MOVEM.W from memory to registers SIGN EXTENDS TO 32 BITS. THIS
	   INCLUDES DATA REGISTERS! So, if using upper halves of data reg-
	   isters to save important data, best to MOVEM.L to and from memory
	   instead, otherwise the upper halves of the data registers will
	   be corrupted!

	3) To ensure correct testing for multiple-precision extended-bit
	   arithmetic instructions (ADDX, SUBX), use something such as
	   MOVEQ #0,D0 to set the Z flag prior to the ADDX/SUBX sequence.
	   Then, testing for zero operands at the end of the operations
	   will work correctly (unless other instructions in your arith-
	   metic loop affect Z also!).

	4) DIVS/DIVU take a 32-BIT SOURCE. The result is a 16-BIT DESTIN-
	   ATION, and a 16-BIT REMAINDER. If an overflow occurs, then the
	   destination is NOT AFFECTED. This holds for 68000/68010. For
	   68020 onwards, extended DIVS/DIVU instructions exist.

	5) MULS/MULU take 16-BIT source and destination operands, but the
	   result is a 32-BIT destination. So the upper half of Dn will
	   be corrupted. If using upper halves of data registers to save
	   important data, save the data somehow first. This holds for
	   68000/68010. For 68020 onwards, extended MULS/MULU instructions
	   exist.

	6) DBcc only affects low words of data registers. So two counters
	   can be kept in one register and SWAPped as appropriate (see
	   DBcc and SWAP below).

	7) Since 68000 address pointers are 24-bit pointers, there are
	   always 8 bits spare at the uppermost byte of an address reg-
	   ister on the 68000. These can be used to mix flags data with
	   address pointers. DO NOT USE THIS TRICK IF CODE IS INTENDED
	   TO BE PORTABLE TO 68020/68030/68040 ENVIRONMENTS! These pro-
	   cessors use the full 32 bits of an address register, and have
	   a full 32-bit address space. Bus errors could result. See the
	   Motorola documentation for more information.

	8) Programmers extending the instruction set via LINEF instructions
	   can do so with impunity on the 68000. On the 68020/68030/60840,
	   this is NOT possible. LINEF instructions are used heavily by the
	   68881/68882 mathematics coprocessors for the 68020/68030, and the
	   68040 is effectively a 68030/68882 combination on one chip. So for
	   higher 680x0 processors, treat LINEF with care. See Motorola docu-
	   mentation for more information.

	9) LINK/UNLK make recursive code simpler to write than on other pro-
	   cessors. Exercise care with extraneous returns! If using so-called
	   "married" recursive functions, ensure that there are no 'secret
	   back-door exits' that bypass the stack cleaning routines!


			68000 - The Instructions
			========================


ABCD	: Add Decimal With Extend.

	Operation : src(10) + dst(10) + X -> dst

	Assembler :	ABCD	Dy,Dx

			ABCD	-(Ay),-(Ax)

	Attributes:size=Byte

	Description	: Perform Binary Coded Decimal (BCD) addition of
			  the source and destination operands, together
			  with the Extend (X) bit of the CCR. The only
			  legal addressing modes are those given above.
			  This is a byte operation only.

	Condition Codes	:	X N Z V C
				* U * U *

				N Undefined
				V Undefined
				Z Cleared if nonzero result.
				  UNCHANGED otherwise!
				C Set if DECIMAL carry generated.
				  Cleared otherwise.
				X Set identically to C.

	Notes		: Normally, the Z bit is set via programming
			  (this is the PROGRAMMER'S responsibility)
			  before the start of an ABCD operation. This
			  allows successful tests upon completion of
			  multiple-precision ABCD operations.

	Instruction Format:

		1 1 0 0 X X X 1 0 0 0 0 M Y Y Y

	Instruction Fields:

		XXX : Register Rx field. Specifies which register
			is used for the destination operand, D0-D7
			for ABCD Dy,Dx or A0-A7 for ABCD -(Ay),-(Ax)

		YYY : Register Ry field. Specifies which register
			is used for the source operand, D0-D7
			for ABCD Dy,Dx or A0-A7 for ABCD -(Ay),-(Ax)

		M   : R/M field. Specifies addressing mode.
			0 : mode is ABCD Dy,Dx
			1 : mode is ABCD -(Ay),-(Ax)


ADD	: Add Binary.

	Operation : src + dst -> dst

	Assembler : ADD <ea>,Dn

		    ADD Dn,<ea>

	Attributes:size=Byte,Word,Long

	Description	: Add the source operand to the destination
			  operand, and store the result in the dest-
			  ination operand. The operation may be spec-
			  ified to be byte, word or long in size. The
			  mode of the instruction indicates which is
			  the source and which is the destination
			  operand.

	Condition Codes :	X N Z V C
				* * * * *

				N Set if result negative when treated as
				  2's complement. Cleared otherwise.
				Z Set if result is zero. Cleared otherwise.
				V Set if an overflow is generated. Cleared
				  otherwise.
				C Set if a binary carry is generated.
				  Cleared otherwise.
				X Set identically to C.

	Instruction Format :

		1 1 0 1 R R R M M M E E E A A A

	Instruction Fields :

		RRR : Register field. Specifies any data register
			D0-D7.

		MMM : Op-Mode field. Specifies operation type in
			accordance with the table:

			  Byte	Word  Long	   Operation
			  ----	----  ----	   ---------
			  000	001   010	  ADD <ea>,Dn
			  100	101   110	  ADD Dn,<ea>

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The legal modes are:

		Source <ea> : All addressing modes.

		Destination <ea> : The following are ILLEGAL addressing
					modes:

					An
					offset(PC)
					offset(PC,Xn)
					#nnn

				   All others are legal.

		Notes		: 1) If the destination is a data register,
				  then the ADD <ea>,Dn form of the instruc-
				  tion MUST be used.

				  2) ADDA is used for ADD <ea>,An. ADDI is
				  used for ADD #nnn,<ea> where <ea> is not
				  a data register. ADDQ is also used for
				  ADD #nnn,<ea> when possible. Most 68000
				  assemblers can automatically make this
				  distinction.


ADDA	: Add Address

	Operation : src + dst -> dst

	Assembler : ADDA  <ea>,An

	Attributes:size=Word,Long

	Description	: Add the source operand to the destination
			  address register, and store the result in
			  the destination address register. The size
			  of the operation may be specified to be a
			  word or long operation.

			  NOTE:All address arithmetic on address
			  registers is performed using the ENTIRE
			  32 bits of the address register. Word
			  operands are sign-extended to 32 bits
			  before adding.

	Condition Codes : NOT AFFECTED.

	Instruction Format :

		1 1 0 1 R R R M M M E E E A A A

	Instruction Fields :

		RRR : Specifies one of the address registers A0-A7.
			This is ALWAYS the destination operand.

		MMM : Op-Mode field. Specifies the size of the
			operation.

			011 : Word operation. See NOTE above.

			111 : Long operation.

		EEE and AAA fields. Defined in addressing mode section
		below. All legal 68000 addressing modes are allowed for
		the source operand.


ADDI	: Add Immediate Operand

	Operation : immediate data + dst -> dst

	Assembler : ADDI  #nnnn,<ea>

	Attributes:size=Byte,Word,Long

	Description	: Add the immediate data contained in the
			  instruction to the destination operand,
			  and store the result in the destination
			  location.

			  NOTE:The contents of the immediate operand
			  part of the instruction is as follows:

			  Byte : 2nd word of operand, upper byte zero.

			  Word : 2nd word of operand.

			  Long : 2nd and 3rd word of operand.

			  Extension words for complex addressing modes
			  follows the immediate operand.

	Condition Codes :	X N Z V C
				* * * * *

				N Set if result negative when treated as
				  2's complement. Cleared otherwise.
				Z Set if result is zero. Cleared otherwise.
				V Set if an overflow is generated. Cleared
				  otherwise.
				C Set if a binary carry is generated.
				  Cleared otherwise.
				X Set identically to C.

	Instruction Format :

		0 0 0 0 0 1 1 0 S S E E E A A A

		W W W W W W W W B B B B B B B B

		L L L L L L L L L L L L L L L L

	Instruction Fields :

		SS	: Size field. Specifies operation size.

			  00 = byte operation

			  01 = word operation

			  10 = long operation

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL modes are:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L

		BBB...	: Byte immediate data field. The immediate
			  data is contained here. The WWW... field
			  is set to zero (00000000 binary) and the
			  LLL... field does not exist.

		WWW...	: Word immediate data field. The immediate
			  data occupies both WWW... and BBB... fields.
			  The LLL... field does not exist.

		LLL...	: Long immediate data field. The immediate
			  data occupies all BBB, WWW and LLL fields,
			  and the long word is divided as follows:

				WWW...BBB...	HIGH word of data
				LLL...		LOW word of data


ADDQ	: Add Immediate Quick Operand

	Operation : immediate data + dst -> dst

	Assembler : ADDQ  #nnnn,<ea>

	Attributes:size=Byte,Word,Long

	Description	: Add the immediate data contained in the
			  instruction to the destination operand,
			  and store the result in the destination
			  location. The range of values for the
			  immediate operand is 1 to 8, represented
			  in the instruction by 0 to 7 (0 repre-
			  senting a value of 8). The immediate data
			  is automatically coerced to the operation
			  size by the 68000.

	Condition Codes :	X N Z V C
				* * * * *

				N Set if result negative when treated as
				  2's complement. Cleared otherwise.
				Z Set if result is zero. Cleared otherwise.
				V Set if an overflow is generated. Cleared
				  otherwise.
				C Set if a binary carry is generated.
				  Cleared otherwise.
				X Set identically to C.

			  NOTE : Condition codes NOT AFFECTED if addition
				 destination is an address register!

	Instruction Format :

		0 1 0 1 D D D 0 S S E E E A A A

	Instruction Fields :

		DDD	: Data field. 3 bits of immediate data,
			  0 representing a value of 8, 1-7 repre-
			  senting those values repsectively.

		SS	: Size field. Specifies operation size.

			  00 = byte operation

			  01 = word operation

			  10 = long operation

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL modes are:

				Dn
				An (Word and Long only)
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L


ADDX	: Add With Extend

	Operation : src + dst + X -> dst

	Assembler : ADDX  Dy,Dx
		    ADDX -(Ay),-(Ax)

	Attributes:size=Byte,Word,Long

	Description	: Add the source operand to the destination
			  operand, along with the extend bit, and
			  store the result in the destination loca-
			  tion.

	Condition Codes :	X N Z V C
				* * * * *

				N Set if result negative when treated as
				  2's complement. Cleared otherwise.
				Z Cleared if result is non-zero.
				  Unchanged otherwise.
				V Set if an overflow is generated. Cleared
				  otherwise.
				C Set if a binary carry is generated.
				  Cleared otherwise.
				X Set identically to C.

			NOTE : Normally the Z bit is set via programming
				(e.g., using MOVEQ #0,D0) before the start
				of the operation. This allows successful
				tests for zero operands upon completion of
				multiple-precision operations.

	Instruction Format :

		1 1 0 1 X X X 1 S S 0 0 R Y Y Y

	Instruction Fields :

		XXX	: Register Rx field. Specifies the destination
			  register, depending upon R field.

		SS	: Size field. Specifies operation size.

			  00 = byte operation

			  01 = word operation

			  10 = long operation

		R	: R/M field, specifies operation addressing mode.
			  0 : operation is ADDX Dy,Dx, and XXX,YYY
				fields specify data registers.

			  1 : Operation is ADDX -(Ay),-(Ax), and XXX,YYY
				fields specify address registers.

		YYY	: Register Ry field. Specifies the source
			  register, depending upon R field.


AND	: Logical AND operation

	Operation : src AND dst -> dst

	Assembler : AND	<ea>,Dn
		    AND	Dn,<ea>

	Attributes:size=Byte,Word,Long

	Description	: Logically (bitwise) AND the source operand
			  with the destination operand, and store the
			  result in the destination location.

	Condition Codes :	X N Z V C
				- * * 0 0

				N Set if result negative when treated as
				  2's complement. Cleared otherwise.
				Z Set if result is zero. Cleared otherwise.
				V Always Cleared.
				C Always Cleared.
				X Not affected.

	Instruction Format :

		1 1 0 0 R R R M M M E E E A A A

	Instruction Fields :

		RRR	: Register field. Specifies any of the
			  8 data registers.

		MMM	: Op-Mode field. Specifies operation
			  according to:

			  Byte	Word  Long	   Operation
			  ----	----  ----	   ---------
			  000	001   010	  AND <ea>,Dn
			  100	101   110	  AND Dn,<ea>

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL modes are:

		Source Operand:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L
				d(PC)
				d(PC,Xi)
				#nnnn

		Destination Operand:

				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L

		NOTES : 1) If the destination is a data register, then
			   it CANNOT be specified using destination <ea>
			   addressing mode, but MUST use the destination
			   Dn mode above instead.

			2) ANDI is used when the source is immediate data.
			   Most assemblers automatically make this distinc-
			   tion.

ANDI	: Logical AND immediate

	Operation : immediate data AND dst -> dst

	Assembler : ANDI  #nnnn,<ea>

	Attributes:size=Byte,Word,Long

	Description	: Logically (Bitwise) AND the immediate data
			  contained in the instruction to the destin-
			  ation operand, and store the result in the
			  destination location.

			  NOTE:The contents of the immediate operand
			  part of the instruction is as follows:

			  Byte : 2nd word of operand, upper byte zero.

			  Word : 2nd word of operand.

			  Long : 2nd and 3rd word of operand.

			  Extension words for complex addressing modes
			  follows the immediate operand.

	Condition Codes :	X N Z V C
				- * * 0 0

				N Set if the most significant bit of the
				  result is set. Cleared otherwise.
				Z Set if the result is zero.
				  Cleared otherwise.
				V Always Cleared.
				C Always Cleared.
				X Not Affected.

	Instruction Format :

		0 0 0 0 0 0 1 0 S S E E E A A A

		W W W W W W W W B B B B B B B B

		L L L L L L L L L L L L L L L L

	Instruction Fields :

		SS	: Size field. Specifies the size of the operation.

			  00 = Byte operation.

			  01 = Word operation.

			  10 = Long operation.

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL modes are:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L

		BBB...	: Byte immediate data field. The immediate
			  data is contained here. The WWW... field
			  is set to zero (00000000 binary) and the
			  LLL... field does not exist.

		WWW...	: Word immediate data field. The immediate
			  data occupies both WWW... and BBB... fields.
			  The LLL... field does not exist.

		LLL...	: Long immediate data field. The immediate
			  data occupies all BBB, WWW and LLL fields,
			  and the long word is divided as follows:

				WWW...BBB...	HIGH word of data
				LLL...		LOW word of data


ANDI	: Logical AND immediate to CCR

	Operation : immediate data AND CCR -> CCR

	Assembler : ANDI  #nnnn,CCR

	Attributes:size=Byte

	Description	: Logically (Bitwise) AND the immediate data
			  contained in the instruction to the contents
			  of the Condition Code Register, and store the
			  result in the Condition Code Register (low 8
			  bits of Status Register).

			  NOTE:The contents of the immediate operand
			  part of the instruction is as follows:

			  Byte : 2nd word of operand, upper byte zero.

			  Extension words for complex addressing modes
			  follows the immediate operand.

	Condition Codes :	X N Z V C
				* * * * *

				N Cleared if Bit 3 of the operand is zero.
				  Unchanged otherwise.
				Z Cleared if Bit 2 of the operand is zero.
				  Unchanged otherwise.
				V Cleared if Bit 1 of the operand is zero.
				  Unchanged otherwise.
				C Cleared if Bit 0 of the operand is zero.
				  Unchanged otherwise.
				X Cleared if Bit 4 of the operand is zero.
				  Unchanged otherwise.

	Instruction Format :

		0 0 0 0 0 0 1 0 0 0 1 1 1 1 0 0

		0 0 0 0 0 0 0 0 B B B B B B B B

	Instruction Fields:

		BBB...	:	Byte data instruction field. The
				immediate data is contained in
				this field.


ANDI	: Logical AND immediate to SR (PRIVILEGED INSTRUCTION)

	Operation : If 68000 in supervisor state
			THEN
				immediate data AND SR -> SR
			ELSE
				TRAP EXCEPTION (PRIVILEGE VIOLATION)

	Assembler : ANDI  #nnnn,SR

	Attributes:size=Word

	Description	: Logically (Bitwise) AND the immediate data
			  contained in the instruction to the contents
			  of the Status Register, and store the result
			  in the Status Register.

			  NOTE:The contents of the immediate operand
			  part of the instruction is as follows:

			  Word : 2nd word of operand.

			  Extension words for complex addressing modes
			  follows the immediate operand.

	Condition Codes :	X N Z V C
				* * * * *

				N Cleared if Bit 3 of the operand is zero.
				  Unchanged otherwise.
				Z Cleared if Bit 2 of the operand is zero.
				  Unchanged otherwise.
				V Cleared if Bit 1 of the operand is zero.
				  Unchanged otherwise.
				C Cleared if Bit 0 of the operand is zero.
				  Unchanged otherwise.
				X Cleared if Bit 4 of the operand is zero.
				  Unchanged otherwise.

	Instruction Format :

		0 0 0 0 0 0 1 0 0 1 1 1 1 1 0 0

		W W W W W W W W W W W W W W W W

	Instruction Fields:

		WWW...	:	Word data instruction field. The
				immediate data is contained in
				this field.


ASL,ASR	: Arithmetic Shift

	Operation : dst (shifted by count) -> dst

	Assembler : ASd	Dx,Dy
		    ASd #nnnn,Dy
		    ASd <ea>

	Attributes:size=Byte,Word,Long

	Description	: Arithmetically shift the bits of the destination
			  operand in the direction specified. The carry bit
			  receives the last bit shifted out of the operand.
			  The shift count for the operation can be specified
			  in two ways:

			  1) Immediate. The shift count value is 1-8.

			  2) Data Register. The value contained in the
				specified data register, modulo 64, is
				used.

			  If the destination operand is a memory operand,
			  then the shift count is ALWAYS 1, and the operand
			  size is ALWAYS word sized.

			  ASL : Operand is shifted left by the value of the
				shift count. Bits shifted out of the high
				order bit are copied to the C and X bits of
				the CCR. V bit indicates sign changes during
				the operation.

			  ASR : Operand is shifted right by the value of the
				shift count. Bits shifted out of the low order
				bit are copied to the C and X bit of the CCR.
				The sign bit (high-order bit) is replicated
				into the now vacant high-order bits.

	Condition Codes :	X N Z V C
				* * * * *

				N Set if result negative when treated as
				  2's complement. Cleared otherwise.
				Z Set if result is zero. Cleared otherwise.
				V Set if most significant bit is changed
				  at any time during the operation. Cleared
				  otherwise.
				C Set according to the last bit shifted out
				  of the operation. Cleared for a shift count
				  of zero.
				X Set according to the last bit shifted out
				  of the operand. UNAFFECTED for a shift
				  count of zero!

	Instruction Format (Register Shifts) :

		1 1 1 0 C C C D S S L 0 0 R R R

	Instruction Fields :

		CCC	: Count/Register field. If immediate count,
			  CCC = 1-7 for a shift count of 7, 0 for a
			  shift count of 8. If data register count,
			  CCC = data register number for register Dx.
			  The value contained in bits 0-5 of Dx is
			  used as the shift count (i.e., Dx modulo
			  64).

		D	: Direction field. Specifies shift direction.

			  0 = right shift

			  1 = left shift

		SS	: Size field. Specifies the size of the operation.

			  00 = Byte operation.

			  01 = Word operation.

			  10 = Long operation.

		L	: L/R field. Specifies shift count type.

			  0 = immediate shift count in CCC field.

			  1 = data register count, register in CCC field.

		RRR	: Register field. Specifies any of the 8 data
			  registers whose content is to be shifted.

	Instruction Format (Memory Shifts) :

		1 1 1 0 0 0 0 D 1 1 E E E A A A

	Instruction Fields :

		D	: Direction field. Specifies shift direction.

			  0 = right shift

			  1 = left shift

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL modes are:

				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L


Bcc	: Branch Conditionally (Also Including BRA)

	Operation : IF condition is TRUE
			THEN
			  PC + d -> PC
			ELSE
			  continue normal sequential operation

	Assembler : Bcc <LABEL>

	Attributes:size=Byte,Word

	Description	: The conditional expression specified in the
			  instruction is evaluated and the result tested.
			  If the result is TRUE, the displacement is
			  sign-extended to 32 bits and added onto the
			  current value of the program counter, at which
			  point program execution continues. If the res-
			  ult is FALSE, program execution continues sequ-
			  entially as normal.

	Possible Instructions (U = unsigned test, S=signed test) :

		BT	Branch if True (Also BRA, Branch Always)
		BF	Branch if False (DOES NOT EXIST:SEE BSR)
		BHI	Branch if Higher		(U)
		BLS	Branch if Lower or Same 	(U)
		BCC	Branch on Carry Clear		(U)
		BCS	Branch on Carry Set		(U)
		BNE	Branch if Not Equal (to Zero)	(U and S)
		BEQ	Branch if Equal (to Zero)	(U and S)
		BVC	Branch if Overflow Clear
		BVS	Branch if Overflow Set
		BPL	Branch if Result Plus (N Clear)
		BMI	Branch if Result Minus (N Set)
		BGE	Branch if Greater Or Equal (to Zero?)	(S)
		BLT	Branch if Less Than (Zero?)		(S)
		BGT	Branch if Greater Than (Zero?)		(S)
		BLE	Branch if Less Than or Equal (to Zero?)	(S)

		Synonyms supported by some assemblers include:

		BHS (Branch if Higher Than or Same) for BCC	(U)
		BLO (Branch if Lower Than) for BCS		(U)

		Also (Not Approved By Motorola) :

		BBS (Branch on Bit Set) for BNE
		BBC (Branch on Bit Clear) for BEQ

	Condition Codes	: NOT AFFECTED.

	Instruction Format :

		0 1 1 0 C C C C D D D D D D D D

		16-bit 2s complement displacement extension
		word follows if DDDD... field is zero.

	Instruction Fields :

		CCCC	: Condition field. Specifies the conditional
			  expression to compute prior to the branch
			  decision. Values are given in the condition-
			  al branch table at the end of this file.

		DDDD..	: Displacement field. For short (Bcc.S) branch
			  instructions, this field contains the signed
			  (2s complement) 8-bit displacement to be added
			  onto the PC if the branch condition holds true.

			  For word-sized displacements, the DDDD... field
			  is zero, and the 16-bit signed (2s complement)
			  displacement follows the Bcc instruction word
			  as an extension word. This extension word ONLY
			  exists if the DDDD... field is zero.

		NOTE : A short branch to the instruction immediately follow-
			ing the Bcc instruction CANNOT exist. This is because
			the resulting short branch would be zero, and the
			68000 would treat this as a signal to access the next
			program word as a displacement for a word-sized cond-
			itional branch. This would possibly result in an add-
			ress error exception caused by the next instruction
			word being odd, and the resulting PC value upon the
			branch execution being odd. Most assemblers issue a
			warning about such branches.


BCHG	: Test Bit And Change

	Operation : NOT ( dst{N} ) -> Z
		    NOT ( dst{N} ) -> dst{N}

	Assembler : BCHG Dn,<ea>
		    BCHG #nnnn,<ea>

	Attributes:size=Byte,Long

	Description	: Copy a bit of the destination operand into 2
			  temporary locations within the 68000 ALU.
			  invert copy 1, and write the result to the Z
			  bit of the CCR. Then invert copy 2, and write
			  the result back into the bit position of the
			  destination whence it originated, thus changing
			  the value of the desired bit.

			  If a data register is the destination, then the
			  operation is a LONG operation, and the bit pos-
			  ition is treated as a modulo 32 value, allowing
			  access to all bits of the register.

			  If a memory operand is the destination, then the
			  operation is a BYTE operation, and the bit pos-
			  ition is treated as a modulo 8 value, allowing
			  access to all 8 bits of the BYTE addressed oper-
			  and.

	Condition Codes :	X N Z V C
				- - * - -

				N Not Affected.
				Z Set if the bit tested is ZERO.
				  Cleared otherwise.
				V Not Affected.
				C Not Affected.
				X Not affected.

	Instruction Format (Bit Number in Data Register) :

		0 0 0 0 R R R 1 0 1 E E E A A A

	Instruction Fields :

		RRR	: Register field. Specifies any of the
			  8 data registers from which the bit
			  position is extracted.

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL modes are:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L

	Instruction Format (Bit Number Immediate) :

		0 0 0 0 1 0 0 0 0 1 E E E A A A

		Extension Word, Bit Position as Immediate Data

	Instruction Fields :

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL modes are:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L


BCLR	: Test Bit And Clear

	Operation : NOT ( dst{N} ) -> Z
		    0 -> dst{N}

	Assembler : BCLR Dn,<ea>
		    BCLR #nnnn,<ea>

	Attributes:size=Byte,Long

	Description	: Copy a bit of the destination operand into 2
			  temporary locations within the 68000 ALU.
			  invert copy 1, and write the result to the Z
			  bit of the CCR. Then clear copy 2, and write
			  the result back into the bit position of the
			  destination whence it originated, thus clear-
			  ing the desired bit.

			  If a data register is the destination, then the
			  operation is a LONG operation, and the bit pos-
			  ition is treated as a modulo 32 value, allowing
			  access to all bits of the register.

			  If a memory operand is the destination, then the
			  operation is a BYTE operation, and the bit pos-
			  ition is treated as a modulo 8 value, allowing
			  access to all 8 bits of the BYTE addressed oper-
			  and.

	Condition Codes :	X N Z V C
				- - * - -

				N Not Affected.
				Z Set if the bit tested is ZERO.
				  Cleared otherwise.
				V Not Affected.
				C Not Affected.
				X Not affected.

	Instruction Format (Bit Number in Data Register) :

		0 0 0 0 R R R 1 1 0 E E E A A A

	Instruction Fields :

		RRR	: Register field. Specifies any of the
			  8 data registers from which the bit
			  position is extracted.

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL modes are:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L

	Instruction Format (Bit Number Immediate) :

		0 0 0 0 1 0 0 0 1 0 E E E A A A

		Extension Word, Bit Position as Immediate Data

	Instruction Fields :

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL modes are:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L


BKPT	: Breakpoint Instruction (68010)

	Operation : Acknowledge breakpoint, then TRAP via
		    illegal instruction exception.

	Assembler : BKPT #<data>

	Attributes:Unsized

	Description	: This instruction causes the 68010 to run a
			  breakpoint acknowledge cycle, with zeros on
			  all address lines. Following the termination
			  of the breakpoint acknowledge cycle, the
			  processor then TRAPS via the illegal instruc-
			  tion exception.

			  This instruction provides hardware support for
			  debug monitors and real-time software emulators.
			  The exact operation of this instruction will be
			  implementation dependent.

	Condition Codes	: NOT AFFECTED.

	Instruction Format :

		0 1 0 0 1 0 0 0 0 1 0 0 1 V V V

	Instruction Fields :

		VVV	: Vector field. Specifies the breakpoint
			  number. This can be used by various im-
			  plementations to cause different funct-
			  ions to be executed for different break-
			  point types.


BRA	: Branch Always. See Bcc Above.


BSET	: Test Bit And Set

	Operation : NOT ( dst{N} ) -> Z
		    1 -> dst{N}

	Assembler : BSET Dn,<ea>
		    BSET #nnnn,<ea>

	Attributes:size=Byte,Long

	Description	: Copy a bit of the destination operand into 2
			  temporary locations within the 68000 ALU.
			  invert copy 1, and write the result to the Z
			  bit of the CCR. Then set copy 2, and write
			  the result back into the bit position of the
			  destination whence it originated, thus set-
			  ting the desired bit.

			  If a data register is the destination, then the
			  operation is a LONG operation, and the bit pos-
			  ition is treated as a modulo 32 value, allowing
			  access to all bits of the register.

			  If a memory operand is the destination, then the
			  operation is a BYTE operation, and the bit pos-
			  ition is treated as a modulo 8 value, allowing
			  access to all 8 bits of the BYTE addressed oper-
			  and.

	Condition Codes :	X N Z V C
				- - * - -

				N Not Affected.
				Z Set if the bit tested is ZERO.
				  Cleared otherwise.
				V Not Affected.
				C Not Affected.
				X Not affected.

	Instruction Format (Bit Number in Data Register) :

		0 0 0 0 R R R 1 1 1 E E E A A A

	Instruction Fields :

		RRR	: Register field. Specifies any of the
			  8 data registers from which the bit
			  position is extracted.

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL modes are:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L

	Instruction Format (Bit Number Immediate) :

		0 0 0 0 1 0 0 0 1 1 E E E A A A

		Extension Word, Bit Position as Immediate Data

	Instruction Fields :

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL modes are:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L

BSR	: Branch to Subroutine

	Operation : PC -> -(SP) ; PC + d -> PC

	Assembler : BSR <label>

	Attributes:size=Byte,Word

	Description	: The long word address of the instruction that
			  immediately follows the BSR instruction is
			  pushed onto the system stack. The 2s complement
			  displacement part of the instruction is then
			  sign-extended to 32 bits, and added onto the
			  program counter.

	Condition Codes : NOT AFFECTED.

	Instruction Format :

		0 1 1 0 0 0 0 1 D D D D D D D D

		16-bit 2s complement displacement word follows
		if DDDD... field is zero.

	Instruction Fields :

		DDDD...	: 8-bit displacement field for short branch
			  (BSR.S). For 16-bit word-sized displacements
			  contained in an extension word, the DDDD...
			  field is zero.

	NOTE : A short branch to the instruction immediately following
		the BSR instruction CANNOT exist. This is because the
		displacement is zero. A zero short displacement would
		instruct the 68000 to treat the next instruction as a
		word displacement for the BSR instruction, and if the
		instruction word thus fetched was odd, would result in
		an address error exception immediately after execution.


BTST	: Test Bit

	Operation : NOT ( dst{N} ) -> Z

	Assembler : BTST Dn,<ea>
		    BTST #nnnn,<ea>

	Attributes:size=Byte,Long

	Description	: Copy a bit of the destination operand into a
			  temporary location within the 68000 ALU.
			  invert the copy, and write the result to the Z
			  bit of the CCR.

			  If a data register is the destination, then the
			  operation is a LONG operation, and the bit pos-
			  ition is treated as a modulo 32 value, allowing
			  access to all bits of the register.

			  If a memory operand is the destination, then the
			  operation is a BYTE operation, and the bit pos-
			  ition is treated as a modulo 8 value, allowing
			  access to all 8 bits of the BYTE addressed oper-
			  and.

	Condition Codes :	X N Z V C
				- - * - -

				N Not Affected.
				Z Set if the bit tested is ZERO.
				  Cleared otherwise.
				V Not Affected.
				C Not Affected.
				X Not affected.

	Instruction Format (Bit Number in Data Register) :

		0 0 0 0 R R R 1 0 0 E E E A A A

	Instruction Fields :

		RRR	: Register field. Specifies any of the
			  8 data registers from which the bit
			  position is extracted.

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL modes are:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L
				d(PC)
				d(PC,Xi)

	Instruction Format (Bit Number Immediate) :

		0 0 0 0 1 0 0 0 0 0 E E E A A A

		Extension Word, Bit Position as Immediate Data

	Instruction Fields :

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL modes are:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L
				d(PC)
				d(PC,Xi)


CHK	: Check Register Against Bounds

	Operation : IF Dn<0 or Dn > src
			THEN TRAP

	Assembler : CHK <ea>,Dn

	Attributes:size=Word

	Description	: The low order word of the specified data register
			  is examined and compared to the upper bound (which
			  is specified in the <ea> specification), treated
			  as a 2s complement integer. If the register value
			  is less than zero, or greater than the upper bound
			  contained in the source operand, then the 68000
			  takes the CHK exception. Otherwise, instruction
			  execution proceeds normally.

	Condition Codes	:	X N Z V C
				- * U U U

				N Set if Dn < 0,
				  Cleared if Dn > src,
				  Undefined otherwise.
				Z Undefined.
				V Undefined.
				C Undefined.
				X Not Affected.

	Instruction Format :

		0 1 0 0 R R R 1 1 0 E E E A A A

	Instruction Fields :

		RRR	: Register field. Specifies the data register
			  whose contents are checked.

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL addressing modes
		for CHK are:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L


CLR	: Clear an operand

	Operation : 0 -> dst

	Assembler : CLR <ea>

	Attributes:size=Byte,Word,Long

	Description	: The destination is cleared to all zero bits.
			  The size of the operation may by byte, word
			  or long.

	Condition Codes	:	X N Z V C
				- 0 1 0 0

				N Always Cleared.
				Z Always Set.
				V Always Cleared.
				C Always Cleared.
				X Not Affected.

	Instruction Format :

		0 1 0 0 0 0 1 0 S S E E E A A A

	Instruction Fields :

		SS	: Size field. Determines the size of the operation.

			  00 = Byte operation.

			  01 = Word operation.

			  10 = Long operation.

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes.The LEGAL addressing modes
		for CLR are:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L


CMP	: Compare

	Operation : dst - src -> CCR (set condition code bits only)

	Assembler : CMP <ea>,Dn

	Attributes:size=Byte,Word,Long

	Description	: Subtract the source operand from the destination
			  operand, but set the condition codes only. The
			  destination operand is NOT changed. The size of
			  the operand may be byte, word or long.

	Condition Codes	:	X N Z V C
				- * * * *

				N Set if the result is negative.
				  Cleared otherwise.
				Z Set if the result is zero.
				  Cleared otherwise.
				V Set if an overflow is generated.
				  Cleared otherwise.
				C Set if a borrow is generated.
				  Cleared otherwise.
				X Not Affected.

	Instruction Format :

		1 0 1 1 R R R M M M E E E A A A

	Instruction Fields :

		RRR	: Register field. Specifies the destination
			  data register.

		MMM	: Op-mode field. Defined according to:

			  Byte	Word  Long	Operation
			  ----	----  ----	---------
			  000	001   010	Dn - <ea>

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. All possible 68000 add-
		ressing modes are legal for source operands.

		NOTE : CMP An,Dn can only be either Word or Long.
			CMPA is used when the destination is an
			address register. CMPI is used when the
			source is an immediate operand. CMPM is
			used for memory to memory comparisons.
			Most assemblers automatically make this
			distinction.


CMPA	: Compare Address.

	Operation : dst - src -> CCR (set condition code bits only)

	Assembler : CMPA <ea>,An

	Attributes:size=Word,Long

	Description	: Subtract the source operand from the destination
			  operand, but set the condition codes only. The
			  destination operand is NOT changed. The size of
			  the operand may be word or long.

			  NOTE : All Word sized operands are sign extended
				 to 32 bits prior to the comparison oper-
				 ation.

	Condition Codes	:	X N Z V C
				- * * * *

				N Set if the result is negative.
				  Cleared otherwise.
				Z Set if the result is zero.
				  Cleared otherwise.
				V Set if an overflow is generated.
				  Cleared otherwise.
				C Set if a borrow is generated.
				  Cleared otherwise.
				X Not Affected.

	Instruction Format :

		1 0 1 1 R R R M M M E E E A A A

	Instruction Fields :

		RRR	: Register field. Specifies the destination
			  data register.

		MMM	: Op-mode field. Defined according to:

			  011 : Word operation. The source operand
				is sign extended to 32 bits and the
				operation performed upon the entire
				32 bits of the address register.

			  111 : Long operation.

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. All possible 68000 add-
		ressing modes are legal for source operands.


CMPI	: Compare Immediate

	Operation : dst - immediate data -> CCR
			(set condition code bits only)

	Assembler : CMPI #nnnn,<ea>

	Attributes:size=Byte,Word,Long

	Description	: Subtract the source operand from the destination
			  operand, but set the condition codes only. The
			  destination operand is NOT changed. The size of
			  the operand may be byte, word or long.

	Condition Codes	:	X N Z V C
				- * * * *

				N Set if the result is negative.
				  Cleared otherwise.
				Z Set if the result is zero.
				  Cleared otherwise.
				V Set if an overflow is generated.
				  Cleared otherwise.
				C Set if a borrow is generated.
				  Cleared otherwise.
				X Not Affected.

	Instruction Format :

		0 0 0 0 1 1 0 0 S S E E E A A A

		W W W W W W W W B B B B B B B B

		L L L L L L L L L L L L L L L L

	Instruction Fields :

		SS	: Size field. Specifies size of operation.

			  00 = Byte operation.

			  01 = Word operation.

			  10 = Long operation.

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. LEGAL addressing modes
		for the destination operand are:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L

		BBB...	: Byte immediate data field. The immediate
			  data is contained here. The WWW... field
			  is set to zero (00000000 binary) and the
			  LLL... field does not exist.

		WWW...	: Word immediate data field. The immediate
			  data occupies both WWW... and BBB... fields.
			  The LLL... field does not exist.

		LLL...	: Long immediate data field. The immediate
			  data occupies all BBB, WWW and LLL fields,
			  and the long word is divided as follows:

				WWW...BBB...	HIGH word of data
				LLL...		LOW word of data


CMPM	: Compare Memory

	Operation : dst - src -> CCR (set condition code bits only)

	Assembler : CMPM (Ay)+,(Ax)+

	Attributes:size=Byte,Word,Long

	Description	: Subtract the source operand from the destination
			  operand, but set the condition codes only. The
			  destination operand is NOT changed. The size of
			  the operand may be byte, word or long.

	Condition Codes	:	X N Z V C
				- * * * *

				N Set if the result is negative.
				  Cleared otherwise.
				Z Set if the result is zero.
				  Cleared otherwise.
				V Set if an overflow is generated.
				  Cleared otherwise.
				C Set if a borrow is generated.
				  Cleared otherwise.
				X Not Affected.

	Instruction Format :

		1 0 1 1 X X X 1 S S 0 0 1 Y Y Y

	Instruction Fields :

		XXX	: Register Rx field. ALWAYS specifies the
			  destination register. Specifies an address
			  register A0-A7.

		SS	: Size field. Specifies the size of the operation.

			  00 = Byte operation.

			  01 = Word operation.

			  10 = Long operation.

		YYY	: Register Ry field. ALWAYS specifies the
			  source register. Specifies an address
			  register A0-A7.


DBcc	: Test Condition, Decrement and Branch

	Operation : IF condition=FALSE
			THEN
			  Dn - 1 -> Dn
			  IF Dn <> -1
			    THEN
				PC + d -> PC
			    ELSE
				PC + 2 -> PC
			  END IF
			ELSE
		    	  PC + 2 -> PC
		     END IF


	Assembler : DBcc Dn, <label>

	Attributes:size=Word

	Description	: A complex loop control instruction. The sequence
			  of operations is:

			  1) Test condition. If condition is TRUE,
				fall through to next instruction.

			  2) If condition is FALSE, decrement the low
				word of the data register used as the
				counter.

			  3) If the resulting value of the counter is -1,
				fall through to next instruction.

			  4) If counter value is not -1, sign-extend the
				displacement to 32 bits, and add it onto
				the current value of the PC.

			  The instruction should be read as "Decrement &
			  Branch UNTIL condition (is true)", as this best
			  summarises the operating logic.

	Possible Instructions (S=signed test, U=unsigned test) :

		DBT	Until True
		DBF	Until False (Also written DBRA)
		DBHI	Until Higher			(U)
		DBLS	Until Lower or Same 		(U)
		DBCC	Until Carry Clear		(U)
		DBCS	Until Carry Set			(U)
		DBNE	Until Not Equal (to Zero)
		DBEQ	Until Equal (to Zero)
		DBVC	Until Overflow Clear
		DBVS	Until Overflow Set
		DBPL	Until Result Plus (N Clear)
		DBMI	Until Result Minus (N Set)
		DBGE	Until Greater Or Equal (to Zero?)	(S)
		DBLT	Until Less Than (Zero?)			(S)
		DBGT	Until Greater Than (Zero?)		(S)
		DBLE	Until Less Than or Equal (to Zero?)	(S)

		Synonyms supported by some assemblers include:

		BHS (Until Higher Than or Same) for BCC	(U)
		BLO (Until Lower Than) for BCS		(U)

	Condition Codes	: NOT AFFECTED.

	Instruction Format :

		0 1 0 1 C C C C 1 1 0 0 1 R R R

		16-bit 2s complement displacement follows as
		extension word.

	Instruction Fields :

		CCCC	: Condition specifier field. See table of
			  condition code specifiers at the end of
			  this file.

		RRR	: Register field. Specifies which data register
			  D0-D7 to use.

	NOTES : When no terminating condition is required for a loop,
		and the counter decrementing to -1 is the sole exit
		condition required (as in PASCAL 'FOR' loop, etc.)
		then DBF is used. Most assemblers allow the synonym
		DBRA to be used.

		Two methods of loop entry are available. Either the
		program can fall into the loop, in which case the
		loop will be executed N+1 times if the value of Dn
		upon entry is N, or the program can branch direct to
		the DBcc instruction, in which case, for a value of
		N in Dn, the loop will be executed N times. The latter
		method is preferred, as it exits consistently for a
		counter value of 0 analogously to a PASCAL 'FOR' loop,
		unless there are good reasons for using the former
		method.


DIVS	: Signed Divide

	Operation : dst / src -> dst

	Assembler : DIVS <ea>,Dn

	Attributes:size=Word

	Description	: 	Divide the 32-BIT destination operand by the
				16-BIT source operand, using SIGNED arith-
				metic, Generate a 32-bit result formed from
				two 16-bit quantities:

				Low Word  : Quotient resulting from the
					    division.

				High Word : Remainder resulting from the
					    division.

				and then store the result in the destination
				location.

				The sign of the remainder is always the same
				as the sign of the dividend unless the rem-
				ainder is zero. Two special conditions can
				arise:

				1) Division by zero initiates exception
				   processing. The 68000 takes the Division
				   By Zero exception.

				2) Overflow may be detected and set before
				   the completion of the instruction. If an
				   overflow is detected, the condition is
				   flagged, and the operands are unaffected.

	Condition Codes	:	X N Z V C
				- * * * 0

				N Set if the QUOTIENT is negative.
				  Cleared otherwise.
				Z Set if the QUOTIENT is zero.
				  Cleared otherwise.
				  Undefined if overflow detected.
				V Set if an overflow is generated.
				  Cleared otherwise.
				C Always Cleared.
				X Not Affected.

	Instruction Format :

		1 0 0 0 R R R 1 1 1 E E E A A A

	Instruction Fields :

		RRR	: Register field. Specifies the destination
			  data register D0-D7. This field ALWAYS
			  specifies the destination operand.

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. All possible 68000 add-
		ressing modes are legal for source operands EXCEPT
		address register direct (i.e., DIVS An,Dn is NOT
		allowed).

		NOTE : Overflow occurs if the QUOTIENT is larger
			than a 16-bit signed integer. So, for
			example, DIVS #10,D0 will generate an
			overflow if D0 contains a value greater
			than ±655,359 decimal.


DIVU	: Unsigned Divide

	Operation : dst / src -> dst

	Assembler : DIVU <ea>,Dn

	Attributes:size=Word

	Description	: 	Divide the 32-BIT destination operand by the
				16-BIT source operand, using UNSIGNED arith-
				metic, Generate a 32-bit result formed from
				two 16-bit quantities:

				Low Word  : Quotient resulting from the
					    division.

				High Word : Remainder resulting from the
					    division.

				and then store the result in the destination
				location.

				Two special conditions can arise:

				1) Division by zero initiates exception
				   processing. The 68000 takes the Division
				   By Zero exception.

				2) Overflow may be detected and set before
				   the completion of the instruction. If an
				   overflow is detected, the condition is
				   flagged, and the operands are unaffected.

	Condition Codes	:	X N Z V C
				- * * * 0

				N Set if the most significant bit of the
				  QUOTIENT is set. Cleared otherwise.
				Z Set if the QUOTIENT is zero.
				  Cleared otherwise.
				  Undefined if overflow detected.
				V Set if an overflow is generated.
				  Cleared otherwise.
				C Always Cleared.
				X Not Affected.

	Instruction Format :

		1 0 0 0 R R R 0 1 1 E E E A A A

	Instruction Fields :

		RRR	: Register field. Specifies the destination
			  data register D0-D7. This field ALWAYS
			  specifies the destination operand.

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. All possible 68000 add-
		ressing modes are legal for source operands EXCEPT
		address register direct (i.e., DIVU An,Dn is NOT
		allowed).

		NOTE : Overflow occurs if the QUOTIENT is larger
			than a 16-bit unsigned integer. So, for
			example, DIVS #10,D0 will generate an
			overflow if D0 contains a value greater
			than 655,359 decimal.


EOR	: Logical Exclusive-OR operation

	Operation : src EOR dst -> dst

	Assembler : EOR	Dn,<ea>

	Attributes:size=Byte,Word,Long

	Description	: Logically (bitwise) Exclusive-OR the source
			  operand with the destination operand, and
			  store the result in the destination location.
			  THIS OPERATION IS RESTRICTED TO DATA REGISTERS
			  AS THE SOURCE OPERAND! The destination operand
			  is specified in the effective address field.
			  The size of the operation may be specified to
			  be byte, word or long.

	Condition Codes :	X N Z V C
				- * * 0 0

				N Set if result negative when treated as
				  2's complement. Cleared otherwise.
				Z Set if result is zero. Cleared otherwise.
				V Always Cleared.
				C Always Cleared.
				X Not affected.

	Instruction Format :

		1 0 1 1 R R R M M M E E E A A A

	Instruction Fields :

		RRR	: Register field. Specifies any of the
			  8 data registers.

		MMM	: Op-Mode field. Specifies operation
			  according to:

			  Byte	Word  Long	   Operation
			  ----	----  ----	   ---------
			  100	101   110	  EOR Dn,<ea>

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL modes are (for
		the destination operand only):

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L

		NOTES : 1) Memory to data register operations are NOT
			   allowed with this binary form of the instruc-
			   tion. There are other binary forms, allowing
			   EOR of immediate data with data registers.
			   See NOTE 2 below and EORI instruction.

			2) EORI is used when the source is immediate data.
			   Most assemblers automatically make this distinc-
			   tion.


EORI	: Logical Exclusive-OR immediate

	Operation : immediate data EOR dst -> dst

	Assembler : EORI #nnnn,<ea>

	Attributes:size=Byte,Word,Long

	Description	: Logically (bitwise) Exclusive-OR the immediate
			  data with the destination operand, and store
			  the result in the destination location. The
			  size of the operand may be specified to be
			  byte, word or long. The immediate data matches
			  the operation size.

			  NOTE:The contents of the immediate operand
			  part of the instruction is as follows:

			  Byte : 2nd word of operand, upper byte zero.

			  Word : 2nd word of operand.

			  Long : 2nd and 3rd word of operand.

			  Extension words for complex addressing modes
			  follows the immediate operand.

	Condition Codes :	X N Z V C
				- * * 0 0

				N Set if result negative when treated as
				  2's complement. Cleared otherwise.
				Z Set if result is zero. Cleared otherwise.
				V Always Cleared.
				C Always Cleared.
				X Not affected.

	Instruction Format :

		0 0 0 0 1 0 1 0 S S E E E A A A

		W W W W W W W W B B B B B B B B

		L L L L L L L L L L L L L L L L

	Instruction Fields :

		SS	: Size field. Specifies the size of the operation.

			  00 = Byte operation.

			  01 = Word operation.

			  10 = Long operation.

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL modes are (for
		the destination operand only):

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L

		BBB...	: Byte immediate data field. The immediate
			  data is contained here. The WWW... field
			  is set to zero (00000000 binary) and the
			  LLL... field does not exist.

		WWW...	: Word immediate data field. The immediate
			  data occupies both WWW... and BBB... fields.
			  The LLL... field does not exist.

		LLL...	: Long immediate data field. The immediate
			  data occupies all BBB, WWW and LLL fields,
			  and the long word is divided as follows:

				WWW...BBB...	HIGH word of data
				LLL...		LOW word of data


EORI	: Exclusive OR immediate to Condition Code Register

	Operation : immediate data EOR CCR -> CCR

	Assembler : EORI #nnnn,CCR

	Attributes:size=Byte

	Description	: Logically (bitwise) Exclusive-OR the immediate
			  data with the contents of the Condition Code
			  Register, and store the result in the Condition
			  Code Register (low order byte of the Status Reg-
			  ister).

	Condition Codes :	X N Z V C
				* * * * *

				N Inverted if Bit 3 of immediate operand
				  is 1. Unchanged otherwise.
				Z Inverted if Bit 2 of immediate operand
				  is 1. Unchanged otherwise.
				V Inverted if Bit 2 of immediate operand
				  is 1. Unchanged otherwise.
				C Inverted if Bit 0 of immediate operand
				  is 1. Unchanged otherwise.
				X Inverted if Bit 4 of immediate operand
				  is 1. Unchanged otherwise.

	Instruction Format :

		0 0 0 0 1 0 1 0 0 0 1 1 1 1 0 0

		0 0 0 0 0 0 0 0 B B B B B B B B

	Instruction Fields :

		BBB..	:	Byte immediate data field. This field
				contains the 8-bit immediate data.


EORI	: Exclusive OR immediate to Status Register

	  (PRIVILEGED INSTRUCTION)

	Operation : IF 68000 in supervisor state
			THEN
				immediate data EOR SR -> SR
			ELSE
				TRAP EXCEPTION (PRIVILEGE VIOLATION)

	Assembler : EORI #nnnn,SR

	Attributes:size=Byte

	Description	: Logically (bitwise) Exclusive-OR the immediate
			  data with the contents of the Status Register,
			  and store the result in the Status Register.

	Condition Codes :	X N Z V C
				* * * * *

				N Inverted if Bit 3 of immediate operand
				  is 1. Unchanged otherwise.
				Z Inverted if Bit 2 of immediate operand
				  is 1. Unchanged otherwise.
				V Inverted if Bit 2 of immediate operand
				  is 1. Unchanged otherwise.
				C Inverted if Bit 0 of immediate operand
				  is 1. Unchanged otherwise.
				X Inverted if Bit 4 of immediate operand
				  is 1. Unchanged otherwise.

	Instruction Format :

		0 0 0 0 1 0 1 0 0 1 1 1 1 1 0 0

		W W W W W W W W W W W W W W W W

	Instruction Fields :

		WWW...	:	Word data instruction field. The
				immediate data is contained in
				this field.


EXG	: Exchange Registers

	Operation : Rx <-> Ry

	Assembler : EXG Ry,Rx

	Attributes:size=Long

	Description	: Exchange the contents of the two registers
			  specified. This exchange is ALWAYS a Long
			  operation (all 32 bits of the register are
			  exchanged). The exchange works in three
			  modes:

			  1) Data register to Data register.

			  2) Address register to Address register.

			  3) Data register to Address register.

	Condition Codes : NOT AFFECTED.

	Instruction Format :

		1 1 0 0 X X X 1 M M M M M Y Y Y

	Instruction Fields :

		XXX	: Register Rx field. Specifies a data
			  register or an address register de-
			  pending upon the mode. If the exchange
			  is between a data register and an
			  address register, this field ALWAYS
			  specifies the DATA register.

		MMMMM	: Op-Mode field. Specifies whether exchanging:

			  01000	: Data Registers.

			  01001 : Address Registers.

			  10001 : Data Register and Address Register.

		YYY	: Register Ry field. Specifies a data
			  register or an address register de-
			  pending upon the mode. If the exchange
			  is between a data register and an
			  address register, this field ALWAYS
			  specifies the ADDRESS register.


EXT	: Sign Extend

	Operation : dst.B -> dst.W

			or

		    dst.W -> dst.L

	Assembler : EXT Dn

	Attributes:size=Word,Long

	Description	: Take the sign bit of the operand, and copy the
			  value of this bit into higher bits of the operand
			  according to the size/attribute specification of
			  the instruction. If EXT.W is specified, take bit
			  7 of the operand, and copy its value into bits 8
			  to 15 (word-sized sign extension). If EXT.L is
			  specified, take bit 15 of the operand, anc copy
			  its value into bits 16-31 (long word sized sign
			  extension).

	Condition Codes	:	X N Z V C
				- * * 0 0

				N Set if the result is negative.
				  Cleared otherwise.
				Z Set if the result is zero.
				  Cleared otherwise.
				V Always Cleared.
				C always Cleared.
				X Not Affected.

	Instruction Format :

		0 1 0 0 1 0 0 M M M 0 0 0 R R R

	Instruction Fields :

		MMM	: Op-mode field. Defined according to:

			  010 : EXT.W (Sign extend byte to word)

			  011 : EXT.L (Sign extend word to longword)

		RRR	: Register field. Specifies the destination
			  data register.


ILLEGAL	: Illegal instruction

	Operation : PC -> -(SSP) ;
		    SR -> -(SSP) ;
		    (Illegal Instruction Vector) -> PC

	Assembler : ILLEGAL

		    or

		    DC.W $4AFC

	Attributes:none

	Description	: This bit pattern will ALWAYS generate an illegal
			  instruction exception on Motorola 680x0 processors.
			  All other bit patterns that currently result in an
			  illegal instruction exception on current proces-
			  sors are reserved for future extension of the in-
			  struction set on next-generation members of the
			  680x0 family.

	Condition Codes : NOT AFFECTED.

	Instruction Format :

		0 1 0 0 1 0 1 0 1 1 1 1 1 1 0 0


JMP	: Jump

	Operation : dst -> PC

	Assembler : JMP <ea>

	Attributes:Unsized

	Description	: Take the value of the destination operand
			  and load it into the program counter. Pro-
			  gram execution continues from this new ad-
			  dress onwards.

	Condition Codes	: NOT AFFECTED.

	Instruction Format :

		0 1 0 0 1 1 1 0 1 1 E E E A A A

	Instruction Fields :


		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values for the
		EEE/AAA fields is listed in the section describing
		the addressing modes. LEGAL addressing modes for
		JMP are:


				(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L
				d(PC)
				d(PC,Xi)


JSR	: Jump to subroutine

	Operation : PC -> -(SP)
		    dst -> PC

	Assembler : JSR <ea>

	Attributes:Unsized

	Description	: The long word address of the instruction
			  immediatedly following the JSR is pushed onto
			  the system stack. Program execution then
			  continues at the address specified in the
			  instruction.

	Condition Codes	: NOT AFFECTED.

	Instruction Format :

		0 1 0 0 1 1 1 0 1 0 E E E A A A

	Instruction Fields :


		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values for the
		EEE/AAA fields is listed in the section describing
		the addressing modes. LEGAL addressing modes for
		JSR are:


				(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L
				d(PC)
				d(PC,Xi)


LEA	: Load Effective Address

	Operation : dst -> An

	Assembler : LEA <ea>,An

	Attributes:size=Long

	Description	: The effective address itself, NOT its contents,
			  are copied into the specified address register.
			  All 32 bits of the address register ar affected
			  by this operation.

	Condition Codes	: NOT AFFECTED.

	Instruction Format :

		0 1 0 0  R R R 1 1 1  E E E A A A

	Instruction Fields :

		RRR	: Register field. Specifies the destination
			  address register.

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The possible LEGAL add-
		ressing modes for LEA are:

				(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L
				d(PC)
				d(PC,Xi)


LINK	: Link And Allocate Workspace

	Operation : An -> -(SP)
		    SP -> An
		    SP + d -> SP

	Assembler : LINK An,#<displacement>

	Attributes:Unsized

	Description	: The current contents of the specified address
			  register is pushed onto the stack. After the
			  push, the updated stack pointer contents are
			  loaded into the specified address register.
			  Finally, the 16-bit signed displacement is
			  added onto the stack pointer. The contents of
			  the address register occupies two words on the
			  stack. A positive displacement is used to
			  access parameters pushed onto the stack (as in
			  code generated by C compilers), and a negative
			  displacement reserves workspace for local var-
			  iables.

	Condition Codes	: NOT AFFECTED.

	Instruction Format :

		0 1 0 0 1 1 1 0 0 1 0 1 0 R R R

		D D D D D D D D D D D D D D D D

	Instruction Fields :

		RRR	: Register field. Specifies the destination
			  address register.

		DDD...	: Displacement field. Contains the 16-bit
			  value ot be sign-extended and added on to
			  the stack pointer.


LSL,LSR	: Logical Shift

	Operation : dst (shifted by count) -> dst

	Assembler : LSd	Dx,Dy
		    LSd #nnnn,Dy
		    LSd <ea>

	Attributes:size=Byte,Word,Long

	Description	: Logically shift the bits of the destination op-
			  erand in the direction specified. The carry bit
			  receives the last bit shifted out of the operand.
			  The shift count for the operation can be speci-
			  fied in two ways:

			  1) Immediate. The shift count value is 1-8.

			  2) Data Register. The value contained in the
				specified data register, modulo 64, is
				used.

			  If the destination operand is a memory operand,
			  then the shift count is ALWAYS 1, and the operand
			  size is ALWAYS word sized.

			  LSL : Operand is shifted left by the value of the
				shift count. Bits shifted out of the high
				order bit are copied to the C and X bits of
				the CCR. Zero bits are shifted into the va-
				cated low order bits.

			  LSR : Operand is shifted right by the value of the
				shift count. Bits shifted out of the low order
				bit are copied to the C and X bit of the CCR.
				Zero bits are shifted into the vacated high
				order bits.

	Condition Codes :	X N Z V C
				* * * 0 *

				N Set if result negative when treated as
				  2's complement. Cleared otherwise.
				Z Set if result is zero. Cleared otherwise.
				V Always Cleared.
				C Set according to the last bit shifted out
				  of the operation. Cleared for a shift count
				  of zero.
				X Set according to the last bit shifted out
				  of the operand. UNAFFECTED for a shift
				  count of zero!

	Instruction Format (Register Shifts) :

		1 1 1 0 C C C D S S L 0 1 R R R

	Instruction Fields :

		CCC	: Count/Register field. If immediate count,
			  CCC = 1-7 for a shift count of 7, 0 for a
			  shift count of 8. If data register count,
			  CCC = data regsiter number for register Dx.
			  The value contained in bits 0-5 of Dx is
			  used as the shift count (i.e., Dx modulo
			  64).

		D	: Direction field. Specifies shift direction.

			  0 = right shift

			  1 = left shift

		SS	: Size field. Specifies the size of the operation.

			  00 = Byte operation.

			  01 = Word operation.

			  10 = Long operation.

		L	: L/R field. Specifies shift count type.

			  0 = immediate shift count in CCC field.

			  1 = data register count, register in CCC field.

		RRR	: Register field. Specifies any of the 8 data
			  registers whose content is to be shifted.

	Instruction Format (Memory Shifts) :

		1 1 1 0 0 0 1 D 1 1 E E E A A A

	Instruction Fields :

		D	: Direction field. Specifies shift direction.

			  0 = right shift

			  1 = left shift

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL modes are:

				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L


MOVE	: Move Data From Source To Destination.

	Operation : src -> dst

	Assembler : MOVE <ea>,<ea>

	Attributes:size=Byte,Word,Long

	Description	: Move the contents of the source effective
			  address to the location specified by the
			  destination effective address. The data is
			  examined as it is moved, and the condition
			  codes set accordingly. The operation may be
			  specified to be a byte, word or long word
			  operation.

	Condition Codes	:	X N Z V C
				- * * 0 0

				N Set if the result is negative.
				  Cleared otherwise.
				Z Set if the result is zero.
				  Cleared otherwise.
				V Always Cleared.
				C Always Cleared.
				X Not Affected.

	Instruction Format :

		0 0 S S X X X M M M N N N Y Y Y

	Instruction Fields :

		SS	: Size field. Specifies the size of operand
			  to be moved.

				01 = Byte operation.
				11 = Word operation.
				10 = Long operation.

		XXX, MMM : Destination effective address field.
				See the Effective Address Specification
				section below for values, where MMM=EEE,
				XXX=AAA.

		YYY, NNN : Source effective address field.
				See the Effective Address Specification
				section below for values, where NNN=EEE,
				YYY=AAA

		The LEGAL addressing modes for this instruction are:

		Source Effective Address:All addressing modes (except
		for byte sized operation where destination is An).

		Destination Effective Address:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L

		NOTE : MOVEA is used when the destination is an address
			register. Most assemblers automatically make this
			distinction.

		       MOVEQ can also be used for loading certain immediate
			constant values into data registers.


MOVE	: Move Data From Condition Code Register to Destination
	  (68010 upwards - NOT 68000).

	Operation : CCR -> dst

	Assembler : MOVE CCR,<ea>

	Attributes:size=Word

	Description	: Move the contents of the status register to
			  the destination effective address. The source
			  operand is a word, but only the low order byte
			  contains the condition codes. The upper byte
			  is set to all zeros.

	Condition Codes	: NOT AFFECTED.

	Instruction Format :

		0 1 0 0 0 0 1 0 1 1 E E E A A A

	Instruction Fields :

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The possible LEGAL add-
		ressing modes for LEA are:

				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L

		NOTE : MOVE from CCR is a word operation.


MOVE	: Move Data From Source To Condition Code Register

	Operation : src -> CCR

	Assembler : MOVE <ea>,CCR

	Attributes:size=Word

	Description	: Move the contents of the soure effective ad-
			  dress to the condition code register. The
			  source operand is a word, but only the low
			  order byte is used to update the condition
			  codes. The upper byte is ignored.

	Condition Codes	: X N Z V C
			  * * * * *

			  N Set to the same value as bit 3 of the
			    source operand.
			  Z Set to the same value as bit 2 of the
			    source operand.
			  V Set to the same value as bit 1 of the
			    source operand.
			  C Set to the same value as bit 0 of the
			    source operand.
			  X Set to the same value as bit 4 of the
			    source operand.

	Instruction Format :

		0 1 0 0 0 1 0 0 1 1 E E E A A A

	Instruction Fields :

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. All addressing modes
		except address register direct are legal (i.e.,
		MOVE An,CCR is illegal).

		NOTE : MOVE to CCR is a word operation. AND, OR
			and EOR to CCR is a byte operation.


MOVE	: Move Data From Status Register to Destination
	  (68000 Version)

	Operation : SR -> dst

	Assembler : MOVE SR,<ea>

	Attributes:size=Word

	Description	: Move the contents of the status register to
			  the destination effective address. The source
			  operand is a word.

	Condition Codes	: NOT AFFECTED.

	Instruction Format :

		0 1 0 0 0 0 0 0 1 1 E E E A A A

	Instruction Fields :

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The possible LEGAL add-
		ressing modes for this instruction are:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L

		NOTE : A memory destination is READ before it is
			WRITTEN to.


MOVE	: Move Data From Status Register to Destination
	  (68010 Version - PRIVILEGED INSTRUCTION).

	Operation : If 68000 in supervisor state
			THEN
				SR -> dst
			ELSE
				TRAP EXCEPTION (PRIVILEGE VIOLATION)

	Assembler : MOVE SR,<ea>

	Attributes:size=Word

	Description	: Move the contents of the status register to
			  the destination effective address. The source
			  operand is a word.

	Condition Codes	: NOT AFFECTED.

	Instruction Format :

		0 1 0 0 0 0 0 0 1 1 E E E A A A

	Instruction Fields :

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The possible LEGAL add-
		ressing modes for this instruction are:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L

		NOTE : On 68010/68020 etc., use MOVE from CCR to
			access the condition codes.


MOVE	: Move Data From Source To Status Register
	  (PRIVILEGED INSTRUCTION)

	Operation : IF 68000 in supervisor state
			THEN
			    src -> SR
			ELSE
			    TRAP EXCEPTION (PRIVILEGE VIOLATION)


	Assembler : MOVE <ea>,SR

	Attributes:size=Word

	Description	: Move the contents of the soure effective ad-
			  dress to the status register. The operation
			  is word sized and all bits of the status
			  register are affected.

	Condition Codes	: X N Z V C
			  * * * * *

			  N Set to the same value as bit 3 of the
			    source operand.
			  Z Set to the same value as bit 2 of the
			    source operand.
			  V Set to the same value as bit 1 of the
			    source operand.
			  C Set to the same value as bit 0 of the
			    source operand.
			  X Set to the same value as bit 4 of the
			    source operand.

	Instruction Format :

		0 1 0 0 0 1 1 0 1 1 E E E A A A

	Instruction Fields :

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. All addressing modes
		except address register direct are legal (i.e.,
		MOVE An,CCR is illegal).


MOVE	: Move User Stack Pointer
	  (PRIVILEGED INSTRUCTION)

	Operation : IF 68000 in supervisor state
			THEN
			    USP -> An

				or

			    An -> USP
			ELSE
			    TRAP EXCEPTION (PRIVILEGE VIOLATION)


	Assembler : MOVE USP,An
		    MOVE An,USP

	Attributes:size=Long

	Description	: Transfer the contents of the User Stack Pointer
			  to or from the specified address register.

	Condition Codes	: NOT AFFECTED.

	Instruction Format :

		0 1 0 0 1 1 1 0 0 1 1 0 D R R R

	Instruction Fields :

		D	: Direction field. Specifies the direction
			  of transfer.

			  0 = MOVE An,USP

			  1 = MOVE USP,An

		RRR	: Register field. Specifies the address register
			  to move to/from.

MOVEA	: Move Address

	Operation : src -> An

	Assembler : MOVE <ea>,An

	Attributes:size=Word,Long

	Description	: Move the contents of the source effective address
			  to the speficied destination address register. If
			  a word sized operation is specified, the operand
			  is sign extended to a full 32-bit operand before
			  the transfer. All 32 bits of the destination ad-
			  dress register are affected by both word and long
			  sized operations.

	Condition Codes	: NOT AFFECTED.

	Instruction Format :

		0 0 S S R R R 0 0 1 E E E A A A

	Instruction Fields :

		SS	: Size field. Specifies the size of operand
			  to be moved.

				11 = Word operation. The source operand is
				     sign-extended to a long operand and all
				     32 bits are loaded into the address
				     register.
				10 = Long operation.

		RRR	: Destination Register field. Specifies the
			  destination address register to use.

		EEE	: Source Effective Address field.

		AAA	: Source Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. All addressing modes are
		legal.


MOVEC	: Move To/From Control Register (PRIVILEGED INSTRUCTION)
	  (68010 onwards-NOT 68000)

	Operation : If 68000 in supervisor state
			THEN
				Rc -> Rn
				   or
				Rn -> Rc
			ELSE
				TRAP EXCEPTION (PRIVILEGE VIOLATION)

	Assembler : MOVEC Rc,Rn
		    MOVEC Rn,Rc

	Attributes:size=Long

	Description	: Copy the contents of the speficied control
			  register to the specified general register,
			  or copy the contents of the specified general
			  register to the specified control register.
			  This is ALWAYS a 32-bit transfer even though
			  the specified control register may be imple-
			  mented with fewer bits. Unimplemented bits are
			  read as zeros, and ignored for write operations.

	Condition Codes	: NOT AFFECTED.

	Instruction Format :

		0 1 0 0 1 1 1 0 0 1 1 1 1 0 1 D

		A R R R C C C C C C C C C C C C

	Instruction Fields :

		D	:	Direction field. Specifies the direction
				of data transfer.

				0 = MOVEC Rc,Rn

				1 = MOVEC Rn,Rc

		A	:	A/D field. Specifies the type of general
				register.

				0 = Data register.

				1 = Address register.

		CCC...	:	Control Register field. Specifies the control
				register number. Currently defined control
				registers for the 68010 are:

				    Binary	Hex	Register
				    ------	---	--------

				0000 0000 0000	000	SFC : Source
							function code
							register

				0000 0000 0001	001	DFC : Destination
							function code
							register

				1000 0000 0000	800	User Stack Pointer
							(USP).

				1000 0000 0001	801	VBR : Vector Base
							register.

				All other codes cause an illegal instruction
				exception.


MOVEM	: Move Multiple Registers

	Operation : src -> Registers

		    Registers -> dst

	Assembler : MOVEM Reglist,<ea>
		    MOVEM <ea>,Reglist

	Attributes:size=Word,Long

	Description	: Selected registers are transferred to or from
			  consecutive memory locations, starting at the
			  location specified by the effective address. A
			  register is transferred if the corresponding bit
			  in the register mask field is set. Either the
			  entire 32 bits of the specified registers can
			  be transferred or the low 16 bits.

				If the transfer is FROM memory TO the
			  registers, then word-sized transfers are sign-
			  extended to 32 bits prior to transfer. THIS IS
			  ALSO TRUE FOR DATA REGISTERS!

	Condition Codes	: NOT AFFECTED.

	Instruction Format :

		0 1 0 0 1 D 0 0 1 S E E E A A A

		M M M M M M M M M M M M M M M M

	Instruction Fields :

		D	:	Direction field. Sprcifies the direction
				of the transfer.

				0 = register to memory.

				1 = memory to register.

		S	:	Size field. Specifies the size of operands
				being transferred.

				0 = word transfer. Word operands are sign-
				    extended to 32 bits and the entire
				    register loaded if a memory to register
				    transfer is being performed.

				1 = long transfer.

		EEE	: Effective Address field.

		AAA	: Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. Legal addressing modes for
		MOVEM are:

		Register to memory:

				(An)
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L

		Memory to register:

				(An)
				(An)+
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L
				d(PC)
				d(PC,Xi)

		MMM...	:	Register list mask field. Specifies which
				registers are to be transferred. The mask
				register for predecrement addressing mode
				(-(An) mode) is:

			D0 D1 D2 D3 D4 D5 D6 D7 A0 A1 A2 A3 A4 A5 A6 A7

				while for all other modes the mask register
				is:

			A7 A6 A5 A4 A3 A2 A1 A0 D7 D6 D5 D4 D3 D2 D1 D0


		NOTE : An extra read bus cycle occurs for memory operands.
			This amounts to a memory word at one address higher
			than expected being addressed during operation.


MOVEP	: Move Peripheral Data

	Operation : src -> dst

	Assembler : MOVEP Dx,d(Ay)
		    MOVEP d(Ay),Dx

	Attributes:size=Word,Long

	Description	: Data is transferred between a data register
			  and alternate bytes of memory, starting at the
			  location specified and incrementing by two. The
			  high order byte of the data register is trans-
			  ferred first, followed by the low order bytes in
			  descending order, the lowest order byte being
			  transferred last. If the effective address is
			  even, transfer is made on the high half of the
			  data bus:if the effective address is odd, then
			  transfer is made on the low half of the data bus.

			  Example:Long transfer to/from an EVEN address

				Byte Organisation In Register

				HI  MIDHI  MIDLO  LO

				Byte Organisation In Memory
				(Lowest Address At Top)

				   Even		Odd

				   HI		---	ADDR
				  MIDHI		---	ADDR+2
				  MIDLO		---	ADDR+4
				   LO		---	ADDR+6

			Example:word transfer to/from an ODD address

				Byte Organisation In Register

				HI  LO

				Byte Organisation In Memory
				(Lowest Address At Top)

				   Even		Odd

				   ---		HI	ADDR
				   ---		LO	ADDR+2



	Condition Codes	: NOT AFFECTED.

	Instruction Format :

		0 0 0 0 R R R M M M 0 0 1 A A A

		D D D D D D D D D D D D D D D D

	Instruction Fields :

		RRR	: Data Register field. Specifies the data
			  register Dx to use.

		AAA	: Address register field. Specifies the
			  address register Ay to use.

		MMM	: Op-Mode field. Specifies the direction and
			  the size of the operation.

			  100 : MOVEP.W d(Ay),Dx

			  101 : MOVEP.L d(Ay),Dx

			  110 : MOVEP.W	Dx,d(Ay)

			  111 : MOVEP.L Dx,d(Ay)

		DDD...	: Displacement field. Specifies the displacement
			  d to use in d(Ay).


MOVEQ	: Move Quick

	Operation : Immediate Data -> Dn

	Assembler : MOVEQ #nnn,Dn

	Attributes:size=Long

	Description	: Move the contents of the immediate field to a
			  data register. The data is contained in an 8-bit
			  field in the instruction word itself. The data is
			  sign-extended to a long operand and all 32 bits
			  are transferred to the data register.

	Condition Codes	: X N Z V C
			  - * * 0 0

			  N Set if the result is negative.
			    Cleared otherwise.
			  Z Set if the result is zero.
			    Cleared otherwise.
			  V Always Cleared.
			  C Always Cleared.
			  X Not Affected.

	Instruction Format :

		0 1 1 1 R R R 0 D D D D D D D D

	Instruction Fields :

		RRR	:	Register field. Specifies which data
				register Dn to use.

		DDD...	:	Data field. These 8 bits are the data
				constant to use, and are sign-extended
				to a long operand before transfer.


MOVES	: Move To/From Address Space (PRIVILEGED INSTRUCTION)
	  (68010 onwards-NOT 68000)

	Operation : If 68000 in supervisor state
			THEN
				src <SFC>  -> Rn
				   or
				Rn -> dst <DFC>
			ELSE
				TRAP EXCEPTION (PRIVILEGE VIOLATION)

	Assembler : MOVES <ea>,Rn
		    MOVES Rn,<ea>

	Attributes:size=Byte,Word,Long

	Description	: Move the byte, word or long word operand from the
			  specified general register to a location within
			  the address space specified by the destination
			  function code register (DFC). Or move the byte,
			  word or long word operand from a location within
			  the address space specified by the source function
			  code register (SFC) to the specified general regis-
			  ter.

	Condition Codes	: NOT AFFECTED.

	Instruction Format :

		0 1 0 0 1 1 1 0 S S E E E A A A

		G R R R D 0 0 0 0 0 0 0 0 0 0 0

	Instruction Fields :

		SS	:	Size field. Specifies the size of the
				operation.

				00 = Byte operation.

				01 = Word operation.

				10 = Long operation.

		G	:	General register field. Specifies the
				type of general register to use.

				0 = Data register.

				1 = Address register.

		RRR	:	Register number field. Specifies which data
				or address register Rn to use.

		D	:	Direction field. Specifies the direction of
				the transfer.

				0 = MOVES <ea>,Rn

				1 = MOVES Rn,<ea>

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The legal modes are:

				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L

MULS	: Signed Multiply

	Operation : dst * src -> dst

	Assembler : MULS <ea>,Dn

	Attributes:size=Word

	Description	: 	Multiply the signed 16-bit source operand by
				the signed 16-bit destination operand, and
				store the 32-bit signed operand in the dest-
				ination data register. If the source operand
				is a data register, then the low 16 bits are
				used:the ligh 16 bits are ignored.

	Condition Codes	:	X N Z V C
				- * * 0 0

				N Set if the result is negative.
				  Cleared otherwise.
				Z Set if the result is zero.
				  Cleared otherwise.
				V Always Cleared.
				C Always Cleared.
				X Not Affected.

	Instruction Format :

		1 1 0 0 R R R 1 1 1 E E E A A A

	Instruction Fields :

		RRR	: Register field. Specifies the destination
			  data register D0-D7. This field ALWAYS
			  specifies the destination operand.

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. All possible 68000 add-
		ressing modes are legal for source operands EXCEPT
		address register direct (i.e., MULS An,Dn is NOT
		allowed).


MULU	: Unsigned Multiply

	Operation : dst * src -> dst

	Assembler : MULU <ea>,Dn

	Attributes:size=Word

	Description	: 	Multiply the signed 16-bit source operand by
				the signed 16-bit destination operand, and
				store the 32-bit signed operand in the dest-
				ination data register. If the source operand
				is a data register, then the low 16 bits are
				used:the ligh 16 bits are ignored.

	Condition Codes	:	X N Z V C
				- * * 0 0

				N Set if the most significant bit of the
				  result is set. Cleared otherwise.
				Z Set if the result is zero.
				  Cleared otherwise.
				V Always Cleared.
				C Always Cleared.
				X Not Affected.

	Instruction Format :

		1 1 0 0 R R R 0 1 1 E E E A A A

	Instruction Fields :

		RRR	: Register field. Specifies the destination
			  data register D0-D7. This field ALWAYS
			  specifies the destination operand.

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. All possible 68000 add-
		ressing modes are legal for source operands EXCEPT
		address register direct (i.e., MULU An,Dn is NOT
		allowed).


NBCD	: Negate Decimal With Extend.

	Operation : 0 -  dst(10) - X -> dst

	Assembler :	NBCD	<ea>

	Attributes:size=Byte

	Description	: The operand addressed at the destination and the
			  current value of the extend (X) bit of the CCR are
			  subtracted from zero. The operation is performed
			  using Binary Coded Decimal (BCD) arithmetic. The
			  result is saved at the destination location. This
			  instruction produces the 10s complement of the
			  destination if the extend bit is clear, the 9s
			  complement if the extend bit is set. This is a byte
			  operation only.

	Condition Codes	:	X N Z V C
				* U * U *

				N Undefined
				Z Cleared if nonzero result.
				  UNCHANGED otherwise!
				V Undefined
				C Set if DECIMAL borrow generated.
				  Cleared otherwise.
				X Set identically to C.

	Notes		: Normally, the Z bit is set via programming
			  (this is the PROGRAMMER'S responsibility)
			  before the start of an NBCD operation. This
			  allows successful tests upon completion of
			  multiple-precision NBCD operations.

	Instruction Format:

		0 1 0 0 1 0 0 0 0 0 E E E A A A

	Instruction Fields:

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The legal modes are:

			Dn
			(An)
			(An)+
			-(An)
			d(An)
			d(An,Xi)
			Abs.W
			Abs.L


NEG	: Negate an operand

	Operation : 0 - dst -> dst

	Assembler : NEG <ea>

	Attributes:size=Byte,Word,Long

	Description	: The destination is cleared to all zero bits.
			  The size of the operation may by byte, word
			  or long.

	Condition Codes	:	X N Z V C
				* * * * *

				N Set if the result is negative.
				  Cleared otherwise.
				Z Set if the result is zero.
				  Cleared otherwise.
				V Set if an overflow was generated.
				  Cleared otherwise.
				C Cleared if the result is zero.
				  Set otherwise.
				X Set identically to C.

	Instruction Format :

		0 1 0 0 0 1 0 0 S S E E E A A A

	Instruction Fields :

		SS	: Size field. Determines the size of the operation.

			  00 = Byte operation.

			  01 = Word operation.

			  10 = Long operation.

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL addressing modes
		for NEG are:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L


NEGX	: Negate With Extend

	Operation : 0 - dst - X -> dst

	Assembler : NEGX <ea>

	Attributes:size=Byte,Word,Long

	Description	: The destination operand and the value of the
			  extend bit are subtracted from zero. The result
			  is stored at the destination effective address.
			  The size of the operation may be specified to be
			  byte, wor dor long.

	Condition Codes :	X N Z V C
				* * * * *

				N Set if result negative when treated as
				  2's complement. Cleared otherwise.
				Z Cleared if result is non-zero.
				  Unchanged otherwise.
				V Set if an overflow is generated. Cleared
				  otherwise.
				C Set if a binary borrow is generated.
				  Cleared otherwise.
				X Set identically to C.

			NOTE : Normally the Z bit is set via programming
				(e.g., using MOVEQ #0,D0) before the start
				of the operation. This allows successful
				tests for zero operands upon completion of
				multiple-precision operations.

	Instruction Format :

		0 1 0 0 0 0 0 0 S S E E E A A A

	Instruction Fields :

		SS	: Size field. Specifies operation size.

			  00 = byte operation

			  01 = word operation

			  10 = long operation

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL addressing modes
		for NEG are:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L

NOP	: No Operation.

	Operation : None

	Assembler : NOP

	Attributes:Unsized

	Description	: No operation occurs. The processor state,
			  other than the program counter, is unchanged.
			  Execcution continues with the instruction
			  immediately following the NOP.

	Condition Codes	: NOT AFFECTED.

	Instruction Format :

		0 1 0 0 1 1 1 0 0 1 1 1 0 0 0 1


NOT	: Logical complement.

	Operation : ~dst -> dst

	Assembler : NOT <ea>

	Attributes:size=Byte,Word,Long

	Description	: The ones complement of the destination operand
			  is computed, and the result stored at the dest-
			  ination effective address. The size of the oper-
			  ation may be specified to be byte, word or long.

	Condition Codes	:	X N Z V C
				- * * 0 0

				N Set if the result is negative.
				  Cleared otherwise.
				Z Set if the result is zero.
				  Cleared otherwise.
				V Always Cleared.
				C Always Cleared.
				X Not Affected.

	Instruction Format :

		0 1 0 0 0 1 1 0 S S E E E A A A

	Instruction Fields :

		SS	: Size field. Determines the size of the operation.

			  00 = Byte operation.

			  01 = Word operation.

			  10 = Long operation.

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL addressing modes
		for NEG are:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L

OR	: Logical OR operation

	Operation : src OR dst -> dst

	Assembler : OR	<ea>,Dn
		    OR	Dn,<ea>

	Attributes:size=Byte,Word,Long

	Description	: Logically (bitwise) OR the source operand
			  with the destination operand, and store the
			  result in the destination location.

	Condition Codes :	X N Z V C
				- * * 0 0

				N Set if result negative when treated as
				  2's complement. Cleared otherwise.
				Z Set if result is zero. Cleared otherwise.
				V Always Cleared.
				C Always Cleared.
				X Not affected.

	Instruction Format :

		1 0 0 0 R R R M M M E E E A A A

	Instruction Fields :

		RRR	: Register field. Specifies any of the
			  8 data registers.

		MMM	: Op-Mode field. Specifies operation
			  according to:

			  Byte	Word  Long	   Operation
			  ----	----  ----	   ---------
			  000	001   010	  OR <ea>,Dn
			  100	101   110	  OR Dn,<ea>

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL modes are:

		Source Operand:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L
				d(PC)
				d(PC,Xi)
				#nnnn

		Destination Operand:

				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L

		NOTES : 1) If the destination is a data register, then
			   it CANNOT be specified using destination <ea>
			   addressing mode, but MUST use the destination
			   Dn mode above instead.

			2) ORI is used when the source is immediate data.
			   Most assemblers automatically make this distinc-
			   tion.


ORI	: Logical OR immediate

	Operation : immediate data OR dst -> dst

	Assembler : ORI  #nnnn,<ea>

	Attributes:size=Byte,Word,Long

	Description	: Logically (Bitwise) OR the immediate data
			  contained in the instruction to the destin-
			  ation operand, and store the result in the
			  destination location.

			  NOTE:The contents of the immediate operand
			  part of the instruction is as follows:

			  Byte : 2nd word of operand, upper byte zero.

			  Word : 2nd word of operand.

			  Long : 2nd and 3rd word of operand.

			  Extension words for complex addressing modes
			  follows the immediate operand.

	Condition Codes :	X N Z V C
				- * * 0 0

				N Set if result negative when treated as
				  2's complement. Cleared otherwise.
				Z Set if result is zero. Cleared otherwise.
				V Always Cleared.
				C Always Cleared.
				X Not Affected.

	Instruction Format :

		0 0 0 0 0 0 0 0 S S E E E A A A

		W W W W W W W W B B B B B B B B

		L L L L L L L L L L L L L L L L

	Instruction Fields :

		SS	: Size field. Specifies the size of the operation.

			  00 = Byte operation.

			  01 = Word operation.

			  10 = Long operation.

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL modes are:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L

		BBB...	: Byte immediate data field. The immediate
			  data is contained here. The WWW... field
			  is set to zero (00000000 binary) and the
			  LLL... field does not exist.

		WWW...	: Word immediate data field. The immediate
			  data occupies both WWW... and BBB... fields.
			  The LLL... field does not exist.

		LLL...	: Long immediate data field. The immediate
			  data occupies all BBB, WWW and LLL fields,
			  and the long word is divided as follows:

				WWW...BBB...	HIGH word of data
				LLL...		LOW word of data


ORI	: Logical OR immediate to CCR

	Operation : immediate data OR CCR -> CCR

	Assembler : ORI  #nnnn,CCR

	Attributes:size=Byte

	Description	: Logically (Bitwise) OR the immediate data
			  contained in the instruction to the contents
			  of the Condition Code Register, and store the
			  result in the Condition Code Register (low 8
			  bits of Status Register).

			  NOTE:The contents of the immediate operand
			  part of the instruction is as follows:

			  Byte : 2nd word of operand, upper byte zero.

			  Extension words for complex addressing modes
			  follows the immediate operand.

	Condition Codes :	X N Z V C
				* * * * *

				N Set if Bit 3 of the operand is 1.
				  Unchanged otherwise.
				Z Set if Bit 2 of the operand is 1.
				  Unchanged otherwise.
				V Set if Bit 1 of the operand is 1.
				  Unchanged otherwise.
				C Set if Bit 0 of the operand is 1.
				  Unchanged otherwise.
				X Set if Bit 4 of the operand is 1.
				  Unchanged otherwise.

	Instruction Format :

		0 0 0 0 0 0 0 0 0 0 1 1 1 1 0 0

		0 0 0 0 0 0 0 0 B B B B B B B B

	Instruction Fields :

		BBB...	:	Byte Data field. Contains the 8-bit data
				with which the CCR is ORed.


ORI	: Logical OR immediate to SR (PRIVILEGED INSTRUCTION)

	Operation : If 68000 in supervisor state
			THEN
				immediate data OR SR -> SR
			ELSE
				TRAP EXCEPTION (PRIVILEGE VIOLATION)

	Assembler : ORI  #nnnn,SR

	Attributes:size=Word

	Description	: Logically (Bitwise) OR the immediate data
			  contained in the instruction to the contents
			  of the Status Register, and store the result
			  in the Status Register.

			  NOTE:The contents of the immediate operand
			  part of the instruction is as follows:

			  Word : 2nd word of operand.

			  Extension words for complex addressing modes
			  follows the immediate operand.

	Condition Codes :	X N Z V C
				* * * * *

				N Set if Bit 3 of the operand is 1.
				  Unchanged otherwise.
				Z Set if Bit 2 of the operand is 1.
				  Unchanged otherwise.
				V Set if Bit 1 of the operand is 1.
				  Unchanged otherwise.
				C Set if Bit 0 of the operand is 1.
				  Unchanged otherwise.
				X Set if Bit 4 of the operand is 1.
				  Unchanged otherwise.

	Instruction Format :

		0 0 0 0 0 0 0 0 0 1 1 1 1 1 0 0

		W W W W W W W W W W W W W W W W

	Instruction Fields:

		WWW...	:	Word data instruction field. The
				immediate data is contained in
				this field.


PEA	: Push Effective Address

	Operation : dst -> -(SP)

	Assembler : PEA <ea>

	Attributes:size=Long

	Description	: The effective address itself, NOT its contents,
			  are pushed onto the stack. A long word address
			  is pushed onto the stack.

	Condition Codes	: NOT AFFECTED.

	Instruction Format :

		0 1 0 0 1 0 0 0 0 1 E E E A A A

	Instruction Fields :

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The possible LEGAL add-
		ressing modes for PEA are:

				(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L
				d(PC)
				d(PC,Xi)


RESET	: Reset External Devices (PRIVILEGED INSTRUCTION)

	Operation : IF 68000 in supervisor state
			THEN
				Assert RESET line
			ELSE
				TRAP EXCEPTION (PRIVILEGE VIOLATION)

	Assembler : RESET

	Attributes:Unsized

	Description	: The RESET line of the processor is asserted,
			  which causes all external devices to be reset.
			  The processor state, other than the program
			  counter, is unaffected and execution continues
			  with the next instruction.

	Condition Codes	: NOT AFFECTED.

	Instruction Format :

		0 1 0 0 1 1 1 0 0 1 1 1 0 0 0 0


ROL,ROR	: Rotate Without Extend

	Operation : dst (rotated by count) -> dst

	Assembler : ROd	Dx,Dy
		    ROd #nnnn,Dy
		    ROd <ea>

	Attributes:size=Byte,Word,Long

	Description	: Rotate the bits of the destination operand in the
			  direction specified. The extend bit is not inclu-
			  ded in the rotation. The carry bit receives the
			  last bit shifted out of the operand. The shift
			  count for the operation can be specified in two
			  ways:

			  1) Immediate. The shift count value is 1-8.

			  2) Data Register. The value contained in the
				specified data register, modulo 64, is
				used.

			  If the destination operand is a memory operand,
			  then the shift count is ALWAYS 1, and the operand
			  size is ALWAYS word sized.

			  ROL : Operand is rotated left by the value of the
				shift count. Bits shifted out of the high
				order bit are copied to the C and X bits of
				the CCR, and back into the low order bits.
				Zero bits are shifted into the vacated low
				order bits.

			  ROR : Operand is rotated right by the value of the
				shift count. Bits shifted out of the low
				order bit are copied to the C and X bit of
				the CCR, and back into the high order bit.
				Zero bits are shifted into the vacated high
				order bits.

	Condition Codes :	X N Z V C
				- * * 0 *

				N Set if result negative when treated as
				  2's complement. Cleared otherwise.
				Z Set if result is zero. Cleared otherwise.
				V Always Cleared.
				C Set according to the last bit shifted out
				  of the operation. Cleared for a shift count
				  of zero.
				X Not Affected.

	Instruction Format (Register Shifts) :

		1 1 1 0 C C C D S S L 1 1 R R R

	Instruction Fields :

		CCC	: Count/Register field. If immediate count,
			  CCC = 1-7 for a shift count of 7, 0 for a
			  shift count of 8. If data register count,
			  CCC = data regsiter number for register Dx.
			  The value contained in bits 0-5 of Dx is
			  used as the shift count (i.e., Dx modulo
			  64).

		D	: Direction field. Specifies shift direction.

			  0 = right shift

			  1 = left shift

		SS	: Size field. Specifies the size of the operation.

			  00 = Byte operation.

			  01 = Word operation.

			  10 = Long operation.

		L	: L/R field. Specifies shift count type.

			  0 = immediate shift count in CCC field.

			  1 = data register count, register in CCC field.

		RRR	: Register field. Specifies any of the 8 data
			  registers whose content is to be shifted.

	Instruction Format (Memory Shifts) :

		1 1 1 0 0 1 1 D 1 1 E E E A A A

	Instruction Fields :

		D	: Direction field. Specifies shift direction.

			  0 = right shift

			  1 = left shift

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL modes are:

				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L


ROXL,ROXR	: Rotate Without Extend

		Operation : dst (rotated by count) -> dst

		Assembler : ROd	Dx,Dy
			    ROd #nnnn,Dy
			    ROd <ea>

	Attributes:size=Byte,Word,Long

	Description	: Rotate the bits of the destination operand in the
			  direction specified. The extend bit IS included in
			  the rotation. The carry bit receives the last bit
			  shifted out of the operand. The shift count for the
			  operation can be specified in two ways:

			  1) Immediate. The shift count value is 1-8.

			  2) Data Register. The value contained in the
				specified data register, modulo 64, is
				used.

			  If the destination operand is a memory operand,
			  then the shift count is ALWAYS 1, and the operand
			  size is ALWAYS word sized.

			  ROXL : Operand is rotated left by the value of the
				shift count. Bits shifted out of the high
				order bit are copied to the C and X bits of
				the CCR, and back into the low order bits.
				The previous value of the X bit prior to
				each single-position rotate is moved into
				the vacated low-order bit.

			  ROXR : Operand is rotated right by the value of
				the shift count. Bits shifted out of the low
				order bit are copied to the C and X bit of
				the CCR, and back into the high order bit.
				The previous value of the X bit prior to
				each single-position rotate is moved into
				the vacated high-order bit.

	Condition Codes :	X N Z V C
				- * * 0 *

				N Set if result negative when treated as
				  2's complement. Cleared otherwise.
				Z Set if result is zero. Cleared otherwise.
				V Always Cleared.
				C Set according to the last bit shifted out
				  of the operation. UNAFFECTED for a shift
				  count of zero!
				X Not Affected.

	Instruction Format (Register Shifts) :

		1 1 1 0 C C C D S S L 1 0 R R R

	Instruction Fields :

		CCC	: Count/Register field. If immediate count,
			  CCC = 1-7 for a shift count of 7, 0 for a
			  shift count of 8. If data register count,
			  CCC = data regsiter number for register Dx.
			  The value contained in bits 0-5 of Dx is
			  used as the shift count (i.e., Dx modulo
			  64).

		D	: Direction field. Specifies shift direction.

			  0 = right shift

			  1 = left shift

		SS	: Size field. Specifies the size of the operation.

			  00 = Byte operation.

			  01 = Word operation.

			  10 = Long operation.

		L	: L/R field. Specifies shift count type.

			  0 = immediate shift count in CCC field.

			  1 = data register count, register in CCC field.

		RRR	: Register field. Specifies any of the 8 data
			  registers whose content is to be shifted.

	Instruction Format (Memory Shifts) :

		1 1 1 0 0 1 0 D 1 1 E E E A A A

	Instruction Fields :

		D	: Direction field. Specifies shift direction.

			  0 = right shift

			  1 = left shift

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL modes are:

				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L


RTD	: Return and Deallocate Parameters
	  (68010 upwards - NOT 68000)

	Operation : (SP)+ -> PC
		    SP + d -> SP

	Assembler : RTD #<displacement>

	Attributes:Unsized

	Description	: The program counter is pulled from the stack.
			  The previous program counter value is lost.
			  After the program counter is read from the
			  stack, the displacement value is sign-extended
			  to 32 bits and added to the stack pointer.

	Condition Codes	: NOT AFFECTED.

	Instruction Format :

		0 1 0 0 1 1 1 0 0 1 1 1 0 1 0 0

		D D D D D D D D D D D D D D D D

	Instruction Fields :

		DDD...	:	Displacement field. The 16-bit displacement
				is contained in this field.


RTE	: Return from Exception (PRIVILEGED INSTRUCTION)
	  (68000 version)

	Operation : IF 68000 in supervisor state
			THEN
				(SP)+ -> SR
				(SP)+ -> PC
			ELSE
				TRAP EXCEPTION (PRIVILEGE VIOLATION)

	Assembler : RTE

	Attributes:Unsized

	Description	: The status register and program counter are
			  pulled from the system stack. The previous
			  status register and program counter are lost.
			  All bits in the status register are affected.

	Condition Codes	: Set according to the content of the word
			  on the stack.

	Instruction Format :

		0 1 0 0 1 1 1 0 0 1 1 1 0 0 1 1


RTE	: Return from Exception (PRIVILEGED INSTRUCTION)
	  (68010 upwards version)

	Operation : IF 680x0 in supervisor state
			THEN
				(SP)+ -> SR
				(SP)+ -> PC
				IF (SP)+ = long format
				  THEN
					full machine state restore
				  ELSE
					do nothing
			ELSE
				TRAP EXCEPTION (PRIVILEGE VIOLATION)

	Assembler : RTE

	Attributes:Unsized

	Description	: The status register and program counter are
			  pulled from the system stack. The previous
			  status register and program counter are lost.
			  All bits in the status register are affected.
			  The vector offset word is then pulled from
			  the stack, and the format field is examined
			  to determine the type of stack frame to pull
			  off the stack to restore the machine state.

	Condition Codes	: Set according to the content of the word
			  on the stack.

	Instruction Format :

		0 1 0 0 1 1 1 0 0 1 1 1 0 0 1 1

	Vector Offset Word Format :

		F F F F 0 0 V V V V V V V V V V

	Vector Offset Word Format Fields :

		FFFF	:	Format field. Specifies the amount of
				information to pull from the stack to
				restore the machine state.

				0000 : Short frame. Four words are
					pulled from the stack.

				1000 : Long frame. 29 words are pulled
					from the stack.

				Any other value is an error on the
				68010. The processor then takes the
				format error exception.


RTR	: Return And Restore Condition Codes

	Operation : (SP)+ -> CC
		    (SP)+ PC

	Assembler : RTR

	Attributes:Unsized

	Description	: The condition codes and program counter are
			  pulled from the stack. The previous program
			  counter and condition codes are lost. The
			  supervisor portion of the status register
			  (the upper 8 bits) are unaffected.

	Condition Codes	: Set according to the content of the word
			  on the stack.

	Instruction Format :

		0 1 0 0 1 1 1 0 0 1 1 1 0 1 1 1


RTS	: Return From Subroutine

	Operation : (SP)+ -> PC

	Assembler : RTS

	Attributes:Unsized

	Description	: The program counter is pulled from the stack.
			  The previous value of the program counter is
			  lost.

	Condition Codes	: NOT AFFECTED.

	Instruction Format :

		0 1 0 0 1 1 1 0 0 1 1 1 0 1 0 1


SBCD	: Subtract Decimal With Extend.

	Operation : dst(10) - src(10) - X -> dst

	Assembler :	SBCD	Dy,Dx

			SBCD	-(Ay),-(Ax)

	Attributes:size=Byte

	Description	: Perform Binary Coded Decimal (BCD) subtraction
			  of the source and destination operands, together
			  with the Extend (X) bit of the CCR. The only
			  legal addressing modes are those given above.
			  This is a byte operation only.

	Condition Codes	:	X N Z V C
				* U * U *

				N Undefined
				Z Cleared if nonzero result.
				  UNCHANGED otherwise!
				V Undefined
				C Set if DECIMAL borrow generated.
				  Cleared otherwise.
				X Set identically to C.

	Notes		: Normally, the Z bit is set via programming
			  (this is the PROGRAMMER'S responsibility)
			  before the start of an SBCD operation. This
			  allows successful tests upon completion of
			  multiple-precision SBCD operations.

	Instruction Format:

		1 0 0 0 X X X 1 0 0 0 0 M Y Y Y

	Instruction Fields:

		XXX : Register Rx field. Specifies which register
			is used for the destination operand, D0-D7
			for ABCD Dy,Dx or A0-A7 for ABCD -(Ay),-(Ax)

		YYY : Register Ry field. Specifies which register
			is used for the source operand, D0-D7
			for ABCD Dy,Dx or A0-A7 for ABCD -(Ay),-(Ax)

		M   : R/M field. Specifies addressing mode.
			0 : mode is ABCD Dy,Dx
			1 : mode is ABCD -(Ay),-(Ax)


Scc	: Set according to condition codes

	Operation : IF condition is TRUE
			THEN
			  11111111 -> dst.B
			ELSE
			  00000000 -> dst.B

	Assembler : Scc <ea>

	Attributes:size=Byte

	Description	: The conditional expression specified in the
			  instruction is evaluated and the result tested.
			  If the result is TRUE, then the byte referred
			  to by the destination effective address is set
			  to the value 11111111 binary ($FF Hex). If the
			  result is FALSE, then the bye referred to by
			  the destination effective address is set to the
			  value 00000000 binary ($00 Hex). The values $FF
			  and $00 are taken to represent TRUE and FALSE
			  respectively.

	Possible Instructions (U = unsigned test, S=signed test) :

		ST	Set if True
		SF	Set if False
		SHI	Set if Higher			(U)
		SLS	Set if Lower or Same 		(U)
		SCC	Set on Carry Clear		(U)
		SCS	Set on Carry Set		(U)
		SNE	Set if Not Equal (to Zero)	(U and S)
		SEQ	Set if Equal (to Zero)		(U and S)
		SVC	Set if Overflow Clear
		SVS	Set if Overflow Set
		SPL	Set if Result Plus (N Clear)
		SMI	Set if Result Minus (N Set)
		SGE	Set if Greater Or Equal (to Zero?)	(S)
		SLT	Set if Less Than (Zero?)		(S)
		SGT	Set if Greater Than (Zero?)		(S)
		SLE	Set if Less Than or Equal (to Zero?)	(S)

		Synonyms supported by some assemblers include:

		SHS (Set if Higher Than or Same) for SCC	(U)
		SLO (Set if Lower Than) for SCS		(U)

	Condition Codes	: NOT AFFECTED.

	Instruction Format :

		0 1 0 1 C C C C 1 1 E E E A A A

	Instruction Fields :

		CCCC	: Condition field. Specifies the conditional
			  expression to compute prior to the branch
			  decision. Values are given in the condition-
			  al branch table at the end of this file.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL modes are:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L


STOP	: Load Status Register and Stop Execution
	  (PRIVILEGED INSTRUCTION)

	Operation : IF 680x0 in supervisor state
			THEN
				immediate data -> SR
				HALT PROCESSOR
			ELSE
				TRAP EXCEPTION (PRIVILEGE VIOLATION)

	Assembler : STOP #nnnn

	Attributes:Unsized

	Description	: The immediate data is moved into the entire
			  status register. The program counter is then
			  incremented to point to the next instruction
			  in the execution sequence immediately follow-
			  ing the STOP instruction, and then the pro-
			  cessor is placed in the HALT state, where the
			  fetching and execution of instructions ceases.
			  Execution resumes when a trace, interrupt or
			  reset exception occurs. A trace exception will
			  occur if the TRACE bit of the status register
			  is set prior to execution of the STOP instruc-
			  tion. If an interrupt request arrives whose
			  priority is greater than the current processor
			  IPLx priority, then an interrupt exception will
			  occur, otherwise the interrupt request has no
			  effect. If the bit of the immediate data cor-
			  responding to the S-bit of the status register
			  (the supervisor bit) is zero, execution of the
			  instruction will cause a privilege violation
			  exception even if the machine is currently in
			  the supervisor state. A reset exception (caused
			  by an external reset) will ALWAYS initiate the
			  processing of a reset exception.

	Condition Codes	: Set according to the content of the immediate
			  data.

	Instruction Format :

		0 1 0 0 1 1 1 0 0 1 1 1 0 0 1 0

		D D D D D D D D D D D D D D D D


	Instruction Fields :

		DDD...	:	Immediate data field. The immediate data
				to be loaded into the status register is
				found in this instruction word.

SUB	: Subctract Binary.

	Operation : dst - src -> dst

	Assembler : SUB <ea>,Dn

		    SUB Dn,<ea>

	Attributes:size=Byte,Word,Long

	Description	: Subtract the source operand from the dest-
			  ination operand, and store the result in the
			  destination operand. The operation may be
			  specified to be byte, word or long in size.
			  The mode of the instruction indicates which
			  is the source and which is the destination
			  operand.

	Condition Codes :	X N Z V C
				* * * * *

				N Set if result negative when treated as
				  2's complement. Cleared otherwise.
				Z Set if result is zero. Cleared otherwise.
				V Set if an overflow is generated. Cleared
				  otherwise.
				C Set if a binary borrow is generated.
				  Cleared otherwise.
				X Set identically to C.

	Instruction Format :

		1 0 0 1 R R R M M M E E E A A A

	Instruction Fields :

		RRR : Register field. Specifies any data register
			D0-D7.

		MMM : Op-Mode field. Specifies operation type in
			accordance with the table:

			  Byte	Word  Long	   Operation
			  ----	----  ----	   ---------
			  000	001   010	  SUB <ea>,Dn
			  100	101   110	  SUB Dn,<ea>

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The legal modes are:

		Source <ea> : All addressing modes.

		Destination <ea> : The following are ILLEGAL addressing
					modes:

					Dn
					An
					offset(PC)
					offset(PC,Xn)
					#nnn

				   All others are legal.

		Notes		: 1) If the destination is a data register,
				  then the SUB <ea>,Dn form of the instruc-
				  tion MUST be used.

				  2) SUBA is used for SUB <ea>,An. SUBI is
				  used for SUB #nnn,<ea> where <ea> is not
				  a data register. SUBQ is also used for
				  SUB #nnn,<ea> when possible. Most 68000
				  assemblers can automatically make this
				  distinction.


SUBA	: Subtract Address

	Operation : dst - src -> An

	Assembler : SUBA  <ea>,An

	Attributes:size=Word,Long

	Description	: Subtract the source operand from the dest-
			  ination address register, and store the result
			  in the destination address register. The size
			  of the operation may be specified to be a word
			  or long operation.

			  NOTE:All address arithmetic on address
			  registers is performed using the ENTIRE
			  32 bits of the address register. Word
			  operands are sign-extended to 32 bits
			  before adding.

	Condition Codes : NOT AFFECTED.

	Instruction Format :

		1 0 0 1 R R R M M M E E E A A A

	Instruction Fields :

		RRR : Specifies one of the address registers A0-A7.
			This is ALWAYS the destination operand.

		MMM : Op-Mode field. Specifies the size of the
			operation.

			011 : Word operation. See NOTE above.

			111 : Long operation.

		EEE and AAA fields. Defined in addressing mode section
		below. All legal 68000 addressing modes are allowed for
		the source operand.


SUBI	: Subtract Immediate Operand

	Operation : dst - immediate data -> dst

	Assembler : SUBI  #nnnn,<ea>

	Attributes:size=Byte,Word,Long

	Description	: Subtract the immediate data contained in
			  the instruction from the destination operand,
			  and store the result in the destination
			  location.

			  NOTE:The contents of the immediate operand
			  part of the instruction is as follows:

			  Byte : 2nd word of operand, upper byte zero.

			  Word : 2nd word of operand.

			  Long : 2nd and 3rd word of operand.

			  Extension words for complex addressing modes
			  follows the immediate operand.

	Condition Codes :	X N Z V C
				* * * * *

				N Set if result negative when treated as
				  2's complement. Cleared otherwise.
				Z Set if result is zero. Cleared otherwise.
				V Set if an overflow is generated. Cleared
				  otherwise.
				C Set if a binary borrow is generated.
				  Cleared otherwise.
				X Set identically to C.

	Instruction Format :

		0 0 0 0 0 1 0 0 S S E E E A A A

		W W W W W W W W B B B B B B B B

		L L L L L L L L L L L L L L L L

	Instruction Fields :

		SS	: Size field. Specifies operation size.

			  00 = byte operation

			  01 = word operation

			  10 = long operation

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL modes are:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L

		BBB...	: Byte immediate data field. The immediate
			  data is contained here. The WWW... field
			  is set to zero (00000000 binary) and the
			  LLL... field does not exist.

		WWW...	: Word immediate data field. The immediate
			  data occupies both WWW... and BBB... fields.
			  The LLL... field does not exist.

		LLL...	: Long immediate data field. The immediate
			  data occupies all BBB, WWW and LLL fields,
			  and the long word is divided as follows:

				WWW...BBB...	HIGH word of data
				LLL...		LOW word of data


SUBQ	: Subtract Immediate Quick Operand

	Operation : dst - immediate data -> dst

	Assembler : SUBQ  #nnnn,<ea>

	Attributes:size=Byte,Word,Long

	Description	: Subtract the immediate data contained in
			  the instruction from the destination op-
			  erand, and store the result in the dest-
			  ination location. The range of values for
			  the immediate operand is 1 to 8, represented
			  in the instruction by 0 to 7 (0 representing
			  a value of 8). The immediate data is automa-
			  tically coerced to the operation size by the
			  68000.

	Condition Codes :	X N Z V C
				* * * * *

				N Set if result negative when treated as
				  2's complement. Cleared otherwise.
				Z Set if result is zero. Cleared otherwise.
				V Set if an overflow is generated. Cleared
				  otherwise.
				C Set if a binary carry is generated.
				  Cleared otherwise.
				X Set identically to C.

			  NOTE : Condition codes NOT AFFECTED if the
				 destination for the subtraction is
				 an address register!

	Instruction Format :

		0 1 0 1 D D D 1 S S E E E A A A

	Instruction Fields :

		DDD	: Data field. 3 bits of immediate data,
			  0 representing a value of 8, 1-7 repre-
			  senting those values repsectively.

		SS	: Size field. Specifies operation size.

			  00 = byte operation

			  01 = word operation

			  10 = long operation

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. The LEGAL modes are:

				Dn
				An (Word and Long only)
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L


SUBX	: Subtract With Extend

	Operation : dst - src - X -> dst

	Assembler : SUBX  Dy,Dx
		    SUBX -(Ay),-(Ax)

	Attributes:size=Byte,Word,Long

	Description	: Subtract the source operand from the dest-
			  ination operand, along with the extend bit,
			  and store the result in the destination loca-
			  tion.

	Condition Codes :	X N Z V C
				* * * * *

				N Set if result negative when treated as
				  2's complement. Cleared otherwise.
				Z Cleared if result is non-zero.
				  Unchanged otherwise.
				V Set if an overflow is generated. Cleared
				  otherwise.
				C Set if a binary carry is generated.
				  Cleared otherwise.
				X Set identically to C.

			NOTE : Normally the Z bit is set via programming
				(e.g., using MOVEQ #0,D0) before the start
				of the operation. This allows successful
				tests for zero operands upon completion of
				multiple-precision operations.

	Instruction Format :

		1 0 0 1 X X X 1 S S 0 0 R Y Y Y

	Instruction Fields :

		XXX	: Register Rx field. Specifies the destination
			  register, depending upon R field.

		SS	: Size field. Specifies operation size.

			  00 = byte operation

			  01 = word operation

			  10 = long operation

		R	: R/M field, specifies operation addressing mode.
			  0 : operation is ADDX Dy,Dx, and XXX,YYY
				fields specify data registers.

			  1 : Operation is ADDX -(Ay),-(Ax), and XXX,YYY
				fields specify address registers.

		YYY	: Register Ry field. Specifies the source
			  register, depending upon R field.


SWAP	: Swap Register Halves.

	Operation : Register {31:16} <-> Register {15:0}

	Assembler : SWAP Dn

	Attributes:size=Word

	Description	: Exchange the upper and lower 16-bit halves of
			  the specified data register.

	Condition Codes :	X N Z V C
				- * * 0 0

				N Set if 32-bit result negative when
				  treated as 2's complement. Cleared
				  otherwise.
				Z Set if the 32-bit result is zero.
				  Cleared otherwise.
				V Always Cleared.
				  otherwise.
				C Always Cleared.
				X Not Affected.

	Instruction Format :

		0 1 0 0 1 0 0 0 0 1 0 0 0 R R R

	Instruction Fields :

		RRR : Register field. Specifies the data register
			D0-D7 to swap.


TAS	: Test And Set

	Operation : dst tested : result -> CCR
		    1 -> dst{7}

	Assembler : TAS <ea>

	Attributes:size=Byte

	Description	: Test and set the byte operand addressed by the
			  effective address field. The current value of
			  the operand is tested and the N and Z flags of
			  the CCR are set accordingly. The high order bit
			  (bit 7) of the operand is set.

			  This operation is performed using an indivisible
			  read-modify-write memory cycle, and allows the
			  synchronsiation of several processors in a multi-
			  processor 680x0 environment.

	Condition Codes :	X N Z V C
				- * * 0 0

				N Set if operand was negative.
				  Cleared otherwise.
				Z Set if operand was zero.
				  Cleared otherwise.
				V Always Cleared.
				C Always Cleared.
				X Not Affected.

	Instruction Format :

		0 1 0 0 1 0 1 0 1 E E E A A A

	Instruction Fields :

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes. 

		The following are ILLEGAL addressing modes:

					Dn
					An
					offset(PC)
					offset(PC,Xn)
					#nnn

				   All others are legal.


		Notes : Bus error retry is inhibited on the read portion
			of the read-modify-write bus cycle to ensure
			system integrity. The bus error exception is
			always taken.


TRAP	: 680x0 TRAP Instruction

	Operation : PC -> -(SSP)
		    SR -> -(SSP)
		    (Trap Vector) -> PC

	Assembler : TRAP #nnnn

	Attributes:Unsized

	Description	: The processor initiates exception processing. The
			  vector number is used to reference the TRAP inst-
			  ruction vector specified by the low order four
			  bits of the instruction. Sixteen TRAP instruction
			  vectors are available.

	Condition Codes : NOT AFFECTED.

	Instruction Format :

		0 1 0 0 1 1 1 0 0 1 0 0 V V V V

	Instruction Fields :

		VVVV	:	Vector field. Specifies which of the 16
				TRAP exception vectors is to be referenced
				to obtain the new program counter.


TRAPV	: TRAP on overflow.

	Operation : IF V bit of CCR set
			THEN
				TRAP (VIA TRAPV EXCEPTION)

	Assembler : TRAPV

	Attributes:Unsized

	Description	: Test the overflow bit of the CCR. If V is
			  cleared, continue execution at the next in-
			  struction in sequence. If V is set, initiate
			  exception processing via the TRAPV exception
			  vector.

	Condition Codes : NOT AFFECTED.

	Instruction Format :

		0 1 0 0 1 1 1 0 0 1 1 1 0 1 1 0


TST	: Test an operand

	Operation : dst - 0  : result -> CCR

	Assembler : TST <ea>

	Attributes:size=Byte,Word,Long

	Description	: Compare the operand with zero. The result
			  is not saved directly. Instead, the various
			  bits of the CCR are conditioned according
			  to the result. The size of the operation may
			  be specified to be byte, word or long.

	Condition Codes	:	X N Z V C
				- * * 0 0

				N Set if the operand is negative.
				  Cleared otherwise.
				Z Set if the operand is zero.
				  Cleared otherwise.
				V Always Cleared.
				C Always Cleared.
				X Not Affected.

	Instruction Format :

		0 1 0 0 1 0 1 0 S S E E E A A A

	Instruction Fields :

		SS	: Size field. Determines the size of the operation.

			  00 = Byte operation.

			  01 = Word operation.

			  10 = Long operation.

		EEE	: Destination Effective Address field.

		AAA	: Destination (Address) Register field.

		EEE and AAA specify the effective address of the
		<ea> operand. The table of possible values of the
		EEE and AAA fields appears in the section describ-
		ing the addressing modes.The LEGAL addressing modes
		for TST are:

				Dn
				(An)
				(An)+
				-(An)
				d(An)
				d(An,Xi)
				Abs.W
				Abs.L


UNLK	: Unlink Workspace.

	Operation : An -> SP
		    (SP)+ -> An

	Assembler : UNLK An

	Attributes:Unsized

	Description	: The stack pointer is loaded from the specified
			  address register. The address register is then
			  loaded from with the long word pulled from the
			  top of the stack.

	Condition Codes	: NOT AFFECTED.

	Instruction Format :

		0 1 0 0 1 1 1 0 0 1 0 1 1 R R R

	Instruction Fields :

		RRR	: Register field. Specifies the destination
			  address register through which the unlinking
			  is done.


Effective Address Specification
-------------------------------

	The possible values for the EEE and AAA fields for specifying effect-
ive addresses in standard 68000 instructions is defined by the table:


	EEE	AAA	Addressing Mode
	---	---	---------------

	000	nnn	Data Register Dn, nnn = 0-7

	001	nnn	Address register An, nnn = 0-7

	010	nnn	(An), nnn = 0-7 to specify address register

	011	nnn	(An)+, nnn = 0-7 to specify address register

	100	nnn	-(An), nnn = 0-7 to specify address register

	101	nnn	d(An), nnn = 0-7 to specify address register

	110	nnn	d(An,Xi), nnn = 0-7 to specify address register.
			Xi is specified by an extension word to the
			instruction.

	111	000	Absolute word operand

	111	001	Absolute long operand

	111	010	d(PC)

	111	011	d(PC,Xi). Xi is specified by an extension word
			to the instruction.

	111	100	Immediate data.


Addressing Modes
----------------

The various addressing modes available on the 68000 are listed below. EA
refers to Effective Address, Generation refers to the mechanism for obtain-
ing the effective address,EEE Mode is the value of the EEE bits in the in-
struction word, and AAA Mode is the value of the AAA bits in the instruction
word.


1) Data Register Direct.

	Generation	: EA = Dn (n = 0 to 7)
	Assembler	: Dn
	EEE Mode	: 000
	AAA Mode	: nnn (0 to 7)

	The operand is the specified data register.


2) Address Register Direct.

	Generation	: EA = An (n = 0 to 7)
	Assembler	: An
	EEE Mode	: 001
	AAA Mode	: nnn (0 to 7)

	The operand is the specified address register.


3) Address Register Indirect.

	Generation	: EA = (An) (n = 0 to 7)
	Assembler	: (An)
	EEE Mode	: 010
	AAA Mode	: nnn (0 to 7)

	The operand is the memory location whose address is contained
	in the specified address register.


4) Address Register Indirect with Postincrement.

	Generation	: EA = (An) (n = 0 to 7)
			  An = An + N
			  (N = operand size:1=byte, 2=word, 4=long)
	Assembler	: (An)+
	EEE Mode	: 011
	AAA Mode	: nnn (0 to 7)

	The operand is the memory location whose address is contained
	in the specified address register, PRIOR to the addition of
	the operand size to the address register contents.


5) Address Register Indirect with Predecrement.

	Generation	: An = An - N
			  EA = (An) (n = 0 to 7)
			  (N = operand size:1=byte, 2=word, 4=long)
	Assembler	: -(An)
	EEE Mode	: 100
	AAA Mode	: nnn (0 to 7)

	The operand is the memory location whose address is contained
	in the specified address register, AFTER the subtraction of
	the operand size from the address register contents.


6) Address Register Indirect with Displacement.

	Generation	: EA = (An) + d (n = 0 to 7)
	Assembler	: Label(An)
	EEE Mode	: 101
	AAA Mode	: nnn (0 to 7) specifies the address
			  register An.

	The effective address of the operand is obtained by computing
	the sum of the contents of the specified address register with
	the 16-bit displacement using standard 680x0 address arithmetic.
	Thus, the 16-bit displacement is sign-extended to 32 bits prior
	to the computation.


7) Address Register Indirect with Displacement And Index.

	Generation	: EA = (An) + (Xn) + d (n = 0 to 7)
	Assembler	: Label(An,Xn.W)
			  Label(An,Xn.L)
	EEE Mode	: 110
	AAA Mode	: nnn (0 to 7) specifies the address
			  register An. Xn is specified by an
			  extension word.

	The effective address of the operand is obtained by computing
	the sum of the contents of the specified address register with
	the 8-bit displacement and the contents of the specified index
	register using standard 680x0 address arithmetic. Thus, the 8-
	bit displacement is sign-extended to 32 bits prior to the compu-
	tation. The index register may be any data or address register
	(hence Xn may be the same as An in the instruction) and the value
	obtained from the index register may be either a word (which will
	be sign-extended for the addition) or a long.


8) Absolute Short.

	Generation	: EA given
	Assembler	: Label.W
	EEE Mode	: 111
	AAA Mode	: 000

	The effective address is the contents of the word following the
	instruction word. This word is sign-extended to 32 bits prior to
	use as an address reference.


9) Absolute Long.

	Generation	: EA given
	Assembler	: Label.L
	EEE Mode	: 111
	AAA Mode	: 001

	The effective address is the contents of the long word following
	the instruction word.


10) Program Counter Indirect with Displacement.

	Generation	: EA = (PC) + d (n = 0 to 7)
	Assembler	: Label(PC)
	EEE Mode	: 111
	AAA Mode	: 010

	The effective address of the operand is obtained by computing
	the sum of the contents of the program counter with the 16-bit
	displacement using standard 680x0 address arithmetic. Thus, the
	16-bit displacement is sign-extended to 32 bits prior to the
	computation.


11) Program Counter Indirect with Displacement And Index.

	Generation	: EA = (PC) + (Xn) + d (n = 0 to 7)
	Assembler	: Label(PC,Xn.W)
			  Label(PC,Xn.L)
	EEE Mode	: 111
	AAA Mode	: 011
			  Xn is specified by an extension word.

	The effective address of the operand is obtained by computing
	the sum of the contents of the program counter with the 8-bit
	displacement and the contents of the specified index register
	using standard 680x0 address arithmetic. Thus, the 8-bit disp-
	lacement is sign-extended to 32 bits prior to the computation.
	The index register may be any data or address register (hence
	Xn may be the same as An in the instruction) and the value ob-
	tained from the index register may be either a word (which will
	be sign-extended for the addition) or a long.


12) Immediate Data.

	Generation	: Operand given
			  (EA = address of instruction word + 2)
	Assembler	: #nnnn
	EEE Mode	: 111
	AAA Mode	: 100

	The effective address of this operand is the address of the in-
	struction word plus two. For byte and word operands, the word
	at this address contains the immediate data. For long operands,
	the long word at this address contains the immediate data.
	


Extension Words for Complex Addressing Modes
--------------------------------------------

	The following extension words are valid for 68000 addressing modes:

	d(An)	 : Extension Word is 16-bit signed value of d.

	d(An,Xi) : Extension Word D R R R W 0 0 0 I I I I I I I I

	D	: D/A field. Specifies index register type.

		  0 : Xi = Dn

		  1 : Xi = An

	RRR	: Index register number 0-7. Either D0-D7 if D/A=0,
		  or A0-A7 if D/A = 1.

	W	: Index size. Specifies size of index register.

		  0 : Word size. Low word of index register used,
			sign-extended to 32 bits before effective
			address computation.

		  1 : Long size. Entire 32 bits of index register
			used in effective address computation.

	III...	: Displacement. 8 bits of displacement data.


	d(PC)	 : Extension Word is 16-bit signed value of d.

	d(PC,Xi) : Extension Word D R R R W 0 0 0 I I I I I I I I

	D	: D/A field. Specifies index register type.

		  0 : Xi = Dn

		  1 : Xi = An

	RRR	: Index register number 0-7. Either D0-D7 if D/A=0,
		  or A0-A7 if D/A = 1.

	W	: Index size. Specifies size of index register.

		  0 : Word size. Low word of index register used,
			sign-extended to 32 bits before effective
			address computation.

		  1 : Long size. Entire 32 bits of index register
			used in effective address computation.

	III...	: Displacement. 8 bits of displacement data.


Rules For Extension Words
-------------------------

In a complex instruction, such as:


			MOVE.L	#$8000,8(A6,D1.L)


the order of extension words is:


			Source Immediate Data Word(s)

			Source Extension Word(s)

			Destination Extension Word(s)


For the above example, the instruction words will be (in hexadecimal):


			2DBC	(MOVE.L)
			0000	#$8000.L
			8000
			1808	Extension word for 8(A6,D1.L)


For the instruction ADD.W $300(PC),D2, the instruction words will be
(Again in hexadecimal):


			D47A	(ADD.W)
			0300	$300 offset in $300(PC)


And MOVE.B #$0F,$4A000.L will appear in memory as:


			1E7C	(MOVE.B)
			000F	Immediate data
			0004	Absolute long
			A000	address data


This becomes completely revised when 68020 and higher processors are taken
into account, which have the extended Memory Indirect addressing modes, and
which may have as many as ten extension words following the instruction word!


Conditional Branch Table
------------------------

	The list of possible values for conditional expression specifiers
in the CCCC fields of Bcc, DBcc etc., is defined by the table:


	DBcc	CCCC	Condition		Expression
	----	----	---------		----------

	DBT	0000	Always True		1

	DBF	0001	Always False		0

	DBHI	0010	Higher Than		(~C) AND (~Z)

	DBLS	0011	Lower Or Same		C OR Z

	DBCC	0100	Carry Clear		~C

	DBCS	0101	Carry Set		C

	DBNE	0110	Not Equal To Zero	~Z

	DBEQ	0111	Equal To Zero		Z

	DBVC	1000	Overflow Clear		~V

	DBVS	1001	Overflow Set		V

	DBPL	1010	Plus (Positive)		~N

	DBMI	1011	Minus (Negative)	N

	DBGE	1100	Greater Or Equal	(N AND V) OR (~N AND ~V)

	DBLT	1101	Less Than		(N AND ~V) OR (~N AND V)

	DBGT	1110	Greater Than		(N AND V AND Z) OR
						(~N AND ~V AND ~Z)

	DBLE	1111	Less Than Or Equal	Z OR (N AND ~V) OR
						(~N AND V)


In the case of Bcc, the instruction BF does not exist on current assemblers,
and BT is usually written BRA. Similarly, DBF is usually written DBRA (even
though the logic of the operation is somewhat different).